## Slide 1: Efficient Collective Operations using Remote Memory Operations on VIA-Based Clusters
Rinku Gupta
Dell Computers
Rinku_Gupta@Dell.Com
Dhabaleswar Panda
The Ohio State University
panda@cis.ohio-state.edu
Pavan Balaji
The Ohio State University
balaji@cis.ohio-state.edu
Jarek Nieplocha
Pacific Northwest National Lab
jarek.nieplocha@pnl.com
Notes: Check the title

## Slide 2: Contents
Motivation
Design Issues
RDMA-based Broadcast
RDMA-based All Reduce
Conclusions and Future Work

## Slide 3: Motivation
Communication Characteristics of Parallel Applications
  Point-to-Point Communication
    Send and Receive primitives
  Collective Communication
    Barrier, Broadcast, Reduce, All Reduce
    Built over Send-Receive Communication primitives
Communication Methods for Modern Protocols
  Send and Receive Model
  Remote Direct Memory Access (RDMA) Model

## Slide 4: Remote Direct Memory Access
Remote Direct Memory Access (RDMA) Model
  RDMA Write
  RDMA Read (Optional)
Widely supported by modern protocols and architectures
  Virtual Interface Architecture (VIA)
  InfiniBand Architecture (IBA)
Open Questions
  Can RDMA be used to optimize Collective Communication? [rin02]
  Do we need to rethink algorithms optimized for Send-Receive?
[rin02]: “Efficient Barrier using Remote Memory Operations on VIA-based Clusters”, Rinku Gupta, V. Tipparaju, J. Nieplocha, D. K. Panda. Presented at Cluster 2002, Chicago, USA

## Slide 5: Send-Receive and RDMA Communication Models
User buffer
Registered
S
R
Registered
NIC
User buffer
NIC
descriptor
descriptor
User buffer
Registered
S
R
NIC
Registered
User buffer
NIC
descriptor
Send/Recv
RDMA Write
Notes: VIA requires data to be sent and received should be from registered buffers.
Send/Recv. – Sender has to copy the data to registered buffer, register the buffer and post a descriptor and send the data.
The Receiver will ALSO post a descriptor indicating location of data. Receiver is completely involved.
The descriptor will tell location of data in send/recv model.
RDMA
No posting of descriptor and no involment of the destination receiver in the RDMA model. Receiving is transparent. Sender gives the address of destination and correct memory handle.

## Slide 6: Benefits of RDMA
RDMA gives a shared memory illusion
Receive operations are typically expensive
RDMA is Receiver transparent
Supported by VIA and InfiniBand architecture
A novel unexplored method
Notes: Higher level libraries induce lot of overhead.
MPI has to take care of many things like unexpected getting of messages, buffering them , copy them when the actual user buffer is found..so receive is expensive
Rdma –eliminates this receiving overhead
Potential to examine simpler collective algorithms on a distributed cluster
This area of research has not been explored in the past

## Slide 7: Contents
Motivation
Design Issues
    Buffer Registration
    Data Validity at Receiver End
    Buffer Reuse
RDMA-based Broadcast
RDMA-based All Reduce
Conclusions and Future Work

## Slide 8: Buffer Registration
Static Buffer Registration
  Contiguous region in memory for every communicator
  Address exchange is done during initialization time
Dynamic Buffer Registration - Rendezvous
  User buffers, registered during the operation, when needed
  Address exchange is done during the operation

## Slide 9: Data Validity at Receiver End
Interrupts
  Too expensive; might not be supported
Use Immediate field of VIA descriptor
  Consumes a receive descriptor
RDMA write a Special byte to a pre-defined location

## Slide 10: Buffer Reuse
Static Buffer Registration
  Buffers need to be reused
  Explicit notification has to be sent to sender
Dynamic Buffer Registration
  No buffer Reuse

## Slide 11: Contents
Motivation
Design Issues
RDMA-based Broadcast
    Design Issues
    Experimental Results
    Analytical Models
RDMA-based All Reduce
Conclusions and Future Work

## Slide 12: Buffer Registration and Initialization
Static Registration Scheme (for size <= 5K bytes)
P0
P1
P2
P3
Constant
Block size
Notify
Buffer
-1
-1
-1
-1
-1
-1
-1
-1
-1
-1
-1
-1
Dynamic Registration Scheme (for size > 5K) -- Rendezvous scheme
Notes: Contiguous buffer space. Once such buffer space is reserved for every communciator. Genreally have 1000 blocks(mention that in thesis)
Divided into blocks of constant size
You also have notify buffers

## Slide 13: Data Validity at Receiver End
-1
1
-1
-1
1
1
P0
P1
P2
P3
-1
-1
-1
-1
-1
-1
-1
-1
Constant
Block size
Broadcast counter = 1 (First Broadcast with Root P0)
Data size
Broadcast
counter
Notify
Buffer
1

## Slide 14: Buffer Reuse
2
2
1
2
2
1
2
2
1
2
2
1
P0
P1
P2
P3
1
1
Notify
Buffer
1
Broadcast
Buffer
P0
P1
P2
P3

## Slide 15: Performance Test Bed
16 1GHz PIII nodes, 33MHz PCI bus, 512MB RAM.
Machines connected using GigaNet cLAN 5300 switch.
MVICH Version : mvich-1.0
  Integration with MVICH-1.0
  MPI_Send modified to support RDMA Write
Timings were taken for varying block sizes
  Tradeoff between number of blocks and size of blocks

## Slide 16: RDMA Vs Send-Receive Broadcast (16 nodes)
Improvement ranging from 14.4% (large messages) to 19.7% (small messages)
Block size of 3K is performing the best
19.7%
14.4%

## Slide 17
Anal. and Exp. Comparison (16 nodes) Broadcast
Error difference of lesser than 7%

## Slide 18: RDMA Vs Send-Receive for Large Clusters (Analytical Model Estimates: Broadcast)
16%
21%
16%
21%
Estimated Improvement ranging from 16% (small messages) to 21% (large messages) for large clusters of sizes 512 nodes and 1024 nodes

## Slide 19: Contents
Motivation
Design Issues
RDMA-based Broadcast
RDMA-based All Reduce
    Degree-K tree
    Experimental Results (Binomial & Degree-K)
    Analytical Models (Binomial & Degree-K)
Conclusions and Future Work

## Slide 20: Degree-K tree-based Reduce
P1
P2
P3
P4
P5
P6
P7
P0
[ 1 ]
[ 1 ]
[ 1 ]
[ 1 ]
[ 3 ]
[ 2 ]
[ 2 ]
P1
P2
P3
P4
P5
P6
P7
P0
[ 1 ]
[ 1 ]
[ 2 ]
P1
P2
P3
P4
P5
P6
P7
P0
[ 1 ]
K = 1
K = 3
K = 7

## Slide 21: Experimental Evaluation
Integrated into MVICH-1.0
  Reduction Operation = MPI_SUM
  Data type = 1 INT (data size = 4 bytes)
  Count = 1 (4 bytes) to 1024 (4096) bytes
Finding the optimal Degree-K
Experimental Vs Analytical (best case & worst case)
Exp. and Anal. comparison of Send-Receive with RDMA

## Slide 22
4 nodes
8 nodes
16 nodes
Degree-3
Degree-7
Degree-3
Degree-3
Degree-1
Degree-3
Degree-1
Degree-3
Degree-1
4-256B
256-1KB
Beyond 1KB
Choosing the Optimal Degree-K for All Reduce
For lower message sizes, higher degrees perform better than degree-1 (binomial)

## Slide 23: Degree-K RDMA-based All Reduce Analytical Model
Experimental timings fall between the best case and the worst case analytical estimates
For lower message sizes, higher degrees perform better than degree-1 (binomial)
4 nodes
8 nodes
16 nodes
Degree-3
Degree-7
Degree-3
Degree-3
Degree-1
Degree-3
Degree-1
Degree-3
Degree-1
4-256B
256-1KB
Beyond 1KB
Degree-3
Degree-3
Degree-1
Degree-3
Degree-3
Degree-1
1024 nodes
512 nodes

## Slide 24: Binomial Send-Receive Vs Optimal & Binomial Degree-K RDMA (16 nodes) All Reduce
38.13%
9%
Improvement ranging from 9% (large messages) to 38.13% (small messages) for the optimal degree-K RDMA-based All Reduce compared to Binomial Send-Receive

## Slide 25: Binomial Send-Receive Vs Binomial & Optimal Degree-K All Reduce for large clusters
Improvement ranging from 14% (large messages) to 35-40% (small messages) for the optimal degree-K RDMA-based All Reduce compared to Binomial Send-Receive
35-40%
14%
35-41%
14%

## Slide 26: Contents
Motivation
Design Issues
RDMA-based Broadcast
RDMA-based All Reduce
Conclusions and Future Work

## Slide 27: Conclusions
Novel method to implement the collective communication library
Degree-K algorithm to exploit the benefits of RDMA
  Implemented the RDMA-based Broadcast and All Reduce
  Broadcast: 19.7% improvement for small and 14.4% for large messages (16nodes)
  All Reduce: 38.13% for small messages, 9.32% for large messages (16nodes)
Analytical models for Broadcast and All Reduce
  Estimate Performance benefits of large clusters
  Broadcast: 16-21% for 512 and 1024 node clusters
  All Reduce: 14-40% for 512 and 1024 node clusters

## Slide 28: Future Work
Exploit the RDMA Read feature if available
  Round-trip cost design issues
Extend to MPI-2.0
  One sided Communication
Extend framework to emerging InfiniBand architecture

## Slide 29
For more information, please visit the
http://nowlab.cis.ohio-state.edu
Network Based Computing Group,
The Ohio State University
Thank You!
NBC
Home Page
Notes: That’s all about the presentation. I would like to take any questions you might be having.

## Slide 30: Backup Slides

## Slide 31: Receiver Side Best for Large messages (Analytical Model)
P3
P2
P1
Tt
To
Tn
Ts
= ( Tt * k ) + Tn + Ts + To + Tc k - No of Sending nodes
Tt
To
Tn
Ts
Tt
To
Tn
Ts

## Slide 32: Receiver Side Worst for Large messages (Analytical Model)
P3
P2
P1
To
Tt
Tn
Ts
To
To
= ( Tt * k ) + Tn + Ts + ( To * k ) + Tc k - No of Sending nodes
Tt
Tn
Ts
Tt
Tn
Ts

## Slide 33: Buffer Registration and Initialization
Static Registration Scheme (for size <= 5K)
P0
P1
P2
P3
Constant
Block size
(5K+1)
P1
P2
P3
Each block is of size 5K+1. Every process has N blocks, where
N is the number of processes in the communicator
Notes: Contiguous buffer space. Once such buffer space is reserved for every communciator. Genreally have 1000 blocks(mention that in thesis)
Divided into blocks of constant size
You also have notify buffers

## Slide 34: Data Validity at Receiver End
P0
P1
P2
P3
2
5
4
3
1
5
1
3
P0
P1
P2
P3
1
9
1
5
2
5
4
3
Computed
Data
P0
P1
P2
P3
1
9
1
5
2
5
4
3
4
Data 1
Data 2
9
1
P0
P1
P2
P3
1
9
1
5
2
5
4
3
4
14
1
Computed
Data