## Slide 1: Sockets Direct Protocol Over InfiniBand in Clusters: Is it Beneficial?
P. Balaji, S. Narravula, K. Vaidyanathan, S. Krishnamoorthy, J. Wu and D. K. Panda
Network Based Computing Laboratory
The Ohio State University

## Slide 2: Presentation Layout
Introduction and Background
Sockets Direct Protocol (SDP)
Multi-Tier Data-Centers
Parallel Virtual File System (PVFS)
Experimental Evaluation
Conclusions and Future Work

## Slide 3: Introduction
Advent of High Performance Networks
  Ex: InfiniBand, Myrinet, 10-Gigabit Ethernet
  High Performance Protocols: VAPI / IBAL, GM, EMP
  Good to build new applications
  Not so beneficial for existing applications
    Built around Portability: Should run on all platforms
    TCP/IP based Sockets: A popular choice
    Performance of Application depends on the Performance of Sockets
    Several GENERIC optimizations for sockets to provide high performance
      Jacobson Optimization: Integrated Checksum-Copy [Jacob89]
      Header Prediction for Single Stream data transfer
[Jacob89]: “An analysis of TCP Processing Overhead”, D. Clark, V. Jacobson, J. Romkey and H. Salwen. IEEE Communications

## Slide 4: Network Specific Optimizations
Generic Optimizations Insufficient
  Unable to saturate high performance networks
Sockets can utilize some network features
  Interrupt Coalescing (can be considered generic)
  Checksum Offload (TCP stack has to modified)
  Insufficient!
Can we do better?
  High Performance Sockets
  TCP Offload Engines (TOE)

## Slide 5: High Performance Sockets
High Performance Network
Pseudo sockets layer
Application or Library
Hardware
Kernel
User Space
Sockets
OS Agent
Network
Native Protocol
NIC
IP
TCP
Sockets
Application or Library
Hardware
Kernel
User Space
Traditional Berkeley Sockets
High Performance Sockets

## Slide 6: InfiniBand Architecture Overview
Industry Standard
Interconnect for connecting compute and I/O nodes
Provides High Performance
  Low latency of lesser than 5us
  Over 840MBps uni-directional bandwidth
  Provides one-sided communication (RDMA, Remote Atomics)
Becoming increasingly popular

## Slide 7: Sockets Direct Protocol (SDP*)
IBA Specific Protocol for Data-Streaming
Defined to serve two purposes:
  Maintain compatibility for existing applications
  Deliver the high performance of IBA to the applications
Two approaches for data transfer: Copy-based and Z-Copy
Z-Copy specifies Source-Avail and Sink-Avail messages
  Source-Avail allows destination to RDMA Read from source
  Sink-Avail allows source to RDMA Write to the destination
Current implementation limitations:
  Only supports the Copy-based implementation
  Does not support Source-Avail and Sink-Avail
*SDP implementation from the Voltaire Software Stack

## Slide 8: Presentation Layout
Introduction and Background
Sockets Direct Protocol (SDP)
Multi-Tier Data-Centers
Parallel Virtual File System (PVFS)
Experimental Evaluation
Conclusions and Future Work

## Slide 9: Multi-Tier Data-Centers
Client Requests come over the WAN (TCP based + Ethernet Connectivity)
Traditional TCP based requests are forwarded to the inner tiers
Performance is limited due to TCP
  Can we use SDP to improve the data-center performance?
  SDP is not compatible with traditional sockets: Requires TCP termination!
(Courtesy Mellanox Corporation)

## Slide 10: 3-Tier Data-Center Test-bed at OSU
Database Servers
Clients
Application Servers
Web Servers
Proxy Nodes
Tier 0
Tier 1
Tier 2
Generate requests for both web servers and database servers
TCP Termination Load Balancing Caching
Caching
Dynamic Content Caching Persistent Connections
File System evaluation Caching Schemes
Apache
MySQL
or
DB2
PHP
Apache
WAN

## Slide 11: Presentation Layout
Introduction and Background
Sockets Direct Protocol (SDP)
Multi-Tier Data-Centers
Parallel Virtual File System (PVFS)
Experimental Evaluation
Conclusions and Future Work

## Slide 12: Parallel Virtual File System (PVFS)
Network
Compute
Node
Compute
Node
Compute
Node
Compute
Node
Meta-Data
Manager
I/O Server
Node
I/O Server
Node
I/O Server
Node
Meta
Data
Data
Data
Data
Relies on Striping of data across different nodes
Tries to aggregate I/O bandwidth from multiple nodes
Utilizes the local file system on the I/O Server nodes

## Slide 13: Parallel I/O in Clusters via PVFS
PVFS: Parallel Virtual File System
  Parallel: stripe/access data across multiple nodes
  Virtual: exists only as a set of user-space daemons
  File system: common file access methods (open, read/write)
Designed by ANL and Clemson
iod
Local file systems
iod
Local file systems
mgr
…
Network
Posix
MPI-IO
libpvfs
Applications
Posix
MPI-IO
libpvfs
Applications
…
Control
Data
“PVFS over InfiniBand: Design and Performance Evaluation”, Jiesheng Wu, Pete Wyckoff and D. K. Panda. International Conference on Parallel Processing (ICPP), 2003.

## Slide 14: Presentation Layout
Introduction and Background
Sockets Direct Protocol (SDP)
Multi-Tier Data-Centers
Parallel Virtual File System (PVFS)
Experimental Evaluation
  Micro-Benchmark Evaluation
  Data-Center Performance
  PVFS Performance
Conclusions and Future Work

## Slide 15: Experimental Test-bed
Eight Dual 2.4GHz Xeon processor nodes
64-bit 133MHz PCI-X interfaces
512KB L2-Cache and 400MHz Front Side Bus
Mellanox InfiniHost MT23108 Dual Port 4x HCAs
MT43132 eight 4x port Switch
SDK version 0.2.0
Firmware version 1.17

## Slide 16: Latency and Bandwidth Comparison
SDP achieves 500MBps bandwidth compared to 180MBps of IPoIB
Latency of 27us compared to 31us of IPoIB
Improved CPU Utilization

## Slide 17: Hotspot Latency
SDP is more scalable in hot-spot scenarios

## Slide 18: Data-Center Response Time
SDP shows very little improvement: Client network (Fast Ethernet) becomes the bottleneck
Client network bottleneck reflected in the web server delay: up to 3 times improvement with SDP

## Slide 19: Data-Center Response Time (Fast Clients)
SDP performs well for large files; not very well for small files

## Slide 20: Data-Center Response Time Split-up
IPoIB
SDP

## Slide 21: Data-Center Response Time without Connection Time Overhead
Without the connection time, SDP would perform well for all file sizes

## Slide 22: PVFS Performance using ramfs

## Slide 23: PVFS Performance with sync (ext3fs)
Clients can push data faster to IODs using SDP; de-stage bandwidth remains the same

## Slide 24: Conclusions
User-Level Sockets designed with two motives:
  Compatibility for existing applications
  High Performance for modern networks
SDP was proposed recently along similar lines
Sockets Direct Protocol: Is it Beneficial?
  Evaluated it using micro-benchmarks and real applications
    Multi-Tier Data-Centers and PVFS
  Benefits in environments it’s good for
    Communication intensive environments such as PVFS
  Demonstrate environments it’s yet to mature for
    Connection overhead involving environments such as Data-Centers

## Slide 25: Future Work
Connection Time bottleneck in SDP
  Using dynamic registered buffer pools, FMR techniques, etc
  Using QP pools
Power-Law Networks
Other applications: Streaming and Transaction
Comparison with other high performance sockets

## Slide 26
For more information, please visit the
http://nowlab.cis.ohio-state.edu
Network Based Computing Laboratory,
The Ohio State University
Thank You!
NBC
Home Page
Notes: That’s all about the presentation. I would like to take any questions you might be having.

## Slide 27: Backup Slides

## Slide 28: TCP Termination in SDP
OS by pass
Ethernet
IP
TCP
Proxy
SDP
Infiniband HW
Ethernet
IP
TCP
Sockets
Browser
Sockets
SDP
Infiniband HW
Web Server
HTTP
HTTP
HTML
HTML
Personal Notebook/Computer
Blade Servers
Network Service Tier
Ethernet Communication
InfiniBand Communication