## Slide 1: Sockets vs. RDMA Interface over 10-Gigabit Networks: An In-depth Analysis of the Memory Traffic Bottleneck
Pavan Balaji Hemal V. Shah¥ D. K. Panda
Network Based Computing Lab
Computer Science and Engineering
Ohio State University
¥Embedded IA Division
Intel Corporation
Austin, Texas

## Slide 2: Introduction and Motivation
Advent of High Performance Networks
  Ex: InfiniBand, 10-Gigabit Ethernet, Myrinet, etc.
  High Performance Protocols: VAPI / IBAL, GM
  Good to build new applications
  Not so beneficial for existing applications
    Built around portability: Should run on all platforms
    TCP/IP based sockets: A popular choice
    Several GENERIC optimizations proposed and implemented for TCP/IP
      Jacobson Optimization: Integrated Checksum-Copy [Jacob89]
      Header Prediction for Single Stream data transfer
[Jacob89]: “An analysis of TCP Processing Overhead”, D. Clark, V. Jacobson, J. Romkey and H. Salwen. IEEE Communications

## Slide 3: Generic Optimizations Insufficient!
10GigE
1GigE
Processor Speed DOES NOT scale with Network Speeds
Protocol processing too expensive for current day systems
http://www.intel.com/research/silicon/mooreslaw.htm

## Slide 4: Network Specific Optimizations
Sockets can utilize some network features
  Hardware support for protocol processing
  Interrupt Coalescing (can be considered generic)
  Checksum Offload (TCP stack has to modified)
  Insufficient!
Network Specific Optimizations
  High Performance Sockets [shah99, balaji02]
  TCP Offload Engines (TOE)
[shah99]: “High Performance Sockets and RPC over Virtual Interface (VI) Architecture”, H. Shah, C. Pu, R. S. Madukkarumukumana, In CANPC ‘99
[balaji02]: “Impact of High Performance Sockets on Data Intensive Applications”, P. Balaji, J. Wu, T. Kurc, U. Catalyurek, D. K. Panda, J. Saltz, In HPDC ‘03

## Slide 5: Memory Traffic Bottleneck
Offloaded Transport Layers provide some performance gains
  Protocol processing is offloaded; lesser host CPU overhead
  Better network performance for slower hosts
  Quite effective for 1-2 Gigabit networks
  Effective for faster (10-Gigabit) networks in some scenarios
Memory Traffic Constraints
  Offloaded Transport Layers rely on the sockets interface
  Sockets API forces memory access operations in several scenarios
    Transactional protocols such as RPC, File I/O, etc.
  For 10-Gigabit networks memory access operations can limit network performance !

## Slide 6: 10-Gigabit Networks
10-Gigabit Ethernet
  Recently released as a successor in the Ethernet family
  Some adapters support TCP/IP checksum and Segmentation offload
InfiniBand
  Open Industry Standard
  Interconnect for connecting compute and I/O nodes
  Provides High Performance
    Offloaded Transport Layer; Zero-Copy data-transfer
    Provides one-sided communication (RDMA, Remote Atomics)
  Becoming increasingly popular
  An example RDMA capable 10-Gigabit network

## Slide 7: Objective
New standards proposed for RDMA over IP
  Utilizes an offloaded TCP/IP stack on the network adapter
  Supports additional logic for zero-copy data transfer to the application
  Compatible with existing Layer 3 and 4 switches
What’s the impact of an RDMA interface over TCP/IP?
  Implications on CPU Utilization
  Implications on Memory Traffic
  Is it beneficial?
We analyze these issues using InfiniBand’s RDMA capabilities!

## Slide 8: Presentation Outline
Introduction and Motivation
TCP/IP Control Path and Memory Traffic
10-Gigabit network performance for TCP/IP
10-Gigabit network performance for RDMA
Memory Traffic Analysis for 10-Gigabit networks
Conclusions and Future Work

## Slide 9: TCP/IP Control Path (Sender Side)
Application
Buffer
Socket Buffer
NIC
Driver
write()
Checksum and Copy
Post TX
Kick Driver
Return to Application
Post Descriptor
INTR on transmit success
DMA
Checksum, Copy and DMA are the data touching portions in TCP/IP
Offloaded protocol stacks avoid checksum at the host; copy and DMA are still present
Packet Leaves

## Slide 10: TCP/IP Control Path (Receiver Side)
Application
Buffer
Socket Buffer
NIC
Driver
Wait for read()
read()
Application gets data
Copy
DMA
Packet Arrives
INTR on Arrival
Data might need to be buffered on the receiver side
Pick-and-Post techniques force a memory copy on the receiver side

## Slide 11: Memory Bus Traffic for TCP
North Bridge
Application and Socket buffers fetched to L2 $
Application Buffer written back to memory
CPU
NIC
FSB
Memory Bus
I/O Bus
Each network byte requires 4 bytes to be transferred on the Memory Bus (unidirectional traffic)
Assuming 70% memory efficiency, TCP can support at most 4-5Gbps bidirectional on 10Gbps (400MHz/64bit FSB)
Appln.
Buffer
Socket
Buffer
L2 $
Memory
Appln.
Buffer
Socket
Buffer
Data DMA
Data Copy

## Slide 12: Network to Memory Traffic Ratio
 | Application Buffer Fits in Cache | Application Buffer Doesn’t fit in Cache
Transmit (Worst Case) | 1-4 | 2-4
Transmit (Best Case) | 1 | 2-4
Receive (Worst Case) | 2-4 | 4
Receive (Best Case) | 2 | 4
This table shows the minimum memory traffic associated with network data
In reality socket buffer cache misses, control messages and noise traffic may cause these to be higher
Details of other cases present in the paper

## Slide 13: Presentation Outline
Introduction and Motivation
TCP/IP Control Path and Memory Traffic
10-Gigabit network performance for TCP/IP
10-Gigabit network performance for RDMA
Memory Traffic Analysis for 10-Gigabit networks
Conclusions and Future Work

## Slide 14: Experimental Test-bed (10-Gig Ethernet)
Two Dell2600 Xeon 2.4GHz 2-way SMP node
1GB main memory (333MHz, DDR)
Intel E7501 Chipset
32K L1, 512K L2, 400MHz/64bit FSB
PCI-X 133MHz/64bit I/O bus
Intel 10GbE/Pro 10-Gigabit Ethernet adapters
8 P4 2.0 GHz nodes (IBM xSeries 305; 8673-12X)
Intel Pro/1000 MT Server Gig-E adapters
256K main memory

## Slide 15: 10-Gigabit Ethernet: Latency and Bandwidth
TCP/IP achieves a latency of 37us (Win Server 2003) – 20us on Linux
  About 50% CPU utilization on both platforms
Peak Throughput of about 2500Mbps; 80-100% CPU Utilization
Application buffer is always in Cache !!

## Slide 16: TCP Stack Pareto Analysis (64 byte)
Sender
Receiver
Kernel, Kernel Libraries and TCP/IP contribute to the Offloadable TCP/IP stack

## Slide 17: TCP Stack Pareto Analysis (16K byte)
Sender
Receiver
TCP and other protocol overhead takes up most of the CPU
Offload is beneficial when buffers fit into cache

## Slide 18: TCP Stack Pareto Analysis (16K byte)
Sender
Receiver
TCP and other protocol overhead takes up most of the CPU
Offload is beneficial when buffers fit into cache

## Slide 19: Throughput (Fan-in/Fan-out)
SB = 128K; MTU=9K
Peak throughput of 3500Mbps for Fan-In and 4200Mbps for Fan-out

## Slide 20: Bi-Directional Throughput
Not the traditional Bi-directional Bandwidth test
Fan-in with half the nodes and Fan-out with the other half

## Slide 21: Presentation Outline
Introduction and Motivation
TCP/IP Control Path and Memory Traffic
10-Gigabit network performance for TCP/IP
10-Gigabit network performance for RDMA
Memory Traffic Analysis for 10-Gigabit networks
Conclusions and Future Work

## Slide 22: Experimental Test-bed (InfiniBand)
8 SuperMicro SUPER P4DL6 nodes
  Xeon 2.4GHz 2-way SMP nodes
  512MB main memory (DDR)
  PCI-X 133MHZ/64bit I/O bus
Mellanox InfiniHost MT23108 DualPort 4x HCA
  InfiniHost SDK version 0.2.0
  HCA firmware version 1.17
Mellanox InfiniScale MT43132 8-port switch (4x)
Linux kernel version 2.4.7-10smp

## Slide 23: InfiniBand RDMA: Latency and Bandwidth
Performance improvement due to hardware support and zero-copy data transfer
Near zero CPU Utilization at the data sink for large messages
Performance limited by PCI-X I/O bus

## Slide 24: Presentation Outline
Introduction and Motivation
TCP/IP Control Path and Memory Traffic
10-Gigabit network performance for TCP/IP
10-Gigabit network performance for RDMA
Memory Traffic Analysis for 10-Gigabit networks
Conclusions and Future Work

## Slide 25: Throughput test: Memory Traffic
Sockets can force up to 4 times more memory traffic compared to the network traffic
RDMA allows has a ratio of 1 !!

## Slide 26: Multi-Stream Tests: Memory Traffic
Memory Traffic is significantly higher than the network traffic
Comes to within 5% of the practically attainable peak memory bandwidth

## Slide 27: Presentation Outline
Introduction and Motivation
TCP/IP Control Path and Memory Traffic
10-Gigabit network performance for TCP/IP
10-Gigabit network performance for RDMA
Memory Traffic Analysis for 10-Gigabit networks
Conclusions and Future Work

## Slide 28: Conclusions
TCP/IP performance on High Performance Networks
  High Performance Sockets
  TCP Offload Engines
10-Gigabit Networks
  A new dimension of complexity – Memory Traffic
Sockets API can require significant memory traffic
  Up to 4 times more than the network traffic
  Allows saturation on less than 35% of the network bandwidth
  Shows potential benefits of providing RDMA over IP
  Significant benefits in performance, CPU and memory traffic

## Slide 29: Future Work
Memory Traffic Analysis for 64-bit systems
Potential of the L3-Cache available in some systems
Evaluation of various applications
  Transactional (SpecWeb)
  Streaming (Multimedia Services)

## Slide 30
For more information, please visit the
http://nowlab.cis.ohio-state.edu
Network Based Computing Laboratory,
The Ohio State University
Thank You!
NBC
Home Page
Notes: That’s all about the presentation. I would like to take any questions you might be having.

## Slide 31: Backup Slides