## Slide 1: Exploiting Remote Memory Operations to Design Efficient Reconfiguration for Shared Data-Centers over InfiniBand
P. Balaji, K. Vaidyanathan, S. Narravula, K. Savitha, H. –W. Jin
D. K. Panda
Network Based Computing Laboratory
The Ohio State University

## Slide 2: COTS Clusters
Advent of High Performance Networks
  Ex: InfiniBand, Myrinet, Quadrics, 10-Gigabit Ethernet
  High Performance Protocols: VAPI / IBAL, GM, EMP
  Provide applications direct and protected access to the network
Commodity-Off-the-Shelf (COTS) Clusters
  Enabled through High Performance Networks
  Built of commodity components
  High Performance-to-Cost Ratio

## Slide 3: InfiniBand Architecture Overview
Industry Standard
Interconnect for connecting compute and I/O nodes
Provides High Performance
  Low latency of lesser than 4us
  Over 935MBps uni-directional bandwidth
  Offloaded Transport Layer; Zero-Copy data-transfer
  Provides one-sided communication (RDMA, Remote Atomics)
Becoming increasingly popular

## Slide 4: Cluster-based Data-Centers
Increasing adoption of Internet
  Primary means of electronic interaction
  Highly Scalable and Available Web-Servers: Critical !
Utilizing Clusters for Data-Center environments?
  Studied and Proposed by the Industry and Research communities
(Courtesy CSP Architecture Design)
Nodes are logically partitioned
  Interact depending on the query
  Provide services requested
  Services provided are related
  Fragmentation of resources

## Slide 5: Shared Multi-Tier Data-Centers
WAN
Clients
Clients
Load Balancing Cluster (Site A)
Load Balancing Cluster (Site B)
Load Balancing Cluster (Site C)
Website A
Website B
Website C
Servers
Servers
Servers
Hosting several unrelated services on a single clustered data-center

## Slide 6: Issues in Shared Data-Centers
Hosting several unrelated services on a single data-center
  Ex: A single data-center hosting multiple websites
  Currently used by several ISPs and Web Service Providers (IBM, HP)
  Allows differentiation in resources provided for each service
  Fragmentation is a big concern!
Over-provisioning of nodes for each service
  Nodes provided to each service based on the worst-case estimates
  Widely used approach
  Leads to severe under-utilization of resources

## Slide 7: Dynamic Reconfigurability
WAN
Clients
Clients
Load Balancing Cluster (Site A)
Load Balancing Cluster (Site B)
Load Balancing Cluster (Site C)
Website A
Website B
Website C
Servers
Servers
Servers
Nodes reconfigure themselves to highly loaded websites at run-time

## Slide 8: Objective
Under Utilization of resources needs to be curbed
Dynamically Configuring nodes allotted to each service
  Widely studied approach for Clusters
  Interesting Challenges in the Data-Center Environment
    Highly loaded back-end servers
    Compatibility with existing applications (Apache, MySQL, etc)
Can the advanced features provided by InfiniBand help?

## Slide 9: Presentation Roadmap
Introduction
and
Background
Shared Data-Centers
Designing Dynamic Reconfigurability for Shared Data-Centers
Experimental Results
Concluding Remarks
Continuing and
Future Work

## Slide 10: Shared Data-Centers Overview
Clients request services using high level protocols such as HTTP
Requests are distributed to the nodes using load-balancers
  Load Balancers expose a single IP address to the clients
  Maintain a list of several internal IP addresses to forward the requests
Several solutions for load-balancers
  Hardware Load-Balancers
  Software Load-Balancers
  Cluster-based load-balancers

## Slide 11: Cluster-based Load Balancers
Hardware Load-Balancers
  Commonly used in several environments
  In-flexible and cannot be tuned to the data-center requirements
Software Load-Balancers
  Easy to modify and tune to the data-center requirements
  Potential bottlenecks for highly loaded data-center environments
Cluster-based load-balancers
  Proposed by several researchers as an additional Edge Tier [shah01]
  Provides intelligent services such as load-balancing, caching, etc
  Use an additional hardware load-balancer or DNS aliasing to get requests
[shah01]: CSP: A Novel System Architecture for Scalable Internet and Communication Services. H. V. Shah, D. B. Minturn, A. Foong, G. L. McAlpine, R. S. Madukkarumukumana and G. J. Regnier. In USITS 2001.

## Slide 12: Presentation Roadmap
Introduction
and
Background
Shared Data-Centers
Designing Dynamic Reconfigurability for Shared Data-Centers
Experimental Results
Concluding Remarks
Continuing and
Future Work

## Slide 13: Design Issues
Support for Existing Applications
  Modifying existing applications: Cumbersome and Impractical
  Utilizing External Helper Modules (external programs running on each node)
    Take care of load monitoring, reconfiguration, etc.
    Reflect changes to the data-center applications using environment settings
Load-Balancer based vs. Server based Reconfiguration
  Trading network traffic for CPU overhead
  Load Balancers “convert” nodes to serve their website
Remote Memory Operations based Design
  Server node applications are typically very compute intensive
  Execution of CGI scripts, business logic, database processing
  Utilizing one-sided operations provided by InfiniBand
  Load-balancers remotely monitor and reconfigure the system

## Slide 14: Implementation Details
History Aware Reconfiguration
  Avoiding Server Thrashing by maintaining a history of the load pattern
Reconfigurability Module Sensitivity
  Time Interval between two consecutive checks
Maintaining a System Wide Shared State
Shared State with Concurrency Control
Tackling Load-Balancing Delays

## Slide 15: System Wide Shared State
Nodes in the cluster need to share control information
  Load, Current State of the node, etc.
Sockets based Implementation has several disadvantages
  All communication needs to be explicitly performed
  Asynchronous requests need to be handled by the host
    A major concern due to the high CPU overhead on the servers
InfiniBand RDMA operations try to avoid these disadvantages
  Load-balancers can share data on the servers using RDMA Read
  Can update system state using RDMA Write and Atomic Operations

## Slide 16: Shared State with Concurrency Control
Load-balancers query the system load at regular intervals
On detecting a high load, a reconfiguration is done
Multiple Concurrency issues to be dealt with:
  Multiple simultaneous transitions possible
    Each node in the load-balancer cluster can attempt a reconfiguration
    Multiple nodes might end up being converted on a single burst
  Hot Spot Effects on remote nodes
    All load-balancers might try to get load information from the same node
    They might try to convert the same node
  Additional Logic Required !

## Slide 17: Locking Mechanism
We propose a two-level hierarchical locking mechanism
  Internal Lock for each web-site cluster
    Only one load-balancer in a cluster can attempt a reconfiguration
  External Lock for performing reconfiguration
    Only one web-site can convert any given node
  Both locks performed remotely using InfiniBand Atomic Operations
Server
Load Balancer
Internal Lock
Internal Lock
External Lock
Website A
Website B
Website C

## Slide 18: Tackling Load-Balancing Delays
Load-Balancing Delays
  After a reconfiguration, balancing of load might take some time
  Locking mechanisms only ensure no simultaneous transitions
  We need to ensure that all load-balancers are aware of reconfigurations
Server
Website A
Load
Balancer
Server
Website B
Not Loaded
Loaded
Load Query
Load Query
Successful Atomic (Lock)
Successful Atomic (SUC)
Reconfigure Node
Successful Atomic (Unlock)
Load Shared
Load Shared
Dual Counters
  Shared Update Counter (SUC)
  Local Update Counter (LUC)
On reconfiguration:
  LUC should be equal to SUC
  All remote SUCs are incremented

## Slide 19: Presentation Roadmap
Introduction
and
Background
Shared Data-Centers
Designing Dynamic Reconfigurability for Shared Data-Centers
Experimental Results
Concluding Remarks
Continuing and
Future Work

## Slide 20: Experimental Test-bed
Cluster 1 with:
  8 SuperMicro SUPER X5DL8-GG nodes; Dual Intel Xeon 3.0 GHz processors
  512 KB L2 cache, 1 GB memory; PCI-X 64-bit 133 MHz
Cluster 2 with:
  8 SuperMicro SUPER P4DL6 nodes; Dual Intel Xeon 2.4 GHz processors
  512 KB L2 cache, 512 MB memory; PCI-X 64-bit 133 MHz
Mellanox MT23108 Dual Port 4x HCAs; MT43132 24-port switch
Apache 2.0.50 Web and PHP servers; MySQL Database server
Experimental Results (Outline)
  Basic IBA Performance
  Impact of Background Computation Threads
  Impact of Request Burst Length
  Node Utilizations

## Slide 21: Basic IBA Performance
RDMA Read operation on IBA outperforms TCP/IP (IPoIB)
  IBA achieves about 12us latency compared to the 56us of IPoIB
  IBA achieves about 830 MBps bandwidth compared to the 230 MBps of IPoIB
More importantly near zero CPU requirements on the receiver side

## Slide 22: Impact of Background Threads
Remote memory operations are not affected AT ALL with remote server load
Ideal for the data-center environment

## Slide 23: Impact of Burst Length
#Co-hosted Web-Sites = 3
#Co-hosted Web-Sites = 4
Rigid has 3 nodes for each website; Over-provisioning has 6 nodes for each website
Large Burst Length allows reconfiguration of the system closer to the best case!
Performs comparably with the static scheme for small burst sizes

## Slide 24: Node Utilization for 3 Co-hosted Web sites
For Burst Length = 512
For Burst Length = 8096
For large burst lengths, the reconfiguration time is negligible; performance is better

## Slide 25: Presentation Roadmap
Introduction
and
Background
Shared Data-Centers
Designing Dynamic Reconfigurability for Shared Data-Centers
Experimental Results
Concluding Remarks
Continuing and
Future Work

## Slide 26: Concluding Remarks
Growing Fragmentation of resources in data-centers
  Related services provided by Multi-Tier Data-Centers
  Unrelated services provided by Shared Data-Centers
Dynamically configuring resources allotted
  A common approach used in clusters
  Data-Center environment has its own challenges
    Highly loaded back-end servers
    Compatibility with existing applications
Provided a novel approach utilizing the RDMA features of IBA
  A scheme resilient to the load on the back-end servers
  Demonstrated up to 2.5 times improvement in the throughput
  Similar performance using only half the nodes

## Slide 27: Presentation Roadmap
Introduction
and
Background
Shared Data-Centers
Designing Dynamic Reconfigurability for Shared Data-Centers
Experimental Results
Concluding Remarks
Continuing and
Future Work

## Slide 28: Continuing and Future Work
Multi-Stage Reconfigurations
  Least loaded servers might not be the best server to reconfigure
  Caching constraints
  Replicated Databases
  Hardware heterogeneity
Utilizing Dynamic Reconfigurability for advanced services
  QoS guarantees
  Differentiation in the resources provided

## Slide 29
For more information, please visit the
http://nowlab.cis.ohio-state.edu
Network Based Computing Laboratory,
The Ohio State University
Thank You!
NBC
Home Page
Notes: That’s all about the presentation. I would like to take any questions you might be having.

## Slide 30: Backup Slides