## Slide 1: Performance Characterization of a 10-Gigabit Ethernet TOE
W. Feng¥ P. Balajiα C. Baron£
L. N. Bhuyan£ D. K. Pandaα
¥Advanced Computing Lab,
Los Alamos National Lab
αNetwork Based Computing Lab,
Ohio State University
£CARES Group,
U. C. Riverside

## Slide 2: Ethernet Overview
Ethernet is the most widely used network infrastructure today
Traditionally Ethernet has been notorious for performance issues
  Near an order-of-magnitude performance gap compared to IBA, Myrinet, etc.
    Cost conscious architecture
    Most Ethernet adapters were regular (layer 2) adapters
    Relied on host-based TCP/IP for network and transport layer support
    Compatibility with existing infrastructure (switch buffering, MTU)
  Used by 42.4% of the Top500 supercomputers
  Key: Reasonable performance at low cost
    TCP/IP over Gigabit Ethernet (GigE) can nearly saturate the link for current systems
    Several local stores give out GigE cards free of cost ! 
10-Gigabit Ethernet (10GigE) recently introduced
  10-fold (theoretical) increase in performance while retaining existing features

## Slide 3: 10GigE: Technology Trends
Broken into three levels of technologies
  Regular 10GigE adapters
    Layer-2 adapters
    Rely on host-based TCP/IP to provide network/transport functionality
    Could achieve a high performance with optimizations
  TCP Offload Engines (TOEs)
    Layer-4 adapters
    Have the entire TCP/IP stack offloaded on to hardware
    Sockets layer retained in the host space
  RDDP-aware adapters
    Layer-4 adapters
    Entire TCP/IP stack offloaded on to hardware
    Support more features than TCP Offload Engines
      No sockets ! Richer RDDP interface !
      E.g., Out-of-order placement of data, RDMA semantics
[feng03:hoti, feng03:sc]
[Evaluation based on the Chelsio T110 TOE adapters]

## Slide 4: Presentation Overview
Introduction and Motivation
TCP Offload Engines Overview
Experimental Evaluation
Conclusions and Future Work

## Slide 5: What is a TCP Offload Engine (TOE)?
Sockets Interface
Application or Library
Hardware
User
Kernel
TCP
IP
Device Driver
Network Adapter
(e.g., 10GigE)
Sockets Interface
Application or Library
Hardware
User
Kernel
TCP
IP
Device Driver
Network Adapter (e.g., 10GigE)
Offloaded TCP
Offloaded IP
Traditional TCP/IP stack
TOE stack

## Slide 6: Interfacing with the TOE
Sockets Layer
Application or Library
Traditional
Sockets Interface
High Performance Sockets
User-level Protocol
TCP/IP
Device Driver
High Performance Network Adapter
Network Features
(e.g., Offloaded Protocol)
TOM
Application or Library
toedev
TCP/IP
Device Driver
High Performance Network Adapter
Network Features
(e.g., Offloaded Protocol)
High Performance Sockets
TCP Stack Override
No changes required to the core kernel
Some of the sockets functionality duplicated
Kernel needs to be patched
Some of the TCP functionality duplicated
No duplication in the sockets functionality
ControlPath
Data Path

## Slide 7: What does the TOE (NOT) provide?
Compatibility: Network-level compatibility with existing TCP/IP/Ethernet; Application-level compatibility with the sockets interface
Performance: Application performance no longer restricted by the performance of traditional host-based TCP/IP stack
Feature-rich interface: Application interface restricted to the sockets interface !
Hardware
Kernel or Hardware
User
Application or Library
Traditional
Sockets Interface
Transport Layer (TCP)
Network Layer (IP)
Device Driver
Network Adapter (e.g., 10GigE)
Kernel
[rait05]: Support iWARP compatibility and features for regular network adapters. P. Balaji, H. –W. Jin, K. Vaidyanathan and D. K. Panda. In the RAIT workshop; held in conjunction with Cluster Computing, Aug 26th, 2005.
[rait05]

## Slide 8: Presentation Overview
Introduction and Motivation
TCP Offload Engines Overview
Experimental Evaluation
Conclusions and Future Work

## Slide 9: Experimental Test-bed and the Experiments
Two test-beds used for the evaluation
  Two 2.2GHz Opteron machines with 1GB of 400MHz DDR SDRAM
    Nodes connected back-to-back
  Four 2.0GHz quad-Opteron machines with 4GB of 333MHz DDR SDRAM
    Nodes connected with a Fujitsu XG1200 switch (450ns flow-through latency)
Evaluations in three categories
  Sockets-level evaluation
    Single-connection Micro-benchmarks
    Multi-connection Micro-benchmarks
  MPI-level Micro-benchmark evaluation
  Application-level evaluation with the Apache Web-server

## Slide 10: Latency and Bandwidth Evaluation (MTU 9000)
TOE achieves a latency of about 8.6us and a bandwidth of 7.6Gbps at the sockets layer
Host-based TCP/IP achieves a latency of about 10.5us (25% higher) and a bandwidth of 7.2Gbps (5% lower)
For Jumbo frames, host-based TCP/IP performs quite close to the TOE
9000)

## Slide 11: Latency and Bandwidth Evaluation (MTU 1500)
No difference in latency for either stack
The bandwidth of host-based TCP/IP drops to 4.9Gbps (more interrupts; higher overhead)
For standard sized frames, TOE significantly outperforms host-based TCP/IP (segmentation offload is the key)

## Slide 12: Multi-Stream Bandwidth
The throughput of the TOE stays between 7.2 and 7.6Gbps

## Slide 13: Hot Spot Latency Test (1 byte)
Connection scalability tested up to 12 connections; TOE achieves similar or better scalability as the host-based TCP/IP stack

## Slide 14: Fan-in and Fan-out Throughput Tests
Fan-in and Fan-out tests show similar scalability

## Slide 15: MPI-level Comparison
MPI latency and bandwidth show similar trends as socket-level latency and bandwidth

## Slide 16: Application-level Evaluation: Apache Web-Server
Apache Web-server
Web Client
Web Client
Web Client
We perform two kinds of evaluations with the Apache web-server:
  Single file traces
    All clients always request the same file of a given size
    Not diluted by other system and workload parameters
  Zipf-based traces
    The probability of requesting the Ith most popular document is inversely proportional to Iα
    α is constant for a given trace; it represents the temporal locality of a trace
    A high α value represents a high percent of requests for small files

## Slide 17: Apache Web-server Evaluation

## Slide 18: Presentation Overview
Introduction and Motivation
TCP Offload Engines Overview
Experimental Evaluation
Conclusions and Future Work

## Slide 19: Conclusions
For a wide-spread acceptance of 10-GigE in clusters
  Compatibility
  Performance
  Feature-rich interface
Network as well as Application-level compatibility is available
  On-the-wire protocol is still TCP/IP/Ethernet
  Application interface is still the sockets interface
Performance Capabilities
  Significant performance improvements compared to the host-stack
    Close to 65% improvement in bandwidth for standard sized (1500byte) frames
Feature-rich interface: Not quite there yet !
  Extended Sockets Interface
  iWARP offload

## Slide 20: Continuing and Future Work
Comparing 10GigE TOEs to other interconnects
  Sockets Interface [cluster05]
  MPI Interface
  File and I/O sub-systems
Extending the sockets interface to support iWARP capabilities [rait05]
Extending the TOE stack to allow protocol offload for UDP sockets

## Slide 21: Web Pointers
http://public.lanl.gov/radiant
http://nowlab.cse.ohio-state.edu
feng@lanl.gov
balaji@cse.ohio-state.edu
Network Based Computing
Laboratory
NOWLAB