## Slide 1: Performance Evaluation of RDMA over IP: A Case Study with the Ammasso Gigabit Ethernet NIC
H.-W. Jin, S. Narravula, G. Brown,
K. Vaidyanathan, P. Balaji, and D.K. Panda
Network-Based Computing Laboratory
Department of Computer Science and Engineering
The Ohio State University
{ jinhy, narravul, browngre, vaidyana, balaji, panda}@cse.ohio-state.edu

## Slide 2: Contents
Introduction
WAN Emulator for Cluster-of-Clusters
Performance Evaluation of RDMA over IP
Conclusions and Future Work

## Slide 3: Introduction
Sockets over TCP/IP
RDMA over LAN
  InfiniBand, Myrinet, Quadrics
  HPC middleware (MPI) and file systems (PVFS)
RDMA over WAN
  iWARP, RDDP
  Grid and Internet applications
RDMA-enabled Gigabit Ethernet NIC
  Ammasso

## Slide 4: Ammasso Gigabit Ethernet NIC
Applications
Sockets Interface
CCIL
(Cluster Core Interface Lang.)
Sockets
TCP
IP
Device Driver
Gigabit Ethernet
RDMA
TOE
(TCP/IP Offload Engine)
Ammasso Gigabit Ethernet NIC
Operating System

## Slide 5: Problem Statement
There have been no comprehensive quantitative evaluations of RDMA over WAN environment
How to Emulate the WAN Environment?
What Kind of Performance Metrics?
Sockets vs. CCIL

## Slide 6: Contents
Introduction
WAN Emulator for Cluster-of-Clusters
Performance Evaluation of RDMA over IP
Conclusions and Future Work

## Slide 7: Experimental WAN Setup
GigE
Switch
GigE
Switch
IP
eth0
eth1
Device Driver
Linux Workstation-based
Router
IP Network A
IP Network B
WAN
Emulation

## Slide 8: WAN Emulator for Cluster-of-Clusters
Characteristics of WAN Environments
  High network delay
  Packet loss
  Etc.
User-Level or Kernel-Level Emulator?
Blocking or Queueing based Delay Adding?

## Slide 9: Degen: Delay generator
eth0
eth1
Device Driver
Device Driver
Routing Decision
Degen Netfilter
Timestamp
delay queue
reinjection
IP
Degen
Kernel Module
Dgen Daemon
WAN Emulator for
Cluster-of-Clusters

## Slide 10: Kernel Patch for CCIL WAN Communication
Ammasso Setup
  Ammasso 1100
  Ammasso software version amso1100-1.2-ga2
Packet Drops for CCIL WAN Communication
  Timeout
  Retransmission
Kernel Patch on Router

## Slide 11: Contents
Introduction
WAN Emulator for Cluster-of-Clusters
Performance Evaluation of RDMA over IP
  Basic communication latency
  Computation and communication overlap
  Communication progress
  CPU resource requirements
  Unification of communication interface
  Bandwidth (throughput)
Conclusions and Future Work

## Slide 12: Basic Communication Latency
No impact of zero-copy on the basic communication latency
Basic communication is not an important metric
1KB Message Size

## Slide 13: Computation and Communication Overlap
Router
Switch
Switch
n0
n1
Computation
(t1)
Total
Time
(t2)
Overlap Ratio = t1/ t2
Send
Receive

## Slide 14: Computation and Communication Overlap
RDMA can achieve a better computation and communication overlap
Its benefit reduces as the network delay increases
1KB Message Size
242ms Computation
1098%
114%

## Slide 15: Communication Progress
Router
Switch
Switch
n0
n1
Response Delay
By Load
Data
Fetching
Latency
Request
Response

## Slide 16: Communication Progress
RDMA can achieve a better communication progress
Its benefit reduces as the network delay increases
16ms Response Delay
1KB Message Size
98%
65%

## Slide 17: CPU Resource Requirements
Router
Switch
Switch
n0
n1
…
40 Streams
Application
Application Execution Time?

## Slide 18: CPU Resource Requirements
RDMA-based communication does not affect to the application execution time
RDMA has a strong potential of saving the CPU resource
16KB Message Size

## Slide 19: Unification of Communication Interface
switch
switch
Inter-Cluster
Intra-Cluster
RDMA over IP can provide a unified communication interface
RDMA can achieve lower latency for intra-cluster communication
38%

## Slide 20: Bandwidth
Where is the bottleneck?
  Ethernet devices on the router
  TCP window size
16KB Message Size

## Slide 21: Contents
Introduction
WAN Emulator for Cluster-of-Clusters
Performance Evaluation of RDMA over IP
Conclusions and Future Work

## Slide 22: Conclusions
The first quantitative study of RDMA over IP on a WAN setup
WAN Emulator for Custer-of-Clusters
  Degen
RDMA over IP Can
  Save CPU resource on the server side even on a high delay WAN environment
  Achieve better
    computation and communication overlap
    communication progress
    peak bandwidth
  Provide unified interface

## Slide 23: Future Work
Performance Evaluations
  Other performance factors
    impact of address exchange
    bandwidth
  Application-level performance
WAN Emulator for Cluster-of-Clusters
  Delay model
  Other components
RDMA-aware Middleware for Widely Distributed Systems over WAN

## Slide 24: Acknowledgements
Our research is supported by the following organizations:
Current Funding support by
Current Equipment donations by

## Slide 25: Thank You
{ jinhy, narravul, browngre, vaidyana, balaji, panda}@
cse.ohio-state.edu
Network-Based Computing Laboratory
http://nowlab.cse.ohio-state.edu/
Network Based Computing
Laboratory