## Slide 1: Designing Next Generation Data-Centers with Advanced Communication Protocols and Systems Services
P. Balaji, K. Vaidyanathan, S. Narravula, H. –W. Jin and D. K. Panda
Network Based Computing Laboratory (NBCL)
Computer Science and Engineering
Ohio State University

## Slide 2: Introduction and Motivation
Interactive Data-driven Applications
  Scientific as well as Enterprise/Commercial Applications
    Static Datasets: Medical Imaging Modalities
    Dynamic Datasets: Stock value datasets, E-commerce, Sensors
  E-science
  Ability to interact with, synthesize and visualize large datasets
  Data-centers enable such capabilities
Clients initiate queries (over the web) to process specific datasets
  Data-centers process data and reply to queries

## Slide 3: Typical Multi-Tier Data-center Environment
Requests are received from clients over the WAN
Proxy nodes perform caching, load balancing, resource monitoring, etc.
If not cached, the request is forwarded to the next tiers  Application Server
Application server performs the business logic (CGI, Java servlets, etc.)
  Retrieves appropriate data from the database to process the requests
Proxy Server
Web-server (Apache)
Application Server (PHP)
Database Server (MySQL)
WAN
Clients
Storage
More Computation and Communication
Requirements

## Slide 4: Limitations of Current Data-centers
Communication Requirements
  TCP/IP used even in the data-center: Sub-optimal performance
    InfiniBand and other interconnects provide more features
  High Performance Sockets (e.g., SDP)
    Superior performance with no modifications
Advanced Data-center Services
  Minimize the computation requirements
    Improved caching of documents
    Issues with caching Dynamic (or Active) Content
  Maximize compute resource utilization
    Efficient resource monitoring and management
    Issues with heterogeneous load characteristics of data-centers

## Slide 5: Proposed Architecture
Existing Data-Center Components
RDMA
Atomic
Multicast
Sockets Direct Protocol
Protocol
Offload
Async. Zero-copy
Communication
Packetized
Flow-control
Dynamic Content
Caching
Global
Memory
Aggregator
Active Resource
Adaptation
Soft
Shared
State
Distributed
Lock
Manager
Point
To
Point
Advanced System Services
Data-Center
Service
Primitives
Advanced
Communication Protocols and Subsystems
Network
Dynamic Content
Caching
Soft
Shared
State
Active Resource
Adaptation
Async. Zero-copy
Communication

## Slide 6: Presentation Layout
Introduction and Motivation
Advanced Communication Protocols and Subsystems
Data-center Service Primitives
Dynamic Content Caching Services
Active Resource Adaptation Services
Conclusions and Ongoing Work

## Slide 7: The Sockets Protocol Stack
High Performance Sockets
(e.g., SDP)
High-speed Network
Device Driver
IP
TCP
Traditional Sockets
Sockets Interface
App #1
App #2
App #N
Berkeley Sockets Implementation
High-speed Network
Device Driver
IP
TCP
Traditional Sockets
Sockets Interface
Application
Offloaded
Protocol
Lower-level Interface
Advanced
Features
The Sockets Protocol Stack allows applications to utilize the network performance and capabilities with NO or MINIMAL modifications

## Slide 8: InfiniBand and Features
An emerging open standard high performance interconnect
High Performance Data Transfer
  Interprocessor communication and I/O
  Low latency (~1.0-3.0 microsec), High bandwidth (~10-20 Gbps) and low CPU utilization (5-10%)
Flexibility for WAN communication
Multiple Operations
  Send/Recv
  RDMA Read/Write
  Atomic Operations (very unique)
    high performance and scalable implementations of distributed locks, semaphores, collective communication operations
Range of Network Features and QoS Mechanisms
  Service Levels (priorities)
  Virtual lanes
  Partitioning
  Multicast
    allows to design a new generation of scalable communication and I/O subsystem with QoS

## Slide 9: SDP Latency and Bandwidth
“Sockets Direct Protocol over InfiniBand in Clusters: Is it Beneficial?”, P. Balaji, S. Narravula, K. Vaidyanathan, K. Savitha, D. K. Panda. IEEE International Symposium on Performance Analysis and Systems (ISPASS), 04.

## Slide 10: Zero-Copy Communication for Sockets
Receiver
Sender
Send Complete
Buffer 2
Send
Buffer 1
Send
Get Data
GET COMPLETE
SRC AVAIL
SRC AVAIL
Get Data
GET COMPLETE
Send Complete
Application Blocks
Application Blocks
Buffer 2
Buffer 1

## Slide 11: Asynchronous Zero-Copy SDP
Receiver
Sender
Memory Protect
Buffer 1
Send
GET COMPLETE
Get Data
Buffer 2
SRC AVAIL
Memory Unprotect
Memory Unprotect
Buffer 2
Buffer 1
Send
Memory Protect

## Slide 12: Throughput and Comp./Comm. Overlap
“Asynchronous Zero-copy Communication for Synchronous Sockets in the Sockets Direct Protocol (SDP) over InfiniBand”. P. Balaji, S. Bhagvat, H. –W. Jin and D. K. Panda. Workshop on Communication Architecture for Clusters (CAC); with IPDPS ‘06.

## Slide 13: Presentation Layout
Introduction and Motivation
Advanced Communication Protocols and Subsystems
Data-center Service Primitives
Dynamic Content Caching Services
Active Resource Adaptation Services
Conclusions and Ongoing Work

## Slide 14: Data-Center Service Primitives
Common Services needed by Data-Centers
  Better resource management
  Higher performance provided to higher layers
Service Primitives
  Soft Shared State
  Distributed Lock Management
  Global Memory Aggregator
Network Based Designs
  RDMA, Remote Atomic Operations

## Slide 15: Soft Shared State
Shared State
Data-Center
Application
Data-Center
Application
Data-Center
Application
Data-Center
Application
Data-Center
Application
Data-Center
Application
Get
Get
Get
Put
Put
Put

## Slide 16: Presentation Layout
Introduction and Motivation
Advanced Communication Protocols and Subsystems
Data-center Service Primitives
Dynamic Content Caching Services
Active Resource Adaptation Services
Conclusions and Ongoing Work

## Slide 17: Active Caching
Dynamic data caching – challenging!
Cache Consistency and Coherence
  Become more important than in static case
User Requests
Proxy Nodes
Back-End Nodes
Update

## Slide 18: Active Cache Design
Efficient mechanisms needed
  RDMA based design
  Load resiliency
Our cooperation protocols
  No-Dependency
  Invalidate-All
Client Polling based design

## Slide 19: RDMA based Client Polling Design
Front-End
Back-End
Request
Cache Hit
Cache Miss
Response
Version Read
Response

## Slide 20: Active Caching - Performance
Higher overall performance – Up to an order of magnitude
Performance is sustained under loaded conditions
Architecture for Caching Responses with Multiple Dynamic Dependencies in Multi-Tier Data-Centers over InfiniBand. S. Narravula, P. Balaji, K. Vaidyanathan, H. -W. Jin and D. K. Panda. CCGrid-2005

## Slide 21: Multi-tier Cooperative Caching
RDMA based schemes
Effective use of system-wide memory from across multiple tiers
Significant performance benefits
  Our Schemes
    BCC, CCWR, MTACC and HYBCC
  Up to 2-3 times compared to the base case
S. Narravula, H. -W. Jin, K. Vaidyanathan and D. K. Panda,
Designing Efficient Cooperative Caching Schemes for Multi-Tier
Data-Centers over RDMA-enabled Networks. IEEE/ACM
International Symposium on Cluster Computing and the Grid (CCGrid 06).

## Slide 22: Presentation Layout
Introduction and Motivation
Advanced Communication Protocols and Subsystems
Data-center Service Primitives
Dynamic Content Caching Services
Active Resource Adaptation Services
Conclusions and Ongoing Work

## Slide 23: Active Resource Adaptation
Increasing popularity of Shared data-centers
How to decide the number of proxy nodes vs. application servers vs. database servers
Current approach
  Use a rigid configuration
  Over-Provisioning
Active Resource Adaptation
  Reconfigure nodes from one tier to another tier
  Allocate resources based on system load and traffic pattern
  Meet QoS and Prioritization constraints
  Load Resiliency

## Slide 24: Active Resource Adaptation in Shared Data-Centers
WAN
Clients
Clients
Load Balancing Cluster (Site A)
Load Balancing Cluster (Site B)
Load Balancing Cluster (Site C)
Website A (low priority)
Website B (medium priority)
Website C (high priority)
Servers
Servers
Servers
Reconf-PQ reconfigures nodes for different websites but also guarantees fixed number of nodes to low priority requests
Hard QoS Maintained

## Slide 25: Active Resource Adaptation Design
Server
Website A
Load
Balancer
Server
Website B
Not Loaded
Loaded
Load Query
Load Query
Successful Atomic (Lock)
Successful Atomic (Update Counter)
Reconfigure Node
Successful Atomic (Unlock)
Load Shared
Load Shared
RDMA
RDMA

## Slide 26: Dynamic Reconfigurability using RDMA operations
“On the Provision of Prioritization and Soft QoS in Dynamically Reconfigurable Shared Data-Centers over InfiniBand”. `P. Balaji, S. Narravula, K. Vaidyanathan, H. –W. Jin and D. K. Panda. IEEE International Symposium on Performance Analysis of Systems and Software (ISPASS) ‘05.

## Slide 27: Presentation Layout
Introduction and Motivation
Advanced Communication Protocols and Subsystems
Data-center Service Primitives
Dynamic Content Caching Services
Active Resource Adaptation Services
Conclusions and Ongoing Work

## Slide 28: Conclusions
Proposed a novel framework for data-centers to address the current limitations
  Low performance due to high communication overheads
  Lack of efficient support of advanced features such as active caching, dynamic resource adaptation, etc
Three-layer Architecture
  Communication Protocol Support
  Data-Center Primitives
  Data-Center Services
Novel approaches using the advanced features of InfiniBand
  Resilient to the load on the back-end servers
  Order of magnitude performance gain for several scenarios

## Slide 29: Work-in-Progress
Data-Center Primitives
  Efficient System-Wide Soft Shared State Mechanisms
  Efficient Distributed Lock Manager Mechanisms
Fine-Grained Active Resource Adaptation
  Fine-grain resource monitoring
  Resource adaptation with database servers and multi-stage reconfigurations
Detailed Data-Center Evaluation with the proposed framework

## Slide 30: Web Pointers
Network Based Computing
Laboratory
Website: http://www.cse.ohio-state.edu/~panda
Group Homepage: http://nowlab.cse.ohio-state.edu
Email: panda@cse.ohio-state.edu
NBCL

## Slide 31: Backup Slides (Sockets Direct Protocol)

## Slide 32: Sockets Direct Protocol (SDP)
IBA Specific Protocol for Data-Streaming
Defined to serve two purposes:
  Maintain compatibility for existing applications
  Deliver the high performance of IBA to the applications
Two approaches for data transfer: Copy-based and Z-Copy
Z-Copy specifies Source-Avail and Sink-Avail messages
  Source-Avail allows destination to RDMA Read from source
  Sink-Avail allows source to RDMA Write to the destination
Current implementation limitations:
  Only supports the Copy-based implementation
  Does not support Source-Avail and Sink-Avail

## Slide 33: The Sockets Protocol Stack
High Performance Sockets
(e.g., SDP)
High-speed Network
Device Driver
IP
TCP
Traditional Sockets
Sockets Interface
App #1
App #2
App #N
Berkeley Sockets Implementation
High-speed Network
Device Driver
IP
TCP
Traditional Sockets
Sockets Interface
Application
Offloaded
Protocol
Lower-level Interface
Advanced
Features
The Sockets Protocol Stack allows applications to utilize the network performance and capabilities with NO or MINIMAL modifications

## Slide 34: Designing High-Performance Sockets
Basic Idea of High-Performance Sockets
  “Hijack” standard sockets calls to use our implementation of sockets
  Hijacking is done through environment variables: non-intrusive
TCP/IP based sockets
  Uses simple yet generic approaches for data communication
  Copy data to temporary buffers
  Credit-based flow-control mechanism to avoid overrunning the receiver
High-performance Sockets can use similar approaches
  Network deals with reliability, data integrity, etc.
  Some amount of performance benefits are possible
  Several disadvantages
  Advanced mechanisms (e.g., RDMA) are not utilized

## Slide 35: TCP/IP-like Credit-based Flow Control
ACK
Sockets Buffers
Application Buffer
Sender
Application Buffer
Receiver
Sockets Buffers

## Slide 36: Limitations with Credit-based Flow Control
Sockets Buffers
Application Buffers
Sender
Application Buffers Not Posted
Receiver
Sockets Buffers
Credits = 4
Application Buffer
ACK
Receiver controlled buffer management – Statically sized temporary buffers
Can lead to excessive wastage of buffers
  E.g., if application buffers are 1 byte each and the socket buffers are 8KB each
  99.98% of the socket buffers remain unused
All messages going out on the network are 1 byte each
  Network performance is under-utilized for small messages

## Slide 37: Packetized Flow-Control
Sockets Buffers
Application Buffers
Sender
Receiver
Sockets Buffers
Packetization: Socket buffer is packetized to 1 byte granularity
  Sender side buffer management
    Utilizes advanced network features such as RDMA
  Avoids buffer wastage when transmitting small messages
  Improves throughput for small messages
Credits = 4
Application Buffers Not Posted
Application Buffer
ACK

## Slide 38: High Performance Sockets over VIA
“Impact of High Performance Sockets on Data Intensive Applications”, P. Balaji, J. Wu, T. Kurc, U. Catalyurek, D. K. Panda and J. Saltz. In the proceedings of IEEE High Performance Distributed Computing (HPDC) ’03.

## Slide 39: Evaluating Sockets over VIA (Data-Cutter Library)
Designed by University of Maryland
Component framework
User-defined pipeline of components
  Stream based communication
  Flow control between components
Several applications supported
  Virtual Microscope
  ISO Surface Oil Reservoir Simulator
Virtual Microscope
TCP
HPS
0
1
Reqd BW
0
1
HPS
TCP
Notes: Talk about data-cutter applications

## Slide 40: Virtual Microscope Application
Blind run
  Performance benefits: 3.5 times
After re-distributing data
  Read chunks are smaller
  Load balancing is more fine-grained
  Benefits: Order of magnitude
  Can reach better image fetch rates
  Note: NO application changes still !
“Impact of High Performance Sockets on Data Intensive Applications”, P. Balaji, J. Wu, T. Kurc, U. Catalyurek, D. K. Panda and J. Saltz. In the proceedings of IEEE High Performance Distributed Computing (HPDC) ’03.

## Slide 41: Parallel Virtual File System (PVFS)
Network
Compute
Node
Compute
Node
Compute
Node
Compute
Node
Meta-Data
Manager
I/O Server
Node
I/O Server
Node
I/O Server
Node
Meta
Data
Data
Data
Data
Relies on Striping of data across different nodes
Tries to aggregate I/O bandwidth from multiple nodes
Utilizes the local file system on the I/O Server nodes

## Slide 42: Parallel I/O in Clusters via PVFS
PVFS: Parallel Virtual File System
  Parallel: stripe/access data across multiple nodes
  Virtual: exists only as a set of user-space daemons
  File system: common file access methods (open, read/write)
Designed by ANL and Clemson
iod
Local file systems
iod
Local file systems
mgr
…
Network
Posix
MPI-IO
libpvfs
Applications
Posix
MPI-IO
libpvfs
Applications
…
Control
Data
“PVFS over InfiniBand: Design and Performance Evaluation”, Jiesheng Wu, Pete Wyckoff and D. K. Panda. International Conference on Parallel Processing (ICPP), 2003.

## Slide 43: Evaluating Sockets over IBA (PVFS Performance)
“Sockets Direct Protocol over InfiniBand in Clusters: Is it Beneficial?”, P. Balaji, S. Narravula, K. Vaidyanathan, K. Savitha, D. K. Panda. IEEE International Symposium on Performance Analysis and Systems (ISPASS), 04.
“The Convergence of Ethernet and Ethernot: A 10-Gigabit Ethernet Perspective”, P. Balaji, W. Feng and D. K. Panda. IEEE Micro Journal ’06.

## Slide 44: SDP Latency and Bandwidth
“Sockets Direct Protocol over InfiniBand in Clusters: Is it Beneficial?”, P. Balaji, S. Narravula, K. Vaidyanathan, K. Savitha, D. K. Panda. IEEE International Symposium on Performance Analysis and Systems (ISPASS), 04.

## Slide 45: Data-Center Response Time
SDP shows very little improvement: Client network (Fast Ethernet) becomes the bottleneck
Client network bottleneck reflected in the web server delay: up to 3 times improvement with SDP

## Slide 46: Data-Center Response Time (Fast Clients)
SDP performs well for large files; not very well for small files

## Slide 47: Data-Center Response Time Split-up
IPoIB
SDP

## Slide 48: Data-Center Response Time (Without Connection Time Overhead)
Without the connection time, SDP would perform well for all file sizes

## Slide 49: Zero-copy Communication
Copy-based approaches can significantly limit performance
  Excessive CPU utilization and memory traffic
  Can limit performance to less than 35% of peak in some cases [jpdc05]
SRC Available
RDMA Read Data
GET Complete
Sender
Receiver
SINK Available
RDMA Write Data
PUT Complete
Sender
Receiver
“Exploiting NIC Architectural Support for Enhancing IP based Protocols on High Performance Networks”. H. –W. Jin, P. Balaji, C. Yoo, J. Y. Choi and D. K. Panda. Journal of Parallel and Distributed Computing (JPDC) ‘05

## Slide 50: Asynchronous Zero-copy Comm.: Design Issues
Handling a Page Fault
  Block-on-Write: Wait till the communication has finished
  Copy-on-Write: Copy data to internal buffer and carry on communication
Handling Buffer Sharing
  Buffers shared through mmap()
Handling Unaligned Buffers
  Memory protection is only in the granularity of a page
  Malloc hook overheads

## Slide 51: Impact of Page-faults on AZ-SDP
AZ-SDP has performance drawbacks if data is touched too often before send completes
If applications don’t touch data frequently, AZ-SDP outperforms both the other schemes

## Slide 52: Backup Slides (Shared State)

## Slide 53: Backup Slides (Dynamic Content Caching)

## Slide 54: Basic Client Polling Architecture
Front-End
Back-End
Request
Cache Hit
Cache Miss
Response

## Slide 55: Active Caching Architecture
Server Node
Mod
Server Node
Mod
Server Node
Mod
Server Node
Mod
Cooperation
Cache Lookup Counter maintained on the Application Servers
Proxy
Servers
Application
Servers

## Slide 56: Active Caching - Basic Design
Home Node based Client Polling
  Cache Documents assigned home nodes
Proxy Server Modules
  Client polling functionality
Application Server Modules
  Support “Version Reads” for client polling
  Handle updates

## Slide 57: Active Caching - Mapping Schemes
Dependency Lists
  Home node based
  Complete dependency lists
    Keep track of all dependencies
Invalidate All
  Single Lookup Counter for a given class of queries
  Low application server overheads

## Slide 58: Active Caching - Handling Updates
Database
Server
Ack (Atomic)
Application
Server
Application
Server
Application
Server
Update Notification
VAPI Send
Local
Search and
Coherent
Invalidate
HTTP
Request
HTTP
Response
DB Query (TCP)
DB Response

## Slide 59: Backup Slides (Active Resource Adaptation)

## Slide 60: Efficient Fine-Grained Resource Monitoring
Fine-grained resource monitoring can help in providing better system-level services like process migration, load balancing, etc
How to provide fine-grained and accurate resource information of loaded back-end servers to the front-end node
Current approach
  Use a two-sided communication mechanism like TCP/IP
  Asynchronous Vs Synchronous approach
Can we design a fine-grained resource monitoring scheme using RDMA operations?
  Use RDMA operations in the kernel space and pin kernel data structures for capturing the system load
  Synchronous by nature
  Apart from accuracy and no back-end CPU involvement, this approach provides more system information like interrupts pending on CPUs
Scheme can be used for other system-level services like reconfiguration, process migration

## Slide 61: Connection Load Accuracy and Impact on Load Balancing
Accuracy of RDMA-Sync closely matches the actual connection load in comparison with all other schemes
RDMA-Sync monitoring assists load-balancing in improving the throughput in comparison with Socket-Async scheme

## Slide 62: Reconfiguration Implementation Details
History Aware Reconfiguration
  Avoiding Server Thrashing by maintaining a history of the load pattern
Reconfigurability Module Sensitivity
  Time Interval between two consecutive checks
Maintaining a System Wide Shared State
Shared State with Concurrency Control
Tackling Load-Balancing Delays

## Slide 63: Locking Mechanisms
We propose a two-level hierarchical locking mechanism
  Internal Lock for each web-site cluster
    Only one load-balancer in a cluster can attempt a reconfiguration
  External Lock for performing reconfiguration
    Only one web-site can convert any given node
  Both locks performed remotely using InfiniBand Atomic Operations
Server
Load Balancer
Internal Lock
Internal Lock
External Lock
Website A
Website B
Website C

## Slide 64: Tackling Load-Balancing Delays
Load-Balancing Delays
  After a reconfiguration, balancing of load might take some time
  Locking mechanisms only ensure no simultaneous transitions
  We need to ensure that all load-balancers are aware of reconfigurations
Server
Website A
Load
Balancer
Server
Website B
Not Loaded
Loaded
Load Query
Load Query
Successful Atomic (Lock)
Successful Atomic (SUC)
Reconfigure Node
Successful Atomic (Unlock)
Load Shared
Load Shared
Dual Counters
  Shared Update Counter (SUC)
  Local Update Counter (LUC)
On reconfiguration:
  LUC should be equal to SUC
  All remote SUCs are incremented

## Slide 65: Basic Dynamic Reconfigurability Performance
Large Burst Length allows reconfiguration of the system closer to the best case; reconfiguration time is negligible;
Performs comparably with the static scheme for small burst sizes

## Slide 66: Reconfigurability Performance with Prioritization and QoS
Reconf does not perform any additional reconfiguration
Reconf and Reconf-P allocate maximum number of nodes to the low-priority website whereas Reconf-PQ allocates nodes to the QoS guaranteed to that website.
Case 1: A load of high priority requests arrives when a load of low priority requests already exists
Case 2: A load of low priority requests arrives when a load of high priority requests already exists
Case 3: Both high and low priority requests arrive simultaneously

## Slide 67: QoS Meeting Capability
Reconf and Reconf-P perform well only in some cases and lack consistency in providing the guaranteed QoS requirements to both websites
Reconf-PQ meets the guaranteed QoS requirements in all cases

## Slide 68: QoS Meeting Capability – Zipf and Worldcup Traces
Similar trends are seen for Zipf and Worldcup traces with QoS meeting capability of nearly 100% for Reconf-PQ

## Slide 69: Backup Slides (Soft Shared State)

## Slide 70: Efficient Soft Shared State Primitive
Higher-level services use some kind of a shared state
Current approach
  Lack of a software layer; adhoc in manner
  Uses two-sided communication mechanism like TCP/IP
  Does not cater to the requirements of higher-level services such as coherency, consistency, timestamping, etc
Need for Soft Shared State Primitive
  Ease of use, simple operations like get(), put()
  Better Performance using advanced operations such as RDMA and atomics
Proposed Architecture
  Coherent Shared State
  Non-Coherent Shared State
  Timestamp-based Shared State
  Memory Stacked Shared State