## Slide 1: Advanced Flow-control Mechanisms for the Sockets Direct Protocol over InfiniBand
P. Balaji, S. Bhagvat, D. K. Panda, R. Thakur, and W. Gropp
Mathematics and Computer Science, Argonne National Laboratory
High Performance Cluster Computing, Dell Inc.
Computer Science and Engineering, Ohio State University

## Slide 2: High-speed Networking with InfiniBand
High-speed Networks
  A significant driving force for ultra-large scale systems
  High performance and scalability are key
  InfiniBand is a popular choice as a high-speed network
What does InfiniBand provide?
  High raw performance (low latency and high bandwidth)
  Rich features and capabilities
    Hardware offloaded protocol stack (data integrity, reliability, routing)
    Zero-copy communication (memory-to-memory)
    Remote direct memory access (read/write data to remote memory)
    Hardware flow-control (sender ensures receiver is not overrun)
    Atomic operations, multicast, QoS and several others

## Slide 3: TCP/IP on High-speed Networks
TCP/IP unable to keep pace with high-speed networks
  Implemented purely in software (hardware TCP/IP incompatible)
  Utilizes the raw network capability (e.g., faster network link)
  Performance limited by the TCP/IP stack
    On a 16Gbps network, TCP/IP achieves 2-3 Gbps
  Reason: Does NOT fully utilize network features
    Hardware offloaded protocol stack
    RDMA operations
    Hardware flow-control
Advanced features of InfiniBand
  Great for new applications!
  How should existing TCP/IP applications use them?

## Slide 4: Sockets Direct Protocol (SDP)
Industry standard high-performance sockets
Defined for two purposes:
  Maintain compatibility for existing applications
  Deliver the performance of networks to the applications
Many implementations:
  OSU, OpenFabrics, Mellanox, Voltaire
High-speed Network
Device Driver
IP
TCP
Sockets
Sockets Direct
Protocol
(SDP)
Sockets Applications or Libraries
Advanced
Features
Offloaded
Protocol
SDP allows applications to utilize the network performance and capabilities with ZERO modifications

## Slide 5: SDP State-of-Art
SDP standard specifies different communication designs
  Large Messages: Synchronous Zero-copy design using RDMA
  Small Messages: Buffer-copy design with credit-based flow-control using send-recv operations
These designs are often times not the best !
Previously, we proposed Asynchronous Zero-copy SDP to improve the performance of large messages [balaji07:azsdp]
In this paper, we propose new flow-control techniques
  Utilizing RDMA and hardware flow-control
  Improve the performance of small messages
[balaji07:azsdp] “Asynchronous Zero-copy Communication for Synchronous Sockets in the Sockets Direct Protocol over InfiniBand”. P. Balaji, S. Bhagvat, H. –W. Jin and D. K. Panda. Workshop on Communication Archictecture for Clusters (CAC), with IPDPS 2007.

## Slide 6: Presentation Layout
Introduction
Existing Credit-based Flow-control design
RDMA-based Flow-control
NIC-assisted RDMA-based Flow-control
Experimental Evaluation
Conclusions and Future Work

## Slide 7: Credit-based Flow-control
Flow-control needed to ensure sender does not overrun the receiver
Popular flow-control for many programming models
  SDP, MPI (MPICH2, OpenMPI), File-systems (PVFS2, Lustre)
  Generic to many networks  does not utilize many exotic features
TCP/IP like behavior
  Receiver presents N credits; ensures buffering for N segments
  Sender sends N message segments before waiting for an ACK
  When receiver application reads out data and receive buffer is free, an acknowledgment is sent out
SDP credit-based flow-control uses static compile-time decided credits (unlike TCP/IP)

## Slide 8: Credit-based Flow-control
ACK
Sockets Buffers
Application Buffer
Sender
Application Buffer
Receiver
Sockets Buffers
Receiver has to pre-specify buffers in which data should be received
  InfiniBand requirement for Send-receive communication
Sender manages send buffers and receiver manages receive buffers
  Coordination between sender-receiver through explicit acknowledgments
Credits = 4

## Slide 9: Limitations with Credit-based Flow-control
Sockets Buffers
Application Buffers
Sender
Application Buffers Not Posted
Receiver
Sockets Buffers
Credits = 4
Application Buffer
ACK
Receiver controls buffers – Statically sized temporary buffers
Two primary disadvantages:
  Inefficient resource usage  excessive wastage of buffers
  Small messages pushed directly to network
    Network performance is under-utilized for small messages

## Slide 10: Presentation Layout
Introduction
Existing Credit-based Flow-control design
RDMA-based Flow-control
NIC-assisted RDMA-based Flow-control
Experimental Evaluation
Conclusions and Future Work

## Slide 11: InfiniBand RDMA capabilities
Remote Direct Memory Access
  Receiver transparent data placement  can help provide a shared-memory like illusion
  Sender-side buffer management  sender can dictate which position in the receive buffer the data should be placed
RDMA with Immediate-data
  Requires receiver to explicitly check for the receipt of data
  Allows receiver to know when the data has arrived
  Loses receiver transparency!
  Still retains sender-side buffer management
In this design, we utilize RDMA with immediate data

## Slide 12: RDMA-based Flow-control
Sockets Buffers
Application Buffers
Sender
Receiver
Sockets Buffers
Utilizes InfiniBand RDMA with Immediate Data feature
  Sender side buffer management
Avoids buffer wastage for small-medium messages
Uses an immediate send threshold to improve the throughput for small-medium messages using message coalescing
Immediate Send Threshold = 4
Application Buffers Not Posted
Application Buffer
ACK

## Slide 13: Limitations of RDMA-based Flow-control
Sockets Buffers
Application Buffers
Sender
Receiver
Sockets Buffers
Immediate Send Threshold = 4
Application Buffers Not Posted
Application Buffer
Application
is computing
Remote credits are available, data is present in sockets buffer
Communication progress does not take place
ACK

## Slide 14: Presentation Layout
Introduction
Existing Credit-based Flow-control design
RDMA-based Flow-control
NIC-assisted RDMA-based Flow-control
Experimental Evaluation
Conclusions and Future Work

## Slide 15: Hardware vs. Software Flow-control
InfiniBand hardware provides a naïve message level flow control mechanism
  Guarantees that a message is not sent out till the receiver is ready
  Hardware takes care of progress even if application is busy with other computation
  Does not guarantee that the receiver has posted a sufficiently large buffer  buffer overruns are errors!
  Does not provide message coalescing capabilities
Software Flow control schemes are more intelligent
  Message coalescing, segmentation and reassembly
  No progress if application is busy with other computation

## Slide 16: NIC-assisted RDMA-based Flow-control
NIC-Assisted Flow Control
  Hybrid Hardware/Software
  Takes the best of IB hardware flow-control and the software features of RDMA-based flow-control
Contains two main mechanisms:
  Virtual window mechanism
    Mainly for correctness – avoid buffer overflows
  Asynchronous interrupt mechanism
    Enhancement to virtual window mechanism
    Improves performance by coalescing data

## Slide 17: Virtual Window Mechanism
Sockets Buffers
Application Buffers
Sender
Receiver
Sockets Buffers
N / W = 4
Application Buffers Not Posted
Application Buffer
Application
is computing
ACK
For a virtual window size of W, the receiver posts N/W work queue entries, i.e., it is ready to receive N/W messages
Sender always sends message segments smaller than W
The first N/W messages are directly transmitted by the NIC
The later send requests are queued by the hardware
NIC-handled Buffers

## Slide 18: Asynchronous Interrupt Mechanism
Sockets Buffers
Application Buffers
Sender
Receiver
Sockets Buffers
N / W = 4
Application Buffers Not Posted
Application Buffer
Application
is computing
ACK
After the NIC gives the interrupt, it still has some messages to send – allows us to effectively utilize the interrupt time without wasting it
We can coalesce small amounts of data – sufficient to reach the performance of RDMA-based flow control
IB Interrupt
Software handled Buffers

## Slide 19: Presentation Layout
Introduction
Existing Credit-based Flow-control design
RDMA-based Flow-control
NIC-assisted RDMA-based Flow-control
Experimental Evaluation
Conclusions and Future Work

## Slide 20: Experimental Testbed
16-node cluster
  Dual Intel Xeon 3.6GHz EM64T processors (single core, dual-processor)
  Each processor has 2MB L2 cache
  The system has 1GB of 533MHz DDR SDRAM
Connected using Mellanox MT25208 InfiniBand DDR adapters (3rd generation adapters)
Mellanox MTS-2400 24-port fully non-blocking switch

## Slide 21: SDP Latency and Bandwidth
RDMA-based and NIC-assisted flow-control designs outperform credit-based flow-control by almost 10X for some message sizes

## Slide 22: SDP Buffer Utilization
RDMA-based and NIC-assisted flow-control designs utilize the SDP buffers in a much better manner, which eventually leads to their better performance

## Slide 23: Communication Progress
Computation
Good
communication
Progress
Bad
communication
Progress

## Slide 24: Data-cutter Library
Component Framework for Combined Task/Data Parallelism
  Developed by U. Maryland
  Popular model for data-intensive applications
User defines sequence of pipelined components (filters and filter groups)
  Data parallelism
  Stream based communication
User tells the runtime system to generate/instantiate copies of filters
  Task parallelism
  Flow control between filter copies
  Transparent: single stream illusion
host1
R
0
R
1
host2
R
2
host3
Ra
0
host1
E
0
E
K
host2
E
K+1
E
N
host4
Ra
1
host5
Ra
2
host1
M
Cluster 1
Cluster 3
Cluster 2
Virtual Microscope Application

## Slide 25: Evaluating the Data-cutter Library
RDMA-based and NIC-assisted flow-control designs achieve about 10-15% better performance
No difference between RDMA-based and NIC-assisted designs  application makes regular progress

## Slide 26: Presentation Layout
Introduction
Existing Credit-based Flow-control design
RDMA-based Flow-control
NIC-assisted RDMA-based Flow-control
Experimental Evaluation
Conclusions and Future Work

## Slide 27: Conclusions and Future Work
SDP is an industry standard to allow sockets applications to transparently utilize the performance and features of IB
  Previous designs allow SDP to utilize some of the features of IB
  Capabilities of features such as hardware flow-control and RDMA for small messages have not been studied so far
In this paper we present two flow-control mechanisms which utilizes these features of IB
Shown that our designs can improve performance by up to 10X in some cases
Future Work: Integrate our designs in the OpenFabrics SDP implementation. Study MPI flow-control techniques.

## Slide 28: Thank You !
Contacts:
P. Balaji: balaji@mcs.anl.gov
S. Bhagvat: sitha_bhagvat@dell.com
D. K. Panda: panda@cse.ohio-state.edu
R. Thakur: thakur@mcs.anl.gov
W. Gropp: gropp@mcs.anl.gov
Web links:
http://www.mcs.anl.gov/~balaji
http://nowlab.cse.ohio-state.edu