## Slide 1: Sockets Direct Protocol for Hybrid Network Stacks: A Case Study with iWARP over 10G Ethernet
P. Balaji, S. Bhagvat, R. Thakur and D. K. Panda,
Mathematics and Computer Science, Argonne National Laboratory
High Performance Cluster Computing, Dell Inc.
Computer Science and Engineering, Ohio State University

## Slide 2: Hybrid Stacks for High-speed Networks
Hardware Offloaded Network Stacks
  Intelligent hardware common on popular networks (InfiniBand, Quadrics, hardware iWARP/10GE)
  Worked well to achieve high performance
  Adding more features  error prone, expensive, complex
Multi-core architectures
  Increased computational power
Hybrid Architectures
  Network Accelerators + Multi-cores
  Higher Performance + Flexibility to add more features
  Qlogic InfiniBand, Myri-10G, hybrid iWARP/10GE

## Slide 3: Sockets Direct Protocol (SDP)
Industry standard high-performance sockets for IB and iWARP
Defined for two purposes:
  Maintain compatibility for existing applications
  Deliver the performance of networks to the applications
Mapping of ‘byte-stream’ protocol to ‘message’ oriented semantics
  Zero copy (for large messages)
  Buffer copy (for small messages)
High-speed Network
Device Driver
IP
TCP
Sockets
Sockets Direct
Protocol
(SDP)
Sockets Applications or Libraries
Advanced
Features
Offloaded
Protocol
SDP allows applications to utilize the network performance and capabilities with ZERO modifications
Current SDP stacks are heavily optimized for hardware offloaded protocol stacks

## Slide 4: The Problem
The problem with network stacks
  Have not been able to keep pace with shift of paradigm
Sockets Direct Protocol (SDP)
  Assumes complete offload
  Optimizations like data buffering for small messages, message-level flow control
    Beneficial on hardware-offload network stack but redundant on hybrid networks. Imposes significant overheads!
SDP on hybrid stacks: Case study with iWARP/10GE
  Understand drawbacks of current SDP implementation
  Propose enhanced SDP design to avoid redundancy
  Study the impact of the new design on applications and benchmarks

## Slide 5: Presentation Layout
Introduction
Overview of iWARP (architecture and different designs)
SDP for Hybrid hardware-software iWARP
Experimental Evaluation
Conclusions and Future Work

## Slide 6: iWARP Components
Relatively new initiative by IETF/RDMAC
Extensions to Ethernet:
  Richer interface (zero-copy, RDMA)
  Backward compatible with TCP/IP
Three Protocol Layers
  RDMAP: Interface layer for applications
  RDDP: Core of the iWARP stack
    Connection management, packet de-multiplexing between connections
  MPA: Glue layer to deal with backward compatibility with TCP/IP
    CRC-based data integrity
    Backward compatibility to TCP/IP using markers
Application
Sockets
SDP, MPI etc.
Software
TCP/IP
10-Gigabit Ethernet
RDMAP Verbs
RDDP
MPA
Offloaded
TCP/IP

## Slide 7: Need for MPA: Issues with Out-of-Order Packets
Packet
Header
iWARP
Header
Data Payload
Packet
Header
iWARP
Header
Data
Payload
Packet
Header
iWARP
Header
Data
Payload
Packet
Header
iWARP
Header
Partial
Payload
Packet
Header
Partial
Payload
Packet
Header
iWARP
Header
Data
Payload
Packet
Header
iWARP
Header
Data
Payload
Delayed Packet
Out-Of-Order Packets
(Cannot identify iWARP header)
Intermediate Switch Segmentation

## Slide 8: Handling Out-of-Order Packets in iWARP
RDMAP
RDDP
CRC
Markers
TCP/IP
RDMAP
Markers
TCP/IP
RDDP
CRC
Markers
TCP/IP
RDMAP
RDDP
CRC
HOST
NIC
Software
Hardware
Hybrid
DDP
Header
Payload (IF ANY)
DDP
Header
Payload (IF ANY)
Pad
CRC
Marker
Segment
Length
Packet structure becomes overly complicated
Performing in hardware no longer straight forward!

## Slide 9: Implementations of iWARP
Several implementations exist
  Hardware implementations
    Optimized for performance
    Do not offer advanced features
  Software implementations
    More feature complete (handling out-of-order communication, packet drops etc)
    Not-optimized for performance
  Hybrid implementations [balaji07:iwarp]
    Best of both worlds
[balaji07:iwarp] “Analyzing the Impact of Supporting Out-of-order Communication on In-order Performance with iWARP”. P. Balaji, S. Bhagvat, D. K. Panda, R. Thakur and W. Gropp. SC ‘07

## Slide 10: Presentation Layout
Introduction
Overview of iWARP (architecture and different designs)
SDP for Hybrid hardware-software iWARP
Experimental Evaluation
Conclusions and Future Work

## Slide 11: SDP Limitations for Hybrid Network Stacks
Current SDP implementations
  Heavily optimized for hardware offloaded protocol stacks
  Do not perform well on Hybrid stacks
Performance limiting features of SDP on hybrid stacks
  Redundant buffer copy for small messages
  Protocol interface extensions for message coalescing
  Asynchronous flow control
  Portability across hybrid stacks

## Slide 12: Redundant Buffer Copy
SDP performs intermediate buffering for small messages
  Avoids memory registration costs for small messages
iWARP performs buffering to implement markers
  Strips of data need to be inserted in between the message
Our approach to avoiding buffering redundancy:
  Integrate SDP and iWARP buffering into a single copy based on information from the iWARP stack (e.g., TCP sequence number)
    SDP copies while leaving gaps for the markers
    iWARP fills in the markers into the space left by SDP
  Loss of generality: close interaction between SDP and iWARP
  Reduces buffering; improves performance

## Slide 13: Message Coalescing
Improves performance for small messages
  Difficult to implement for hardware offloaded stacks
  Easier in hybrid stacks as software resources can be used
Issue: protocol stacks such as iWARP have no interface to perform message coalescing
  Message sent out as soon as the application calls a send
Our solution:
  Extend iWARP interface for applications to “append” to messages
  If a message is still queued and the next message can be added to it, so the iWARP implementation can coalesce the messages
    Improves small message performance, as lesser headers are sent
  No performance loss, as previous message was anyway queued

## Slide 14: Query Mechanism for iWARP
Portability across different network stacks affected by proposed changes
  E.g., disabling buffer copy is beneficial only for hybrid stacks, and not for hardware offloaded stacks
Different hybrid stacks might provide different features
  We should not have to develop a separate SDP for each such network stack
Solution: Extend iWARP to allow applications to query functionality
  E.g., is buffer copy provided in software?
Allows SDP to query functionality and execute appropriately

## Slide 15: Presentation Layout
Introduction
Overview of iWARP (architecture and different designs)
SDP for Hybrid hardware-software iWARP
Experimental Evaluation
Conclusions and Future Work

## Slide 16: SDP Latency and Bandwidth
Chart: SDP Latency
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1K | 2K
SDP/iWARP (basic) | 15.947 | 16.01 | 16.056 | 15.998 | 16.153 | 16.169 | 16.455 | 16.947 | 18.204 | 20.362 | 23.443 | 29.191
SDP/iWARP (enhanced) | 14.854 | 14.867 | 14.944 | 14.932 | 15.012 | 14.989 | 15.23 | 15.992 | 16.991 | 18.934 | 22.034 | 27.456
Chart: SDP Bandwidth
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1K | 2K | 4K | 8K | 16K | 32K | 64K | 128K | 256K
SDP/iWARP (basic) | 0.0004 | 0.0534 | 0.4525 | 3.5456 | 12.5236 | 80.8764 | 275.5376 | 704.5346 | 1434.9567 | 2447.7646 | 3632.4622 | 4323.3254 | 4812.5475 | 5154.7457 | 5215.5634 | 5302.6855 | 5247.5685 | 5264.5899 | 4156.7856
SDP/iWARP (integrated) | 0.0004 | 5.0604 | 16.5341 | 39.5436 | 89.1236 | 176.5894 | 356.7633 | 978.0991 | 1852.3757 | 3012.415 | 4315.2366 | 5256.2673 | 5809.2356 | 6312.4155 | 6381.5432 | 6379.0908 | 6389.151 | 6370.1258 | 5299.1998
The enhanced SDP/iWARP outperforms the basic SDP/iWARP in both the latency (10%) and bandwidth (20%) benchmarks

## Slide 17: SDP Cache to Network Traffic Ratio
Chart: SDP Cache Miss Ratio (Transmit Side)
| 16 | 256 | 4k | 64k | 256K
SDP (basic) | 5.47 | 4.08 | 3.982 | 3.967 | 4.144 | 4.096
SDP (enhanced) | 2.528 | 2.164 | 2.202 | 2.127 | 2.001 | 2.169
Chart: SDP Cache Miss Ratio (Receive Side)
| 1 | 16 | 256 | 4K | 64K | 256K
SDP (basic) | 3.531 | 2.995 | 3.081 | 2.968 | 3.019 | 3.061
SDP (enhanced) | 1.494 | 1.482 | 1.018 | 1.187 | 1.037 | 1.021

## Slide 18: Application-level Performance
Chart: Virtual Microscope Application (1KB)
| 512x512 | 1024x1024 | 2048x2048 | 4096x4096
SDP (basic) | 0.442 | 1.111 | 3.609 | 5.12
SDP (enhanced) | 0.422 | 1.06 | 3.5 | 4.88
Chart: Iso-surface Application (8KB)
| 1024x1024 | 2048x2048 | 4096x4096 | 8192x8192
SDP (basic) | 18.539 | 75.059 | 247.1 | 340.565
SDP (enhanced) | 18.11 | 71.303 | 235.237 | 323.809
The enhanced SDP/iWARP outperforms the basic SDP/iWARP by 5% for the iso-surface application and virtual microscope application

## Slide 19: Presentation Layout
Introduction
Overview of iWARP (architecture and different designs)
SDP for Hybrid hardware-software iWARP
Experimental Evaluation
Conclusions and Future Work

## Slide 20: Conclusions and Future Work
Current implementations of SDP are optimized for hardware offloaded network stacks
  Performance overhead on hybrid stacks due to redundant features
We presented an extended design for SDP
  Optimizes its execution based on underlying network features (e.g., what features are offloaded/onloaded)
  Demonstrated significant performance benefits
Future Work:
  Extend support for hybrid network stacks to other programming models as well

## Slide 21: Thank You !
Contacts:
P. Balaji: balaji@mcs.anl.gov
S. Bhagvat: sitha_bhagvat@dell.com
D. K. Panda: panda@cse.ohio-state.edu
R. Thakur: thakur@mcs.anl.gov
Web links:
http://www.mcs.anl.gov/~balaji
http://nowlab.cse.ohio-state.edu