## Slide 1: Massively Parallel Genomic Sequence Search on Blue Gene/P
Heshan Lin (NCSU)
Pavan Balaji (ANL)
Ruth Poole, Carlos Sosa (IBM)
Xiaosong Ma (NCSU & ORNL)
Wu Feng (VT)

## Slide 2: Sequence Search
Fundamental tool in computational biology
  Search similarities between a set of query sequences and sequence databases (DBs)
  Analogous to web search engines
  Example application: predict functions of newly discovered sequences
 | Web Search Engine | Sequence Search
Input | Keyword(s) | Query sequence(s)
Search space | Internet | Known sequence database
Output | Related web pages | DB sequences similar to the query
Sorted by | Closeness & rank | Similarity score

## Slide 3: Demands of Large-scale Sequence Search
Exponentially Growing
Genomic databases growing faster than compute capability of single CPU
  CPU clock scaling hits the power wall
Many biological problems requiring large-scale sequence search
  Example: “Finding Missing Genes”
  Compute: 12,000+ cores across 7 supercomputer centers worldwide
  WAN: Shared Gigabit Ethernet
  Feat: Completed in 10 days what would normally take years to finish
Storage Challenge Award

## Slide 4: Challenge: Scaling of Sequence Search
Performance of a massively parallel sequence search tool – mpiBLAST BG/L prototype
  Search 28,014 Arabidopsis thaliana against the NCBI NT DB
93%
70%
55%

## Slide 5: Our Major Contributions
Identification of key design issues of scalable sequence search on next-generation massively parallel supercomputers
I/O and scheduling optimizations that allow efficient sequence searching across 10,000s of processors
  An extended prototype of mpiBLAST on BG/P with up to 32,768 compute cores (93% efficiency).

## Slide 6: Road Map
Introduction
Background
Optimizations
Performance Results
Conclusion

## Slide 7: BLAST & mpiBLAST
BLAST (Basic Local Alignment Sequence Tool)
  De facto standard tool for sequence search
  Computationally intensive: O(n2) worst-case
  Algorithm: Heuristics-based alignment
    Execution time of a BLAST job hard to predic
mpiBLAST
  Originally master-worker with database segmentation
  Enhanced for large-scale deployments
    Parallel I/O [Lin05, Ching06]
    Hierarchical Scheduling [Gardner06]
    Integrated I/O & Scheduling [Thorsen07]

## Slide 8: Blue Gene/P System Overview
1024 nodes, 4096 cores per rack
  Compute node: Quad-core PowerPC 450, 2GB memory
Scalable I/O system
  Compute and I/O nodes organized into PSET
Five networks
  3D torus, global collective, global interrupt, 10-Gigabit Ethernet, control
Execution modes
  SMP, DUAL, VN
Node Card 32 Nodes
72 Racks PetaFlops
1 Rack 32 Node Cards

## Slide 9: Road Map
Introduction
Background
Optimizations
Performance Results
Conclusion

## Slide 10: Current mpiBLAST Scheduling
Scheduling hierarchy
Limitations
  Fixed worker-to-master mapping
  High overhead with fine-grained load balancing
SuperMaster
f1
P1,1
Partition 1
f2
P1,2
qi
qi
…
Master1
f1
P2,1
f2
P2,2
qj
qj
Master2
f1
Pn-1,1
Partition n
f2
Pn-1,2
qk
qk
Mastern-1
f1
Pn,1
f2
Pn,2
ql
ql
Mastern

## Slide 11: Scheduling Optimization Overview
Optimizations
  Allow mapping arbitrary workers to a master
  Hide balancing overhead with query prefetching
SuperMaster
f1
P1,1
Partition 1
f2
P1,2
f1
P1,3
qi
qi
qj
…
f2
P1,4
Master1
qj
f1
Pn,1
Partition n
f2
Pn,2
f1
Pn,3
qk
qk
ql
f2
Pn,4
Mastern
ql
prefetch

## Slide 12: Mapping on BG/P
…
Partition 1
Disk
Disk
Disk
Disk
Disk
DB frags cached in workers, queries streamed across
One output file per partition
Results merged and written to GPFS through I/O nodes
Compute Nodes
IO Node
IO Node
qi+2
qi
qi+1
qi+2
qi
qi+1
qi+2
qi
qi+1
…
…
Config example
  PSize 128
  4 DBs / partition
  32768/128 = 256 partitions
IO Node
Partition i
Compute Nodes
Compute Nodes
Partition 2
Partition i
File i
qi
qi+1
File 1
File 2
G P F S

## Slide 13: I/O Characteristics
Irregularity
  Output data from a process is unstructured and non-contiguous
  I/O data distribution varies from query to query
  Query search time are imbalanced across workers
…
…
Straightforward non-contiguous I/O bad for BG/P I/O systems
  Too many requests create contention at I/O node
  GPFS less optimized for small-chunk, irregular I/O [Yu06]

## Slide 14: Existing Option 1: Collective I/O
Optimizes accesses from N processes
  Two-phase I/O: Merge small, non-contiguous I/O requests into large, contiguous ones
Advantage
  Excellent I/O throughput
  Highly optimized on Blue Gene [Yu06]
Disadvantage
  Synchronization between processes
Suitable applications
  Synchronizations in the compute kernel
  Balanced computation time between I/O phases

## Slide 15: Option1 Implementation: WorkerCollective
qi
Merge blocks info
qi+1
Calculate offsets of qi
Output of qi
qi
qi+1
qi+2
qi
qi+1
qi+2
1
1
1
2
2
2
Search
Merge
1
Send evalue+size
2
Send offsets
3
Write data
4
Exchange data
3
3
Wait
4
4
4
qi+2
Worker 1
Worker 2
Worker 3
Master
Output File

## Slide 16: Existing Option2: Optimized Independent I/O
Optimized with data sieving
  Read-modify-write: read in large chunks and only modify target regions
Advantages
  Does not incur synchronizations
  Performs well for dense non-contiguous requests
Disadvantages
  Introduces redundant data accesses
  Causes lock contentions with false sharing

## Slide 17: Option2 Implementation: WorkerIndividual
qi
Merge blocks info
qi+1
Calculate offsets of qi
Worker 1
Worker 2
Worker 3
Master
qi+2
qi
qi+1
qi+2
qi
qi+1
qi+2
Search
Merge
1
Send evalue+size
1
2
Send offsets
3
Write data
1
1
2
2
2
3
3
3
3
Output of qi
Output File

## Slide 18: Our Design: Asynchronous Two-Phase I/O
Achieving high I/O throughput without forcing synchronization
  Asynchronously aggregate small, non-contiguous I/O requests into large chunks
Current implementation
  Master selects a write leader for each query
  Write leader aggregates requests from other workers

## Slide 19: Our Design Implementation: WorkerMerge
qi
Merge blocks info
qi+1
Calculate offsets of qi
qi+2
qi
qi+1
qi+2
qi
qi+1
qi+2
1
1
1
2
2
2
4
Output of qi
Search
Merge
1
Send evalue+size
2
Offsets
3
3
Worker 1
Worker 2
Worker 3
Master
Output File
3
Write data
4
Exchange data

## Slide 20: Discussion
WorkerMerge implementation concerns
  Non-blocking MPI communications vs. threads
  Incremental write to avoid memory overflow
    Only a limited amount of data collected and written at a time
Will split-collective I/O help?
  MPI_File_write_all_begin, MPI_File_write_all_end
  MPI_File_set_view is synchronized by definition

## Slide 21: Road Map
Introduction
Background
Optimizations
Performance Results
Conclusion

## Slide 22: Compare I/O Strategies – Single Partition
Experimental setup
  Database: NT (over 6 million seqs, 23 GB raw size)
  Query: 512 sequences randomly sampled from the database
  Metric: Overall execution time
WM outperforms WC and WI by a factor of 2.7 and 4.9

## Slide 23: Compare I/O Strategies – Multi-Partitions
Experimental setup
  Database: NT
  Query: 2048 sequences randomly sampled from the database
  Fixed partition size at 128, scale number of partitions

## Slide 24: Scalability on A Real Problem
Discovering “missing genes”
  Database: 16M microbial sequences
  Query: 0.25M randomly sampled sequences
  93% parallel efficiency
All to all search entire DB within 12 hours

## Slide 25: Road Map
Introduction
Background
Optimizations
Performance Results
Conclusion

## Slide 26: Conclusion
Blue Gene/P: Well-suited for massively parallel sequence search when designed properly
We proposed I/O and scheduling optimizations for scalable sequence searching across 10,000s processors
  mpiBLAST prototype scales efficiently (93% efficiency) on 32,768 cores on BG/P
For non-contiguous I/O with imbalanced compute kernels, collective I/O without synchronization is desirable

## Slide 27: References
O. Thorsen, K. Jiang, A. Peters, B. Smith, H. Lin, W. Feng and C. Sosa, "Parallel Genomic Sequence-Search on a Massively Parallel System," ACM Int’l Conference on Computing Frontiers, 2007.
H. Yu, R. Sahoo, C. Howson, G. Almasi, J. Castanos, M. Gupta J. Moreira, J. Parker, T. Engelsiepen, R. Ross, R. Thakur, R. Latham, and W. Gropp, "High Performance File I/O for the BlueGene/L Supercomputer," 12th IEEE Int’l Symposium on High-Performance Computer Architecture (HPCA-12), 2006.
M. Gardner, W. Feng, J. Archuleta, H. Lin and X. Ma, "Parallel Genomic Sequence-Searching on an Ad-Hoc Grid: Experiences, Lessons Learned, and Implications," IEEE/ACM Int’l Conference for High-Performance Computing, Networking, Storage and Analysis (SC), Best Paper Finalist, 2006.
H. Lin, X. Ma, P. Chandramohan, A. Geist and N. Samatova, "Efficient Data Access for Parallel BLAST," IEEE Int’l Parallel and Distributed Processing Symposium (IPDPS), 2005.
A. Ching, W. Feng, H. Lin, X. Ma and A. Choudhary, "Exploring I/O Strategies for Parallel Sequence Database Search Tools with S3aSim," ACM Int’l Symposium on High Performance Distributed Computing (HPDC), 2006.

## Slide 28: Thank You
Questions?