## Slide 1: Understanding Network Saturation Behavior on Large-Scale Blue Gene/P Systems
Pavan Balaji (presenter), Harish Naik and Narayan Desai
Mathematics and Computer Science Division
Argonne National Laboratory

## Slide 2: Massive Scale High End Computing
We have passed the Petaflop Barrier
  Two systems over the Petaflop mark in the Top500: LANL Roadrunner and ORNL Jaguar
  Argonne has a 163840-core Blue Gene/P
  Lawrence Livermore has a 286720-core Blue Gene/L
Exaflop systems will out by 2018-2020
  Expected to have about a hundred million processing elements
  Might be processors, cores, SMTs
Such large systems pose many challenges to middleware trying to take advantage of these systems

## Slide 3: Hardware Sharing at Massive Scales
At massive scales, number of hardware components cannot increase exponentially with system size
  Too expensive (cost plays a major factor!)
  E.g., Crossbar switches vs. Fat-tree networks
At this scale, most systems do a lot of hardware sharing
  Shared caches, shared communication engines, shared networks
More sharing means more contention
  The challenge is how do we deal with this contention?
  More importantly: what’s the impact of such architectures?

## Slide 4: Blue Gene/P Overview
Second Generation of the Blue Gene supercomputers
Extremely energy efficient design using low-power chips
  Four 850MHz cores on each PPC450 processor

## Slide 5: BG/P Network Stack
Uses five specialized networks
  Two of them (10G and 1G Ethernet) are used for File I/O and system management
  Remaining three (3D Torus, Global collective network, Global interrupt network) are used for MPI communication
    3D torus: 6 bidirectional links for each node (total of 5.1 GBps)
X-Axis
Z-Axis
Y-Axis

## Slide 6: Presentation Roadmap
Introduction
Network Communication Behavior on BG/P
Measuring Network Congestion with Hardware Counters
Concluding Remarks and Future Work

## Slide 7: Network Communication Behavior
Network communication between pairs would oftentimes have overlapping links
  This can cause network congestion
  Communication throttling is a common approach to avoid such congestion
On massive scale systems getting network congestion feedback to the source might not be very scalable
  Approach: If a link is busy, backpressure applies to all of the remaining 5 inbound links
  Each DMA engine verifies busy link before sending data
P0
P1
P2
P3
P4
P5
P6
P7

## Slide 8: Network Congestion Behavior
Chart: Message Size (bytes)
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1K | 2K | 4K | 8K | 16K | 32K | 64K | 128K | 256K | 512K | 1M
P2-P5 | 2.92 | 6.584 | 13.12 | 26.072 | 52.536 | 104.856 | 208.544 | 413.96 | 671.352 | 1355.136 | 2362.952 | 2366.208 | 2596.464 | 2798.344 | 2910.728 | 2970.688 | 2989.464 | 3005.016 | 3013.6 | 3017.536 | 3018.352
P3-P4 | 2.904 | 6.544 | 13.064 | 25.896 | 52.04 | 103.672 | 207.528 | 411.72 | 657.952 | 893.04 | 1212.272 | 1279.216 | 1349.496 | 1426.064 | 1467.272 | 1488.96 | 1494.232 | 1499.776 | 1502.744 | 1504.136 | 1504.376
No overlap | 3.222 | 6.402 | 12.763 | 25.226 | 51.174 | 101.78 | 202.797 | 400.834 | 655.891 | 1324.282 | 2195.234 | 2332.492 | 2563.568 | 2769.574 | 2885.639 | 2947.349 | 2968.43 | 2984.152 | 2992.056 | 2996.054 | 2997.386
P0
P1
P2
P3
P4
P5
P6
P7

## Slide 9: Communication Behavior on Massive-scale Systems
Global communication on a torus network is not a good idea
  With N processes, there will be N2 communication flows, but only 3N network links
  Too much over-subscription, even for small messages
Local communication models such as Cartesian grids (every process communicates with √N processes) or nearest neighbor are “expected” to be better
  But Cartesian grids and nearest neighbors mostly rely on a logical view of the processes, not the physical view (bugs in the MPI standard!)
  While the number of messages is not as bad as global communication, overlap of network flows is still possible

## Slide 10: 2D Nearest Neighbor: Process Mapping (XYZ)
X-Axis
Z-Axis
Y-Axis

## Slide 11: 2D Nearest Neighbor: Process Mapping (YXZ)
X-Axis
Z-Axis
Y-Axis

## Slide 12: HALO: Modeling Ocean Modeling
NRL Layered Ocean Model (NLOM) simulates enclosed seas, major oceans basins, and the global ocean
HALO was initially developed as the communication kernel for NLOM
  Gained popularity because of its similarity to other models as well (e.g., algebraic solvers)
  Rough indication of the communication behavior of other models as well, including CFD and nuclear physics
Distributes data on a 2D logical process grid and performs a nearest neighbor exchange along the logical grid

## Slide 13: Nearest Neighbor Performance
Chart: System Size : 16K Cores
| 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1K
XYZT | 18 | 19 | 20 | 23 | 31 | 45 | 70 | 137 | 271 | 496
TXYZ | 19 | 19 | 21 | 25 | 41 | 60 | 94 | 204 | 405 | 756
ZYXT | 19 | 19 | 20 | 25 | 41 | 60 | 99 | 208 | 429 | 832
TZYX | 18 | 19 | 20 | 23 | 30 | 43 | 65 | 121 | 226 | 412
Chart: System Size : 128K Cores
| 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1K
XYZT | 24 | 25 | 27 | 34 | 77 | 141 | 227 | 449 | 1145 | 2045
TXYZ | 19 | 19 | 21 | 25 | 40 | 59 | 93 | 201 | 399 | 745
ZYXT | 24 | 24 | 26 | 40 | 97 | 142 | 234 | 468 | 960 | 1812
TZYX | 19 | 19 | 21 | 25 | 41 | 59 | 92 | 194 | 389 | 737

## Slide 14: Presentation Roadmap
Introduction
Network Communication Behavior on BG/P
Measuring Network Congestion with Hardware Counters
Concluding Remarks and Future Work

## Slide 15: BG/P Network Hardware Counters
Blue Gene/P provides various counters for measuring network activity
Flow control stall event (Torus Network)
  When a packet needs to be sent out, it is queued in a DMA FIFO
  The DMA engine checks if the link is free (no ongoing traffic) and if it is, tries to send out a packet
  Each link uses a credit-based flow control; if a link has no credit available, a flow control stall event is generated
Collective network queue (Collective Network)
  BG’s collective network can only have one ongoing operation
  Other requests are queued; length of the queue gives an indication of congestion on the collective network

## Slide 16: Network Congestion with Global Communication
Chart: Alltoallv (MPI_COMM_WORLD)
| 2048.0 | 4096.0 | 8192.0 | 16384.0 | 32784.0
Series 1 | 98534211 | 12300117766 | 59495561360 | 127358884212 | 164509464480
Chart: Allgather (MPI_COMM_WORLD)
| 2048.0 | 4096.0 | 8192.0 | 16384.0 | 32784.0
Series 1 | 954625 | 1617890 | 2429642 | 4878662 | 15522853

## Slide 17: Network Congestion with Cartesian Communication
Chart: Alltoallv (Cartesian): 64KB message size
| 2048.0 | 4096.0 | 8192.0 | 16384.0 | 32784.0
Series 1 | 1627120 | 256817526 | 1916473261 | 3624513911 | 242725525
Drop in congestion?
Reason: Impact of system layout

## Slide 18: Impact of System Layout on Congestion
System size vs. congestion
  In general larger system means more congestion, but not always true
Increasing system size can sometimes decrease congestion
  BG/P is laid out as a 3D torus; doubling the system size does not have any implication on how the dimensions have changed
    A possible 4096 CPU system can have a configuration of 8 x 8 x 64
    A possible 8192 CPU system can have a configuration of 16 x 16 x 32
      X and Y dimensions have increased, but Z dimension has decreased
  Even if one dimension doubles and the remaining dimensions stay constant, it is not trivial to guess the amount of congestion
    8 x 8 x 64 partition is more elongated (possibly more congestion)
    16 x 16 x 32 partition is more cubic (possibly lesser congestion)

## Slide 19: Network Congestion with NN Communication
Chart: 2D Nearest Neighbor: 64KB Message size
| 2048.0 | 4096.0 | 8192.0 | 16384.0
Series 1 | 112276 | 122484 | 4758656 | 113353
Chart: 3D Nearest Neighbor: 64KB Message Size
| 2048.0 | 4096.0 | 8192.0 | 16384.0
Series 1 | 53606662 | 62175744 | 24135010 | 146512441

## Slide 20: Presentation Roadmap
Introduction
Network Communication Behavior on BG/P
Measuring Network Congestion with Hardware Counters
Concluding Remarks and Future Work

## Slide 21: Concluding Remarks
Massive scale systems such as Blue Gene and Cray tend to use flat torus networks instead of fat tree networks
  Lower cost (linearly increasing network cost, not super-linear)
  Lower failure rate (lesser components)
This means that there is going to be significantly more communication interleaving as compared to earlier
  This is obvious for global communication
  While not obvious, this is true for more localized communication too
We studied network congestion characteristics with different benchmarks on a large-scale Blue Gene/P
  … hopefully providing insights into what to expect at such scales

## Slide 22: Future Work
Process mapping tends to have a large impact on performance
  How do we determine process mapping up front without knowing what the application is going to do?
There are two dimensions of optimization for this:
  MPI virtual topology functionality: not very well optimized, not multi-core aware in many cases, not network topology aware (we probably need to start with fixing the bugs in the MPI standard)
  Communication description language (CDL)
    MPI virtual topology functions might not be easily usable in many cases (e.g., when the application cannot allow for rank reordering)
    CDL can allow applications to tell the process management system what the application communication characteristics are

## Slide 23: Thank You!
Contacts:
Pavan Balaji: balaji@mcs.anl.gov
Harish Naik: hnaik@mcs.anl.gov
Narayan Desai: desai@mcs.anl.gov