## Slide 1: Revisiting Network Interface Cards as First-Class Citizens
Wu-chun Feng (Virginia Tech)
Pavan Balaji (Argonne National Lab)
Ajeet Singh (Virginia Tech)

## Slide 2: Forecast
Application-network interface is the bottleneck in the network communication today.
Survey of existing system architectures.
  Evaluate their merits and demerits.
New system architecture proposed
  Network Interface card (NIC) treated as First-Class Citizens at par with other CPUs.
  New architecture potentially solves application-network interfacing problem.

## Slide 3: Outline
Motivation
Trends
Evolution of System Architectures
Current Status
NIC as First-Class Citizens
Problems and Solutions
Drawbacks
Conclusion

## Slide 4: Motivation
Problem: Application-to-network interface is still bottleneck
Network and I/O
Host
TCP/IP
NIC
RDMA reduces the overhead by 40-90%

## Slide 5: Trends : Ethernet Wire Time Vs Processing Time
Image Source: Intel Corporation
Chart: 
| 1991.0 | 1993.0 | 1995.0 | 1998.0 | 2001.0
Processing Time | 48 | 33 | 69 | 89 | 95
Ethernet Wire Time | 52 | 67 | 31 | 11 | 5

## Slide 6: Trends
CPU
  Multi-core systems
Memory Access Time (DRAM)
  7% - 9% decreases every year (5-70 ns now)
Memory Capacity
  Increasing four-fold every 3 years.
Network Link Bandwidth
  Already hundreds of Gbps and improving!
Application-to-Network Latency?
Notes: CPU speeds: Ten fold increase from 1991 to 2004… Last 4 years speeds have not even doubled…
AM speeds: 7-9% increase every year.
2x in 20 years! (Figure 5.1, pg. 374, H&P)
Reduce growing disparity with hierarchy.
  On-chip L1 cache --> non-blocking too!
  On-package L2 cache
  Pre-fetching and wider buses
Link BW: 4 Mbps (1986) - 6400 Mbps (1996). 160x increase per year!
Appl-to-network latency: Proportional to memory, memory bus, and I/O bus speed & bus crossings.
Memory bus peak: 6.4 Gbps (100 MHz * 64 bits/cycle)
sustained: 2-3 Gbps (pipeline: 20+ Gbps)
PCI I/O bus peak: 888 Mbps (WE’VE TOPPED OUT!)
AGP to memory bus: 4 Gbps peak
SEE Link BW vs. Memory Bus BW vs. I/O Bus BW

## Slide 7: Outline
Motivation
Trends
Evolution of System Architectures
Current Status
NIC as First-Class Citizens
Problems and Solutions
Drawbacks
Conclusion

## Slide 8: AMD NUMA Architecture

## Slide 9: Approach 1: NIC on I/O Bus
CPU
Disk
Northbridge
(memory controller hub)
Southbridge
(I/O controller hub)
CPU
Northbridge
(memory controller hub)
Memory Slots
Memory Slots
Internal
Bus
High- speed graphics bus(AGP
or PCI Express)
PCI
Bus
LPC
Bus
Network Interface Card
Graphics Card Slot
Flash BIOS ROM
Notes: Treated like a disk.
PCI bus has peak bandwidth of 866 Mbps
CPU – NIC communication through two bridges

## Slide 10: Approach 1: Features
I/O Bus is many order times slower than the Memory Bus (memory latency)
DMA initiation process is very expensive
Software overhead (OS intervention)
No direct access to CPU.
NIC connected to standard I/O Bus
Direct Memory Access (DMA) to easy out CPU

## Slide 11: Approach 2: NIC connected to memory bus (2004)
CPU
Disk
Northbridge
(memory controller hub)
Southbridge
(I/O controller hub)
CPU
Northbridge
(memory controller hub)
Memory Slots
Memory Slots
Internal
Bus
High- speed graphics bus(AGP
or PCI Express)
PCI
Bus
LPC
Bus
Network Interface Card
Flash BIOS ROM
PCI Slots
1
2
4
3

## Slide 12: Approach 2: Features
PCI-Express orders of magnitude faster than PCI
NIC closer to main memory (reduced latency)
Not integrated with memory subsystem
No direct access to CPU cache
DMA initiation process is very expensive
Software overhead (OS intervention)
Notes: PCI-X 1.0 - 2 Gbps
PCI-X 1.0 - 4.Gbps
PIC 866 Mbps

## Slide 13: Approach 3: Direct Cache Access Capability (Simulated)
CPU
CPU
Disk
Northbridge
(memory controller hub)
Southbridge
(I/O controller hub)
Northbridge
(memory controller hub)
Memory Slots
Memory Slots
Internal
Bus
High- speed graphics bus(AGP
or PCI Express)
PCI
Bus
LPC
Bus
Network Interface Card
Flash BIOS ROM
PCI Slots
1
2
Notes: Adapter capable of accessing processor cache
In this architecture, Cache lines modified by processor are read by the I/O adapter and vice versa.
Therefore there is a need to maintain coherency using the system interconnect.
Two main benefits:
Timely availability of data in cache -> lower average memory latency
Reduction in memory bandwith
Ideal implementation of DCA would eliminate the need to write the data to memory
Continuously updating the cache lines in the cache with new data

## Slide 14: Approach 3: Features
NIC has access to processor cache (low latency)
Reduced memory bandwidth requirement.
Not integrated with memory subsystem.
Software overhead (OS intervention)
Increases processor cache requirements.
Notes: Requesting Agent and Target Agent for multi-core systems.
Cash replacement policy not defined.

## Slide 15: Outline
Motivation
Trends
Evolution of System Architectures
Current Status
NIC as First-Class Citizens
Problems and Solutions
Drawbacks
Conclusion

## Slide 16: Where are we now?
Software
  Several high performance RDMA protocols available.
Hardware
  Intel’s Communication Stream Architecture subsumed by PCI-Express technology.
  Myrinet Cards also provide feature of User Level Network Interface.
  Qs-Net product of Quadrics is closest to the status of First-Class Citizen.

## Slide 17: Where Do We Go From Here?
What has been done so far?
  Bad NIC architecture
    Giving first-class citizenship to NIC (attaching NIC to memory bus), but treating it as a second-class citizen, i.e., peripheral device.
Obvious Solution
  RDMA
  Treat NIC as a first-class citizen. How?

## Slide 18: Outline
Motivation
Trends
Evolution of System Architectures
Current Status
NIC as First-Class Citizens
Problems and Solutions
Drawbacks
Conclusion

## Slide 19: Approach 4: NIC as First-Class Citizen (Proposed)
CPU
Disk
Northbridge
(memory controller hub)
Southbridge
(I/O controller hub)
Northbridge
(memory controller hub)
Memory Slots
Memory Slots
Internal
Bus
High- speed graphics bus(AGP
or PCI Express)
LPC
Bus
Graphics Card Slot
Flash BIOS ROM
PCI
Bus
PCI Slots
Network CPU

## Slide 20: First Class Citizens?
Beyond direct cache access.
Connected on to the faster memory bus (or PCI-e).
NIC integrated with memory sub-system.
Have processing capabilities.
Not a general purpose CPU but task-specific.
Have its own cache like other processors.
Treat NIC as a co-processor!

## Slide 21: Outline
Motivation
Trends
Evolution of System Architectures
Current Status
NIC as First-Class Citizens
Problems and Solutions
Drawbacks
Conclusion

## Slide 22: NIC Access º Memory Access

## Slide 23: Virtualize NIC & Bypass OS
Virtualize NIC
  High latency to access NIC
    Packets go through OS via Unix sockets.
    High DMA initiation overhead.
  + Easy protection of address spaces
  + Easy address translation
  Treat it like a main memory and not like a disk!
Notes: Virtualize NIC:
Enable the user process to read the data on the NIC using virtual addressing.
  Protection: Memory-map NIC memory. (Isolate one user process from another
  Translation: At page granularity level.
    OS virtualizes Disk requiring all disc access must be initiated through system calls
      Expensive
      Most microprocessors don’t support this efficiently
      Disk access are than 10-100 microsec
    Main memory is virtualized using through a virtual memory hardware
      Supported by all high performance microprocessors today
      Does not require OS intervention in a common case.
      Main memory divided into physical pages and mapped to user virtual pages on demand.
      Hardware structure called TLB (Translation Lookaside Buffer) does the translation.
      Memory access are much faster (less than a microsec )
    Accessing NI as virtual memory and not the OS can drastically improve performance.
Bypass OS
  Already being done by OS-bypass protocols such as ST and PM.
  Show considerable improvement in increasing the throughput.
  VIA (Virtual Interface Architecture) is a standard for kernel bypassing and RDMA.
    Developed by Compaq, Intel and Microsoft
    Basis for Infiniband, Iwarp

## Slide 24: NIC Access º Memory Access

## Slide 25: Cache NIC Registers/Data
NIC Registers Currently Uncached
  CPU accesses to NIC may have side effects (unlike normal cache memory)
  Behaves more like cache than main memory(passive)
  Cache replacement issue
Advantages
  + Low memory latency
  + Exploit temporal locality
    Remove unnecessary memory traffic (e.g. during polling)
  + Explicit Handshake required
Notes: Why NIC registers uncached?
1) CPU access to NIC memory often have side effects unlike normal cacheable memory. (Loads/stores appear strictly in order)
    2) No coherence on I/O buses. (They behave more like a processor cache than passive main memory…
  Must have ability to invalidate memory location as new messages arrive)
  3) Processor cache replacement: Could lose NIC registers cached due to cache block replacement.
  Handshake required between ULNI and processor for explicit cache block usage.
Advantages:
  Exploit temporal locality (e.g., status & ctrl registers) and thus remove unnecessary memory traffic. For example, if a CPU is polling on an uncached status register, every CPU poll goes across memory bus, bridge, and I/O bus before reaching NIC, resulting in wasted memory bus BW. If status register were cached, all unsuccessful polls would hit in CPU’s cache. When new msg arrives to chage status, the ULNI invalidates cached status reg.
  Explicit handshake to reuse cached NIC register.

## Slide 26: NIC Access º Memory Access

## Slide 27: NIC memory as cache – Block transfer
I/O Transfer
  Uncached load/stores to memory-mapped device registers transfer very few bytes (1-16 bytes)
  High DMA initiation overhead (through CPU)
Cache Block Transfer
  + High bandwidth (32-128 bytes)
  + Memory buses are optimized for cache block transfer
  + Cache-cache transfer
Notes: Treatinf the
NIC having its own cache… caches its registers in its cache..
Data Movement
  CPU performs uncached loads/stores to memory-mapped device registers and directly load/store data to/from CPU registers.
  CPU initiates a DMA request thru a system call or user-level DMA request.
Cache Block transfer
  CPU cache miss can be intercepted and directly satisfied by ULNI cache by a cache-cache transfer.

## Slide 28: NIC Access º Memory Access

## Slide 29: Proper Notification
Interrupt
  Heavyweight
    Cache corrupted due to context switch
  Corrupts the cache(s). Adversely affects cache hit rate.
    Results in added memory-bus traffic.
Cache Invalidation
  + “Non-intrusive”
    NIC invalidates cached NIC register in CPU’s cache.
    CPU misses on cached but invalidated NIC register & gets valid NIC register from NIC.
Notes: Cache corrupted due to context switch.

## Slide 30: NIC Access º Memory Access

## Slide 31: Buffering Packets
Use device memory of NIC
  Limited buffer space
Use virtual memory
  + Plentiful buffer space

## Slide 32: NIC Access º Memory Access
Notes: ACL Scalable Software folks: OOO access & spec.

## Slide 33: [NIC Access º Memory Access] Out-of-Order Access Possible
+ Additional scheduling flexibility in a dynamic pipeline.
    Certain loads/stores
      May be scheduled earlier than other loads/stores
    CPU may not need to stall ...
+ Speculative access
    Due to memory based queues
Notes: Speculative access SA more aggressive in tolerating the memory latency.
Branch prediction, speculate data addresses, data values and does the computation on the data
If predictions are incorrect rollback….
Three main problems in the performing OOO to NI memory:
1 ) I/O bus does not support multiple outstanding transactions… Forces processor access to CPU to be serialized on I/O Bus.
2) Due to NI memory side effects: Rollback not possible
3) Most microprocessors don’t allow speculative access on uncached loads /store.
Solutions:
Memory bus
By eliminating application programming interface
Caching NIC registers in processors’ cache

## Slide 34: NIC Access º Memory Access

## Slide 35: Memory-Based Queue API
Memory-Based Queue API vs. User-Level NIC API
  + Decouples NIC from CPU
    Sending/receiving packets = reading/writing queue memory
    Both CPU and NIC can send/receive multiple packets to/from queues without blocking
  + No longer explicit DMA initiation requests
  + Treat NIC queue accesses as side-effect-free memory accesses.
  + Enables Out-of-order and speculative access.
Notes: Allocated in virtual memory.
Decouples NIC from CPU
  User has no knowledge of how data is actually moved between CPU and NIC.
Details:
Circular with head and tail pointers
Receive queue and send queues
Tail pointer increment by processor in the send queue
If tail pointer not cached in the NI cache, it signals data store
Else send the data to network/ poll for the new messages.

## Slide 36: Outline
Motivation
Trends
Evolution of System Architectures
Current Status
NIC as First-Class Citizens
Problems and Solutions
Drawbacks
Conclusion

## Slide 37: Drawbacks
Proprietary Memory Bus
  Non-standard interface, but bridges possible.
Data Movement
  Lose explicit program control.
  Proposed solution currently applies only to bus-based cache-coherence protocols.
High Risk
  Standard interface needs to be developed and adopted.
Notes: EXAMPLES
Intel’s MPP Teraflop attaches a user-level network interface (ULNI) directly to the Pentium Pro memory bus.
SGI’s Power Challenge uses a bridge to convert between SGI’s proprietary bus & standard SCSI device.
Intel’s Accelerated Graphics Port / PCI-X is a standard bridge that offers graphics accelerators a dedicated high-bandwidth path to main memory.
Lower Risk Options
  Program control over the queue in the PCI controller.

## Slide 38: Conclusion
Application-network bottleneck is the biggest challenge.
Incremental adjustments in the system architecture are no longer sufficient to allow network to realize its full capacity.
Network interface cards must be treated as First-Class Citizens at par with other CPUs.

## Slide 39: Questions??
Contact Information:
Wu-chun Feng (feng@cs.vt.edu)
Pavan Balaji (balaji@mcs.anl.gov.in)
Ajeet Singh (ajeets@vt.edu)