## Slide 1: PMI: A Scalable Process-Management Interface for Extreme-Scale Systems
Pavan Balaji, Darius Buntinas, David Goodell, William Gropp, Jayesh Krishna, Ewing Lusk and Rajeev Thakur

## Slide 2: Introduction
Process management is integral part of HPC
Scalability and performance are critical
Close interaction between process management and parallel library (e.g., MPI) is important
  Need not be integrated
Separation allows
  Independent development and improvement
  Parallel libraries portable to different environments

## Slide 3: PMI
Generic process management interface for parallel applications
PMI-1 is widely used
  MVAPICH, Intel MPI, Microsoft MPI
  SLURM, OSC mpiexec, OSU mpirun
Introducing PMI-2
  Improved scalability
  Better interaction with hybrid MPI+threads

## Slide 4: PMI Functionality
Process management
  Launch and monitoring
    Initial job
    Dynamic processes
  Process control
Information exchange
  Contact information
  Environmental attributes

## Slide 5: System Model

## Slide 6: System Model
MPICH2
MVAPICH2
Intel-MPI
SCX-MPI
Microsoft MPI
Simple PMI
SMPD PMI
SLURM PMI
BG/L PMI
Hydra
MPD
SLURM
SMPD
OSC mpiexec
OSU mpirun
Communication Subsystem
MPI Library
PMI API
PMI Library
Process Manager

## Slide 7: Process Manager
Handles
  Process launch
    Start and stop processes
    Forwarding I/O and signals
  Information exchange
    Contact information to set up communication
Implementation
  May be separate components
  May be distributed
E.g., PBS, Sun Grid Engine, SSH

## Slide 8: PMI Library
Provides interface between parallel library and process manager
Can be system specific
  E.g, BG/L uses system specific features
Wire protocol between PMI library and PM
  PMI-1 and PMI-2 have specified wire protocols
  Allows PMI lib to be used with different PM
  Note: wire protocol and PMI API are separate entities
    PMI implementation need not have wire protocol

## Slide 9: PMI API
PMI-1 and PMI-2
Functions associated with
  Initialization and finalization
    Init, Finalize, Abort
  Information exchange
    Put, Get, Fence
  Process creation
    Spawn

## Slide 10: Information Exchange
Processes need to exchange connection info
PMI uses a Key-Value database (KVS)
At init, processes Put contact information
  E.g., IP address and port
Processes Get contact info when establishing connections
Collective Fence operation to allow optimizations

## Slide 11: Connection Data Exchange Example
At init
  Proc 0 Puts (key=“bc-p0”, value=“192.168.10.20;3893”)
  Proc 1 Puts (key=“bc-p1”, value=“192.168.10.32;2897”)
  Proc 0 and 1 call Fence
    PM can collectively distribute database
Later Proc 0 wants to send a message to Proc 1
  Proc 0 does a Get of key “bc-p1”
    Receives value “192.168.10.32;2897”
  Proc 0 can now connect to Proc 1

## Slide 12: Implementation Considerations
Allow the use of “native” process manager with low overhead
  Systems often have existing PM
    E.g., integrated with resource manager
  Minimize async processing and interrupts
Scalable data exchange
  Distributed process manager
  Collective Fence provides opportunity for scalable collective exchange

## Slide 13: Second Generation PMI

## Slide 14: New PMI-2 Features
Attribute query functionality
Database scope
Thread safety
Dynamic processes
Fault tolerance

## Slide 15: PMI-2 Attribute Query Functionality
Process and resource managers have system-specific information
  Node topology, network topology, etc.
Without this, processes need to determine this themselves
  Each process gets each other's contact-info to discover local processes
  O(p2) queries

## Slide 16: PMI-2 Database Scope
Previously KVS had only global scope
PMI-2 adds node-level scoping
  E.g., keys for shared memory segments
Allows for optimized storage and retrieval of values

## Slide 17: PMI-2 Thread Safety
PMI-1 is not thread safe
  All PMI calls must be serialized
    Wait for request and response
  Can affect multithreaded programs
PMI-2 adds thread safety
  Multiple threads can call PMI functions
  One call cannot block the completion of another

## Slide 18: PMI-2 Dynamic Processes
In PMI-1 a separate database is maintained for each MPI_COMM_WORLD (process group)
  Queries are not allowed across databases
  Requires out-of-band exchange of databases
PMI-2 allows cross-database queries
  Spawned or connected process groups can now query each other’s databases
  Only process group ids need to be exchanged

## Slide 19: PMI-2 Fault Tolerance
PMI-1 provides no mechanism for respawning a failed process
  New processes can be spawned, but they have a unique rank and process group
Respawn is critical for supporting fault-tolerance
  Not just for MPI but other programming models

## Slide 20: Evaluation and Analysis

## Slide 21: Evaluation and Analysis
PMI-2 implemented in Hydra process manager
Evaluation
  System information query performance
  Impact of added PMI functionality over native PM
  Multithreaded performance

## Slide 22: System Information Query Performance
PMI-1 provides no attribute query functionality
  Processes must discover local processes
  O(p2) queries
PMI-2 has node topology attribute
Benchmark (5760 cores on SiCortex)
  MPI_Init();MPI_Finalize();

## Slide 23: Process Launch (5760-core SiCortex)
Launch Time
Chart: System Size (cores)
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1K | 2K | 4K | 5760
PMI-1 | 0.5961 | 0.6419 | 0.7124 | 0.8839 | 1.0754 | 1.5217 | 2.7752 | 7.6873 | 29.0077 | 126.394 | 659.141 | 4387.48
PMI-2 | 0.418 | 0.481 | 0.581 | 0.523 | 0.621 | 0.623 | 0.652 | 0.8 | 0.849 | 1.287 | 2.932 | 6.361 | 16.658 | 28.468
PMI Request Count
Chart: System Size (cores)
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1K | 2K | 4K | 5760
PMI-1 | 5 | 18 | 44 | 122 | 371 | 1260 | 4588 | 17390 | 67586 | 266330 | 1057112
PMI-2 | 3 | 6 | 12 | 26 | 51 | 108 | 236 | 494 | 1026 | 2138 | 4440 | 9222 | 19118 | 26880

## Slide 24: Impact of PMI Functionality
Systems often have integrated process managers
  Not all provide PMI functionality
Efficient PMI implementation must make effective use of native process managers
  Minimizing overhead
Benchmark (1600 cores on SiCortex)
  Class C BT, EP and SP
  Using SLURM (which provides PMI-1)
  Using Hydra over SLURM (for launch and management) plus PMI daemon

## Slide 25: Runtime Impact of Separate PMI Daemons (1600 cores SiCortex)
Absolute Performance
Percentage Variation
Chart: Variation in Execution Time
| BT | EP | SP
SLURM | 0.013701 | 0.012712 | 0.051929
Hydra | 0.013492 | 0.02014 | 0.052282
Chart: Execution Time (seconds)
| BT | EP | SP
SLURM | 146.702 | 14.946 | 189.682
Hydra | 146.687 | 14.9 | 189.69

## Slide 26: Multithreaded Performance
PMI-1 is not thread safe
  External locking is needed
PMI-2 is thread safe
  Multiple threads can communicate with PM
  Hydra: lock only for internal communication
Benchmark (8-core x86_64 node)
  Multiple threads calling MPI_Publish_name(); MPI_Unpublish _name()
  Work is fixed, number of threads increases

## Slide 27: Multithreaded Performance
Chart: Thread Count
PMI-1 | 444.825 | 448.799 | 449.44 | 457.084 | 452.45 | 452.499 | 456.972 | 453.569
PMI-2 | 539.525 | 328.263 | 247.701 | 205.95 | 183.079 | 170.332 | 164.06 | 163.473

## Slide 28: Conclusion

## Slide 29: Conclusion
We presented a generic process management interface PMI
PMI-2: second generation eliminates PMI-1 shortcomings
  Scalability issues for multicore systems
  Issues for hybrid MPI-with-threads
  Fault tolerance
Performance evaluation
  PMI-2 allows better implementations over PMI-1
  Low overhead implementation over existing PM