## Slide 1: Enabling Concurrent Multithreaded MPI Communication on Multicore Petascale Systems
Gabor Dozsa1, Sameer Kumar1, Pavan Balaji2, Darius Buntinas2,
David Goodell2, William Gropp3, Joe Ratterman4, and Rajeev Thakur2
1 IBM T. J. Watson Research Center, Yorktown Heights, NY 10598
2 Argonne National Laboratory, Argonne, IL 64039
3 University of Illinois, Urbana, IL 61801
4 IBM Systems and Technology Group, Rochester, MN 55901
Joint Collaboration between Argonne and IBM

## Slide 2: Outline
Motivation
MPI Semantics for multi-threading
Blue Gene/P overview
  Deep computing messaging framework (DCMF)
Optimize MPI thread parallelism
Performance results
Summary

## Slide 3: Motivation
Multicore architectures with many threads per node
Running MPI processes on each core results in
  Less memory per process
  Higher TLB pressure
  Problem may not scale to as many processes
Hybrid Programming
  Use MPI across nodes
  Use shared memory within nodes (posix threads, OpenMP)
  MPI library accessed concurrently from many threads
Fully concurrent network interfaces that permit concurrent access from multiple threads
Thread optimized MPI library critical for hybrid programming

## Slide 4: MPI Semantics for Multithreading
MPI defines four thread levels
Single
  Only one thread will execute
Funneled
  The process may be multi-threaded, but only the main thread will make MPI calls
Serialized
  The process may be multi-threaded, and multiple threads may make MPI calls, but only one at a time: MPI calls are not made concurrently from two distinct threads
Multiple
  Multiple threads may call MPI, with no restrictions

## Slide 5: Blue Gene/P Overview

## Slide 6: BlueGene/P Interconnection Networks
3 Dimensional Torus – DMA responsible for handing packets
  Interconnects all compute nodes
  Virtual cut-through hardware routing
  3.4 Gb/s on all 12 node links (5.1 GB/s per node)
  0.5 µs latency between nearest neighbors, 5 µs to the farthest 100 ns
  Communications backbone for computations
Collective Network – core responsible for handling packets
  One-to-all broadcast functionality
  Reduction operations functionality
  6.8 Gb/s (850 MB/s) of bandwidth per link
  Latency of one way network traversal 1.3 µs
Low Latency Global Barrier and Interrupt
  Latency of one way to reach all 72K nodes 0.65 µs, MPI 1.2 µs

## Slide 7: BG/P Torus network and the DMA
Torus network accessed via a direct memory access unit
DMA unit sends and receives data with physical addresses
Messages have to be in contiguous buffers
DMA performs cache injection on sender and receiver
Resources in the DMA managed by software
Blue Gene/P Compute Card

## Slide 8: BG/P DMA
DMA Resources
  Injection Memory FIFOs
  Reception Memory FIFOs
  Counters
A collection of DMA resources forms a group
  Each BG/P node has four groups
  Access to a DMA group can be concurrent
  Typically used to support virtual node mode with four processes
Blue Gene/P Node Card

## Slide 9: Message Passing on the BG/P DMA
Sender injects a DMA descriptor
  Descriptor provides detailed information to the DMA on the actions to perform
DMA initiates intra-node or inter-node data movement
  Memory FIFO send : results in packets in the destination reception memory FIFO
  Direct put : moves local data to a destination buffer
  Remote get : pulls data from a source node to a local (or even remote) buffer
Access to injection and reception FIFOs in different groups can be done in parallel by different processes and threads

## Slide 10: Deep Computing Messaging Framework (DCMF)
Low level messaging API on BG/P
Supporting multiple paradigms on BG/P
Active message API
  Good match for LAPI, Charm++ and other active message runtimes
  MPI supported on this active message runtime
Optimized collectives

## Slide 11: Extensions to DCMF for concurrency
Introduce the notion of channels
  In SMP mode the four injection/reception DMA groups exposed as four DCMF channels
  New DCMF API calls
    DCMF_Channel_acquire()
    DCMF_Channel_release()
    DCMF progress calls enhanced to only advance acquired channel
    Channel state stored in thread private memory
      Pt-to-pt API unchanged
Channels are similar to the notion of enpoints proposal in the MPI Forum

## Slide 12: Optimize MPI thread concurrency

## Slide 13: MPICH Thread Parallelism
Coarse Grained
  Each MPI call is guarded by an ALLFUNC critical section macro
  Blocking MPI calls release the critical section enabling all threads to make progress
Fine grained
  Decrease size of the critical sections
  ALLFUNC macros are disabled
  Each shared resource is locked
    For example a MSGQUEUE critical section can guard a message queue
    The RECVQUEUE critical section will guard the MPI receive queues
    HANDLE mutex for allocating object handles
  Eliminate critical sections
    Operations such as reference counting can be optimized via scalable atomics (e.g. fetch-add)

## Slide 14: Enabling Concurrent MPI on BG/P
Messages to the same destination always use the same channel to preserve MPI ordering
Messages from different sources arrive on different channels to improve parallelism
Map each source destination pair to a channel via a hash function
  E.g. (srcrank + dstrank) % numchannels

## Slide 15: Parallel Receive Queues
Standard MPICH has two queues for posted receives and unexpected messages
Extend MPICH to have
  Queue of unexpected messages and posted receives for each channel
  Additional queue for wild card receives
Each process posts receives to the channel queue in the absence of wild cards
  When there is a wild card all receives are posted to the wild card queue
When a packet arrives
  First the wild card queue is processed after acquiring WC lock
  If its empty, the thread that receives the packet
    acquires channel RECVQUEUE lock
    Matches packet with posted channel receives or
    If no match is found a new entry is created in the channel unexpected queue

## Slide 16: Performance Results

## Slide 17: Message Rate Benchmark
Message rate benchmark where each thread exchanges messages with a different node

## Slide 18: Message Rate Performance
Zero threads = MPI_THREAD_SINGLE

## Slide 19: Thread scaling on MPI vs DCMF
Absence of receiver matching enables higher concurrency in DCMF

## Slide 20: Summary and Future work
We presented different techniques to improve throughput of MPI calls in multi-threaded architectures
Performance improves 3.6x on four threads
These techniques should be extendible to other architectures where network interfaces permit concurrent access
Explore lockless techniques to eliminate critical sections for handles and other resources
  Garbage collect request objects