## Slide 1: Designing Energy Efficient Communication Runtime Support for Data Centric Programming Models
Abhinav Vishnu1, Shuaiwen Song2,
Andres Marquez1, Kevin Barker1,
Darren J. Kerbyson1, Kirk Cameron2, Pavan Balaji3
1Pacific Northwest National Laboratory
2Virginia Tech
3Argonne National Laboratory

## Slide 2: Power is becoming the Key Challenge for the future
Ever increasing computational requirements of scientific domains
  Significantly rising to future 10-, 100-, 1000-petaflop systems
System energy consumption is not scalable
  Roadrunner (1.4PF) ~2.4MW, naïve scaling not possible
Aim for US DOE is a 1000x increase in computational performance with only a 10x increase in power consumption from present day
Energy efficiency important at all levels:
  Hardware, algorithms, programming models, system stack
We focus here on the communication runtime stack of Programming Models

## Slide 3: Questions posed for Energy Efficient Communication Runtime
How should an energy efficient one-sided communication runtime system for modern interconnects be designed ?
  What are the design challenges?
  What are the energy savings on today’s machines ?
  What is the impact on performance ?
  What can we expect from future systems?

## Slide 4: Programming models and Communications: Two-sided and One-sided
Example: Global Arrays
Two-Sided:
  Message requires cooperation on both sides.
  Useful for tightly coupled applications
  MPI common place with very-large application base
One-sided:
  Asynchronous Get, Put & atomic operations (accumulate) on data.
  Useful for applications with irregular communication characteristics
  Global Arrays: application base centered on Computational Chemistry, Subsurface modeling
P0
P1
P0
P1
Example: MPI

## Slide 5: Global Arrays: Programming Model that Provides Easy Access to Distributed Data
Aims: provide easy global access to distributed data
  Traditionally has suited to irregular access to dense arrays
  Application domains include Chemistry, Bio-informatics, sub-surface modeling
  Use of one-sided communication
Active development @ PNNL
  Arbitrary distributed data structures
  Fault Tolerance
  Task based execution
Global Address Space
Physically distributed data

## Slide 6: Global Arrays (cont.)
Example: Obtaining a sub-region from a distributed array
Global Arrays:
if (me = P0)
NGA_Get(g_a, lo, hi, buffer, ld);
Global Array handle
}
Global upper and lower indices of data patch
Local buffer and array of strides
}
Message Passing:
identify size and location of data
loop over processors:
  if (me = P_N) then
    pack data in local message buffer
    send block of data to message buffer on P0
  else if (me = P0) then
    receive block of data from P_N in message buffer
    unpack data from message buffer to local buffer
  endif
end loop
copy local data on P0 to local buffer
P0
P1
P2
P3
P0

## Slide 7: ARMCI: underlying communication runtime for Global Arrays
Aggregate Remote Memory Copy Interface (ARMCI)
Provides one-sided communication primitives
  Put, Get, Accumulate, Atomic Memory Operations
  Abstract network interfaces
Established & available on all leading platforms
  Cray XTs, XE
  IBM Blue Gene L | P
  Commodity interconnects (InfiniBand, Ethernet etc)
Further upcoming platforms
  IBM BlueWaters, Blue Gene Q
  Cray Cascade

## Slide 8: Asynchronous Agent for One-sided Communication
Asynchronous agent used for multiple purposes
  Accumulate and atomic memory operations
  Non-contiguous data transfer
  Needs to be active only during active communication
Default operation: Blocks/polls on a network event
Asynchronous
Agent Thread
Application Process
Node1
Coherency Domain
Node2

## Slide 9: Energy Efficiency Mechanisms for Communications
Get
Data
Get
Data
Get
Data
Get
Data
Interrupt
DVFS scaling
DVFS
No
Yes
Interrupt
Polling
Default
Energy Saving & increase in time
Dynamic Voltage/Frequency Scaling (DVFS)
  Scale down during communication, Freq (core), Voltage (socket)
  But may lead to increased latency
Interrupt Driven Execution
  Yield CPU & wake up on network event, BUT may increase latency

## Slide 10: Handling Different Data Transfer Types Leads to Differences in Possible Gains
Contiguous data transfer
  Request DVFS scale down after data transfer request initiated
  Interrupt driven execution also requested at this point
  DVFS scale up after data transfer has been completed
Non-contiguous (e.g. strided) data transfer
  Requires data copy in intermediate buffers
  DVFS/Interrupt based execution performed after data transfer request initiation
Result is less potential gain on non-contiguous transfers

## Slide 11: Experimental Test-Bed: The Energy Smart Data Center at PNNL
ESDC
  Developed with high energy efficiency in mind
  Integrated power monitoring
    Node level (some), Rack level, machine room level
  Also used to explore cooling techniques (spray cooling)
192 node compute cluster
  Node: Dual socket quad core (Intel Harpertown)
  2.33 GHz, 16GBytes main memory
  InfiniBand 4xDDR Fat-tree
DVFS possible:
  Enabled DFS scaling: 2.33 GHz &1.9 GHz
  Upper bound on expected benefits is only 20%
  Voltage scaling not available

## Slide 12: Evaluation Methodology
All-to-all personalized communication using ARMCI one-sided communication primitives
Accumulate/Get/Put Strided benchmarks
Metrics
  Normalized Energy consumed/Mbyte
  Normalized latency
  w.r.t. default (polling/no DFS)
For I = 0 to iterations do
For j = 1 to nprocs-1 do
Dest = myid + j
Put(data) to dest
Fence to dest
End for
End for
Time
Power
Timers: start & end (in code)
Power: sampled & averaged

## Slide 13: Results: ARMCI Get Performance
Combinations of Interrupt and DVFS approaches compared
For small message:
  Default (polling only) outperforms in latency and Energy/Mbytes
For large messages (> 32KB):
  Interrupt+DVFS improves Energy/Mbytes by ~6% with a small increase in latency (up to 5%)

## Slide 14: Results: ARMCI Put Performance
Interrupt+DVFS improves Energy/MBytes by up to 10% compared to default (polling only)
Negligible increase in latency (up to 5%)

## Slide 15: Results: ARMCI Accumulate Performance
Interrupt+DVFS improves Energy/MBytes by up to 5% compared to default (polling only)
Negligible increase in latency (up to 3%)

## Slide 16: Results: ARMCI Put Strided Performance
Interrupt+DVFS improves Energy/MBytes by up to 6% compared to default (polling only)
Negligible increase in latency (up to 3%)

## Slide 17: Summary of Results
 | Min Message Size (KB) | Increase (%) in Latency (@256KB) | Decrease (%) in Energy (@256KB)
Get | 32 | 5 | 6
Put | 16 | 5 | 9
Accumulate | 16 | 3 | 5
Strided Put | 16 | 2 | 6
Consistent results across different communication types
Recall maximum energy saving is < 20%
  Only two frequencies available: 2.3 & 1.9 GHz
Results show that a significant portion of this saving can be achieved
  E.g. for Get, the Energy saving is 6% (from a max of 20%)

## Slide 18: Results show limited improvements and for large transfers, BUT …
Results show that approach can result in energy reduction
  Limited by both speed of DVFS, & freq levels (on testbed)
  Expect greater potential from future processors
Greater impact of DVFS
Testbed limited to 2 frequencies (1.9 vs. 2.3 GHz)
Less overheads for DVFS (?)

## Slide 19: Conclusions
We presented the mechanisms for energy efficiency provided by modern processors and networks
We leveraged these mechanisms to design a communication runtime system for a data centric programming model
Our evaluation shows:
  Up to 10% reduction in Energy/Mbytes with negligible performance penalty
  Up to 50% of achievable improvement possible in our test-bed
  Approach should have greater impact on upcoming processor architectures

## Slide 20: Future Work
This is a part of active work:
  Exploring the interplay between Performance and Power
  Significant focus on applications
  Modeling of Performance / Power / Reliability in concert
  Looking at the co-design for future large-scale systems
Our thanks go to:
  eXtreme Scale Computing Initiative (XSCI) @PNNL
  US DOE Office of Science
  Energy Smart Data Center