## Slide 1: iWARP Redefined: Scalable Connectionless Communication Over High-Speed Ethernet
M. J. Rashti, R. E. Grant, P. Balaji and A. Afsahi

## Slide 2: PRESENTATION OUTLINE
Background
Motivation for a Datagram-based iWARP
Datagram-iWARP Design & Implementation
Experimental Results
Summary & Future Works
Notes: 2

## Slide 3: iWARP Ethernet Standard
Internet Wide-Area RDMA Protocol
  RDMA-enabled Ethernet
  Standardized by RDMA Consortium
Defined over Reliable Transports
  TCP and SCTP
Benefits over Traditional TCP/IP
  Low latency / high throughput
  Protocol offload: lower host CPU/bus utilization
  Zero-copy: lower latency and host CPU utilization
    Critical for servers
  User-level library: bypass OS involvement overhead
Message-oriented Protocol Stack

## Slide 4: Queue-pair Communication
CPU posts WRs to QP
RNIC performs data transfer asynchronously and are Zero-copy
Completion events are put in CQ for polling
WRs can be:
  Send
  Receive
  RDMA Write
  RDMA Read
Consumer CPU
Port
QP
send
recv
iWARP and TCP/IP Stack
data packet
WR
CQ
iWARP RNIC

## Slide 5: iWARP Stack compared to Host-based TCP/IP
User Applications
MPI,SDP, etc.
Verbs Interface
Socket Interface
RDMAP
DDP
MPA
TCP/IP
SCTP/IP
Ethernet Link Layer
Socket Buffer
Kernel Processing
Interrupt Handling
OS
TCP/IP proc.
NIC Hardware
Software
NIC Driver
RNIC Driver
NIC Hardware
Software

## Slide 6: PRESENTATION OUTLINE
Background
Motivation for a Datagram-based iWARP
Datagram-iWARP Design & Implementation
Experimental Results
Summary & Future Works
Notes: 6

## Slide 7: Motivation for Datagram-iWARP (1)
Widespread use of Ethernet:
  HPC Clusters (~50% of Top500)
  Data Services (media streaming, gaming, etc.)
    Extensively use Ethernet for intra- and inter-networking
  UDP-based Services and Applications
    Currently cannot utilize iWARP
  Datagrams Traffic Increase: 40% per year
    91% of Internet traffic by 2014 (according to Cisco)

## Slide 8: Motivation for Datagram-iWARP (2)
Memory-usage Scalability of iWARP
  Future systems will be much more memory-tight
  Connection memory usage is not scalable
    At NIC / HW layer
      Limited NIC cache need to utilize host memory
    At application library (MPI / socket) layer
      pre-allocated user- and/or kernel-level buffers
HW Complexity and Fabrication Cost
  UDP is much simpler to offload
  More room for offload-engine parallelism for multi-cores
  More room for more offloaded functionality
  For applications that only need datagrams

## Slide 9: Motivation for Datagram-iWARP (3)
Performance Issues of the Current iWARP
  TCP/SCTP performance barriers
    Reliability / Flow control
    Too much overhead for low-error-rate networks
  Marking (MPA layer) costs: required for TCP
Hardware-level Multicast and Broadcast
  Important for HPC and datacenters
  Not supported in TCP
  Can be efficiently supported in UDP

## Slide 10: PRESENTATION OUTLINE
Background
Motivation for a Datagram-based iWARP
Datagram-iWARP Design & Implementation
Experimental Results
Summary & Future Works
Notes: 10

## Slide 11: Datagram-iWARP: General Design at Different Layers
Verbs layer
Modify verbs & data structures to comply with datagram semantics.
Define datagram QPs & WRs
No streams/connections. No message segmentation. Use UDP sockets. Checksum moved here.
MPA layer is bypassed for datagrams.
Use UDP for UD QPs and lightweight reliable UDP for RD QPs.
RDMAP layer
DDP layer
MPA layer
Transport layer
(TCP/IP)

## Slide 12: Design Considerations (1)
Addition of New Queue-pair (QP) Types
  For reliable and unreliable datagrams
  Current iWARP does not have QP types
QP Operations
  QP Create: new input modifiers for datagram mode
  QP Modify: need a pre-established datagram socket for RTS state
Work Requests
  Need address-handles for individual datagrams
Completion of WRs
  As soon as accepted by LLP

## Slide 13: Design Considerations (2)
Completion Events
  Need to report the source information
Datagram Error Management (reliable mode)
  No connection to terminate
  QP goes into Error state
    Use MSN for notification into an “Error Queue”
  Re-use after resetting QP
MPA Layer Removed
  CRC moved to DDP layer
MTU-sized Message Segmentation
  Not required anymore
  Up to 64KB datagrams allowed

## Slide 14: Software-based Datagram iWARP
MVAPICH-hybrid with Reliability Settings
OF Verbs Interface
Native iWARP Verbs Interface
RDMAP Layer -RC & UD
DDP Layer - Untagged
MPA markers
TCP
UDP
Tuned Linux Kernel
Tuned Ethernet Link Layer
Extended for SW Datagram-iWARP
Extended for SW Datagram-iWARP
Developed for SW iWARP
Adapted to run over SW iWARP
Tuned for best performance
of MPI over SW Datagram iWARP

## Slide 15: Software Implementation
Based on the OSC SW-iWARP (TCP-based)
New Native Verbs to Support Datagrams
Implementing Standard OF-verbs
  On top of UDP- and TCP-based native verbs
  No new verbs at this layer
Using IO-Vectors for Low-latency SW-based Datagram Transfer
Utilizing UDP Offload-engine
  Large Receive Offload
  UDP checksum (optional)

## Slide 16: PRESENTATION OUTLINE
Background
Motivation for a Datagram-based iWARP
Datagram-iWARP Design & Implementation
Experimental Results
Summary & Future Works
Notes: 16

## Slide 17: Experimental Platform
Platform | Nodes | Processor | Memory/ Cache | Network | OS/ Software
C1 | 4 | Two quad-core 2GHz Opteron | RAM: 8GB L3: 8MB L2: 512K | NIC: NetEffect 10GE Switch: Fujitsu 10GE | Fedora 12/ MVAPICH 1.1
C2 | 16 | Two dual-core 2.8GHz Opteron | RAM: 4GB L2: 1MB | NIC: Myricom 10GE Switch: Fulcrum 10GE | Ubuntu/ MVAPICH 1.1

## Slide 18: Verbs-level Latency - Small Messages

## Slide 19: Verbs-level Latency - Medium Messages

## Slide 20: Verbs-level Latency - Large Messages

## Slide 21: MPI-level Latency – Small Messages

## Slide 22: MPI-level Latency – Medium Messages

## Slide 23: MPI-level Latency - Large Messages

## Slide 24: MPI Micro-benchmark Bandwidth Results

## Slide 25: Application Performance Improvement (I)
Application
Communication-time
Improvement
exceeding 40% for Radix

## Slide 26: Application Performance Improvement (II)
Application Runtime
Improvement
exceeding 45% for
SMG2000

## Slide 27: Application Memory-usage Reduction
Memory usage decrease
exceeding 30% for Radix
High savings for SMG, Radix which have complete connection graphs
Scalable improvement
trend
For both performance
and memory usage:
  C2 cluster results are
  better than C1 cluster

## Slide 28: PRESENTATION OUTLINE
Background
Motivation for a Datagram-based iWARP
Datagram-iWARP Design & Implementation
Experimental Results
Summary & Future Works
Notes: 28

## Slide 29: Summary
Proposed extension of iWARP over Datagrams
  Over UDP (reliable & unreliable)
Implemented Untagged Model (send/recv) in Software
  OF-verbs over SW Datagram-iWARP
  MPI over OF-verbs using Datagram-iWARP
Results
  Significant application memory usage reduction
  High application performance increase
  The benefits scale up with more #processes

## Slide 30: Conclusions
Datagram-iWARP Complements the Current iWARP Standard
Extends Usability Domain of iWARP Standard
  Can serve datagram-based applications
  For both HPC and datacenter systems
Improves Performance
Offers Higher Scalability
  Lower memory usage
  Lower fabrication cost & power consumption
    If implemented in HW

## Slide 31: Future Directions
Tagged (RDMA Read/Write) Model
  Define unreliable RDMA operations over UD
  Integrate with socket-based applications
    To appear in IPDPS 2011
  Integrate with MPI
    To be completed soon
Port Datagram-iWARP over Reliable UDP
  No need for reliability at MPI layer
  Much lighter weight than TCP/SCTP
Standardization of Datagram-iWARP

## Slide 32: Acknowledgement

## Slide 34: Extra Slides

## Slide 35: Related Work
OSC Software iWARP (TCP-based)
  Kernel-level
  User-level: the base of our work
IBM Zurich SoftRDMA
  SW iWARP stack for OFED package
Myricom MX over Ethernet
InfiniBand over Ethernet
RDMA over CEE
Notes: iWARP and RDMAoE are in fact competing technologies, but iWARP is a more mature standard. It supports features such as WAN (IP), not supported in RDMAoE. Datagram-based applications which need IP compatibility cannot use RDMAoE and are currently unable to utilize iWARP either. Datagram iWARP will also be a more economical alternative to an IB based transport over Ethernet (i.e. RDMAoE). Considering these benefits, our paper is focused on increasing the scalability of iWARP, making it more suitable for both HPC and data centers.

## Slide 36: iWARP Protocol Stack
Verbs: a set of descriptive user-level interfaces
  User-level: bypass OS
RDMAP: supplies communication primitives for verbs layer
  Send/Recv, RDMA Write, RDMA Read
  QP-based semantics
DDP: directly transfers data between the user buffer and the RNIC
without intermediate buffering
MPA: inserts markers to distinguish iWARP messages in TCP stream

## Slide 37: RDMA Technology – Zero copy
User Buffer
User Buffer
CPU
CPU
NIC
NIC
Kernel Buffer
Kernel Buffer
RDMA
RDMA
DMA
DMA
Data Source
Data Sink