## Slide 1: A Study of Hardware Assisted IP over InfiniBand and its Impact on Enterprise Data Center Performance
Ryan E. Grant1, Pavan Balaji2, Ahmad Afsahi1
1Department of Electrical and Computer Engineering
Queen’s University Kingston, ON, Canada K7L 3N6
2Mathematics and Computer Science
Argonne National Laboratory
Argonne, IL, USA

## Slide 2: Introduction
Motivation
Background Information
Experimental Framework
Experimental Results
  Baseline Performance
  Offloading Performance
  Data Center Performance Results
  Performance Bottleneck Investigation
  Validation
Conclusions
  Future Work
Questions

## Slide 3: Motivation
Sockets-based protocols are used extensively in enterprise data centers
IPoIB provides a high performance socket interface that does not rely on upper layer protocol support (such as TCP)
Future convergence of networking fabrics, will use elements of InfiniBand and Ethernet
Behaviour and performance of such systems is important to study in order to guide the development and installation of advanced networking technologies

## Slide 4: Motivation
Why is UD/RC offloading important?
  Its new to IPoIB (UD offloading)
  It narrows the performance gap between IPoIB-UD and Sockets Direct Protocol (SDP)
  UD offloading allows us to effectively use software that does not utilize TCP (TCP is required for SDP)

## Slide 5: Outline
Motivation
Background Information
Experimental Framework
Experimental Results
  Baseline Performance
  Offloading Performance
  Data Center Performance Results
  Performance Bottleneck Investigation
  Validation
Conclusions
  Future Work
Questions

## Slide 6: Background Information
InfiniBand
  Queue Pair Operation, supporting RDMA and send/receive modes
  Mellanox ConnectX host channel adapters support 4x InfiniBand operation
    Bandwidth of 40 Gigabit/s (32 Gigabits/s data)
  The OpenFabrics Enterprise Software Distribution (OFED-1.4) (InfiniBand drivers) supports both SDP and IPoIB protocols

## Slide 7: Background Information
Socket-based protocols provide IP functionality, using IP over IB (IPoIB)
  IPoIB provides Large receive offload (LRO) and Large send offload (LSO)
  Large receive offload aggregates incoming packets
  Large send offload segments large messages into appropriate packet sizes in hardware
Sockets Direct Protocol (SDP) provides RDMA capabilities
  Bypasses the operating system’s TCP/IP stack
  Utilizes hardware flow control, offloaded network and transport stack in addition to RDMA
  Operates in buffered-copy and zero-copy modes

## Slide 8: Background Information

## Slide 9: Background Information
InfiniBand operates in several modes:
  Reliable Connection (RC): Keeps traditional connections while offering low level reliability and in order delivery
  Unreliable Datagram (UD): non-connection based datagram transmission, with no reliability
IB is capable of RDMA, which is utilized for socket interfaces through the SDP API which replaces TCP programming semantics
Additional IB modes: unreliable connection and reliable datagram, do not currently have hardware offloading implementations

## Slide 10: Outline
Motivation
Background Information
Experimental Framework
Experimental Results
  Baseline Performance
  Offloading Performance
  Data Center Performance Results
  Performance Bottleneck Investigation
  Validation
Conclusions
  Future Work
Questions

## Slide 11: Experimental Framework
OS | Processors | InfiniBand HCA | Switch | OFED version
Fedora Kernel 2.6.27 | 2 – 2.0 Ghz Quad-Core AMD Opteron | ConnectX 4X DDR HCA Firmware: 2.6.11 | Mellanox 24-port MT47396 Infiniscale-III | 1.4
Network performance data was collected using Netperf-2.4.4
Performance was validated using iperf-2.0.4

## Slide 12: Baseline Performance Results
  As expected Verbs RDMA and SDP (RDMA) show major latency advantages for small messages over IPoIB

## Slide 13: Baseline Multi-Stream Performance
The use of multiple streams for IPoIB shows good performance for IPoIB-RC/UD while IPoIB RC/UD and SDP Buffered copy are comparable

## Slide 14: Offloading Performance
IPoIB-UD with offloading provides similar latency to that of IPoIB-RC

## Slide 15: Offloading Performance
Although IPoIB-UD offloading outperforms non-offloaded IPoIB-UD, the single stream is still outperformed by IPoIB-RC

## Slide 16: Offloading Performance
With multiple streams, IPoIB-UD-LRO-LSO outperforms IPoIB-RC, and greatly outperforms non offloaded IPoIB-UD

## Slide 17: Offloading Performance
Offloaded IPoIB-UD provides a 85.1% improvement in bandwidth over non-offloaded IPoIB-UD
Offloaded IPoIB-UD outperforms Multi-stream IPoIB-RC by 7.1%, and provides similar latency
Offloaded IPoIB-UD provides bandwidth only 6.5% less than that of SDP

## Slide 18: Data Center Performance

## Slide 19: Data Center Performance
Data center throughput shows IPoIB-UD-LRO-LSO to maintain the highest level of throughput, while SDP is unexpectedly the worst performer of the group
Notes: Similar patterns on all results except for CG

## Slide 20: Data Center Performance
IPoIB-UD-LRO-LSO
IPoIB-RC
IPoIB-UD-noLRO-noLSO
SDP

## Slide 21: Data Center Performance
IPoIB-UD-LRO-LSO provides the highest sustained bandwidth of all of the protocols, beating non-offloaded IPoIB-UD by 15.4% and IPoIB-RC by 5.8% and SDP by 29.1%
IPoIB-UD-LRO-LSO provides similar response time to its nearest competitor, IPoIB-RC
All of the IPoIB configurations provide higher bandwidth than SDP

## Slide 22: Performance Bottleneck Investigation
SDP shows poor throughput and latency, much worse than would be initially expected
Given the excellent performance of SDP at the micro-benchmarks level, several tests were conducted to determine the cause of SDP’s poor performance in the data center test
It was determined that the large number of simultaneous connections were causing poor performance with SDP
The number of connections used by the SDP data center were reduced while increasing the activity level of each connection to confirm this analysis

## Slide 23: Performance Investigation
The resulting performance of SDP (with 50 connections) is increased greatly to a level that is more inline with expectations

## Slide 24: Performance Investigation
SDP delay - with many connections
SDP delay - with fewer connections

## Slide 25: Performance Validation
IPoIB and SDP show similar performance results on SPECWeb as were seen using the TPC-W benchmarks

## Slide 26: Performance Validation
SPECWeb response time results show IPoIB-UD-LRO-LSO to have the overall lowest response times

## Slide 27: Outline
Motivation
Background Information
Experimental Framework
Experimental Results
  Baseline Performance
  Offloading Performance
  Data Center Performance Results
  Performance Bottleneck Investigation
  Validation
Conclusions
  Future Work
Questions

## Slide 28: Conclusions
Micro-benchmarks have shown a 85.1% improvement in bandwidth of offloaded IB-UD over the non-offloaded case and a 26.2% maximum reduction in latency
Offloaded IPoIB-UD shows a 15.4% improvement in throughput over non offloaded IPoIB-UD
IPoIB-UD-LRO-LSO has a 29.1% higher throughput than SDP in our data center testing
The benefits of using IPoIB-RC are minimal over those of IPoIB-UD when utilizing offloading capabilities
Therefore, for future networks such as CEE the inclusion of a reliable connection mode is most likely unnecessary

## Slide 29: Future Work
Resolving the issues holding back SDP performance when using large numbers of connections
Utilizing Quality of Service to further enhance enterprise data center performance
Combining IPoIB-UD, QoS and Virtual Protocol Interconnect to improve overall data center performance

## Slide 30: Questions?
Thank You
Questions?