## Slide 1: Mapping Communication Layouts to Network Hardware Characteristics on Massive-Scale Blue Gene Systems
Pavan Balaji*, Rinku Gupta*, Abhinav Vishnu+ and Pete Beckman*
* Argonne National Laboratory
+ Pacific Northwest National Laboratory

## Slide 2: Power and Cost Constraints on Large-scale Machines
Massive scale machines available today
  Machines with 500,000 cores already available
  Upcoming machines expected to have a few million cores (e.g., the Sequoia BG/Q machine at LLNL is expected to have 1.6 million cores)
  Exascale machines might have close to a billion cores
For machines of this scale, it is impractical to assume that all system resources will increase at the same rate
  Caches, memory, floating point units, instruction decoders
Network is no exception:
  Many of the largest machines in the world are moving away from fat-tree topologies to “scalable” topologies (typically torus topologies)
    Lesser bisection bandwidth, but linearly increasing cost

## Slide 3: Scalable Network Topologies
Many of the largest machines in the world are increasingly using linearly scaling topologies
  IBM BG/L, BG/P and Cray XT machines utilized a 3D torus topology
  Sandia RedSky InfiniBand cluster uses a 3D topology
  IBM Blue Gene/Q will feature a 5D torus topology
  The Japanese K supercomputer uses a 6D torus
Impact on communication:
  Limited bisection bandwidth: Each node on a 3D torus connects directly to six other nodes
    Forcing nodes to share network links during communication
    Results in significant communication contention and performance loss
Locality of communication is absolutely critical for efficient usage of the network infrastructure  these networks are not at all well suited for random communication between all processes in the system

## Slide 4: Locality Aware Process Mapping
Communication locality requires information about the application communication pattern and hardware topology
Traditional approach involves using the MPI virtual topology functionality, but unused for several reasons including lack of data locality
  MPI virtual topology functions do not remap processes; instead they let the user create a new communicator with the appropriate communication characteristics
  What happens to the data that is already present on the processes? Applications have to manually redistribute it to match the new communicator’s rank ordering

## Slide 5: Data Layout Example for Domain-based Ray Tracing
Preprocessing step typically involves the application breaking the data into a regular Cartesian grid (and in some cases data exchange in a star stencil format)
Actual communication follows the processes that contain data on a given ray  the tracing library has to use the data layout given by the application which does not follow locality constraints to improve communication
Many other examples of such non-trivial communication patterns exist (box-stencil computations in many math libraries, dimension-wise communication in P3DFFT, etc.)

## Slide 6: State of Practice
The key issue that needs to be addressed is that the data layout (which process has what data) is independent of and thus does not match the communication pattern
Currently application developers tediously try out different process layouts and decide on the best layout
  This is impractical in many cases
    BG/P’s 3D torus requires a large number of “trial runs” for each application developer to converge on a good mapping
    BG/Q’s 5D torus is going to be a nightmare; try the 6D torus on the K-supercomputer
  … and impossible in other cases
    The best mapping many times depends on the actual partition layout in an allocation (8 x 8 x 8 is very different from 8 x 16 x 4)

## Slide 7: This paper in a nutshell
Basic idea is to perform process mapping at application launch time, rather than within the MPI library
  This allows the data placement to match the communication pattern of the applications
How this works:
  Application specifies the communication pattern it wants to use offline
  We allocate a partition of nodes for the application
  We study different process layouts and the amount of contention they are expected to have
  Pick the best layout and launch processes so as to minimize contention
We demonstrate that different mappings can show significant difference in overall performance for real applications on up to 128K cores of the Argonne BG/P system

## Slide 8: Presentation Roadmap
Motivation
Understanding the Complexity in Process Mapping
Contention Analysis
Experiments and Analysis
Concluding Remarks

## Slide 9: Complexity in Process Mapping
Most communication libraries (like MPI) hide physical layout of system from applications to improve portability
Applications form logical topologies on the processes available to match their problem
  E.g: for climate modeling applications, data representation is typically 2D plane, 3D volume or multi-dimensional unstructured grid
  Each process gets a part of the overall data
  Local data computation depends on partially evaluated results from neighboring processes on the logical process grid formed by application
Applications rely on the logical process layout without any information about the physical placement or mapping of actual processes

## Slide 10: 1D Mapping for nearest neighbor communication on BG/P
Easiest scenario: For 1D logical nearest neighbor, most of application processes will get mapped next to each other in a sequential order
Logical Mapping
Physical Mapping (XYZ)
8 x 8 x 8 physical grid
X
Z
Y
Physical Mapping (YXZ)
8 x 8 x 8 physical grid
Z
X
Y

## Slide 11: 2D mapping for nearest neighbor communication
In 2D mapping, each process communicates with 8 other processes. Communicating groups are dispersed -> network overlap
Mapping type impacts extent of dispersal (XYZ < YXZ below)
Logical Mapping
Physical Mapping (XYZ)
8 x 16 x 8 grid
Physical Mapping (YXZ)
8 x 16 x 8 grid

## Slide 12: 3D mapping for nearest neighbor communication
In 3D mapping, each process communicates with 26other processes. Mapping type significantly impact dispersal rate
Logical Mapping
Physical Mapping (XYZ)
8 x 16 x 8 grid
Physical Mapping (XZY)
8 x 16 x 8 grid

## Slide 13: Presentation Roadmap
Motivation
Understanding the Complexity in Process Mapping
Contention Analysis
Experiments and Analysis
Concluding Remarks

## Slide 14: Assumptions/Restrictions
We only consider symmetric topologies
  BG/P (and the upcoming BG/Q) only support symmetric allocations
  Cray XT and Sandia RedSky (IB) do not
We only consider symmetric communication patterns
  This simplifies the routing analysis as described in the later slides
  Irregular communication patterns exist in many applications and are very important, but is not the focus of this paper
The possible mappings we consider are restricted by the ones supported by the BG/P software stack
  Process management framework of BG/P allows application processes to be mapped in several combination of X,Y,Z axis and T (i.e. 4 cores per node – which can be considered as 4th dimension)
  IBM does not support all mappings; we did not make an attempt to improve this as finding an optimal mapping is NP-complete

## Slide 15: Communication Contention Analysis
Aim is to provide a methodology for analyzing different communication patterns of applications and mapping them optimally on a given platform for best performance
  Understand the communication pattern of the application by allowing the application to describe it
  Understand the physical platform network topology and the routing algorithm behavior on the platform
  Map these two categories of information to calculate the network contention for the given application pattern on the available network
  Application communication pattern and its optimal mapping can then be integrated with the IBM BG/P launching system (our chosen platform)
  Application, can then, simply specify their pattern during job submission time and optimal mapping will be automatically chosen by the run-time

## Slide 16: Routing on BG/P
Our contention analysis model relies on routing algorithm used by BG/P
BG/P routes data in dimension-wide order
  For large messages, BG/P uses destination-based adaptive routing
  To avoid live-locks, BG/P picks one of the minimum distance routes
    At each hop, the adaptive routing algorithm considers only the outgoing links that reduce hop count to destination
  As a first-order approximation, we assume data packets are split equally among all possible paths at each hop of the network
    Though not theoretically guaranteed, this is quite true in practice, but only for symmetric communication patterns (and hence our assumption that the communication pattern is symmetric)
  Every partition on the BG/P is fully symmetric and form a torus on all dimensions

## Slide 17: Intuition for Calculating Contention (TXYZ mapping)
To analyze optimal mapping for a given application and physical topology, we need to understand the network contention due to shared links
Map 64 x 256 2D grid on a 4,096 nodes on a BG/P system – with partition dimensions 8 x 16 x32
32
16
64 x 256 2D
Process Grid
8
TXYZ mapping: Each 64 row of the process grid occupies 4 ‘X’ rows
Each link is utilized 3 times by 1 center node
Total contention count: 24

## Slide 18: Intuition for Calculating Contention (TZYX mapping)
32
16
64 x 256 2D
Process Grid
8
TZYX mapping: Each 64 row of the process grid occupies 1 ‘Z’ row
Each link is utilized 3 times by 1 center node
Total contention count: 6
To analyze optimal mapping for a given application and physical topology, we need to understand the network contention due to shared links
Map 64 x 256 2D grid on a 4,096 nodes on a BG/P system – with partition dimensions 8 x 16 x32

## Slide 19: Calculating Contention
Calculate link usage for each peer communication
  For each pair of processes, see how much data is sent over each link
  The link with the maximum amount of data communication is our bottleneck and represents our measure of contention
    Note that this is only valid when all processes communicate with their peers at the same time, but that is the common model applications use and is what this paper focuses on
  Requires O(P2) computation with O(P) storage
For symmetric communication, however, this can be done in close to O(P) time
  This is because of the similarity in link usage between processes
  Data communication over links is similar, but shifted by one hop

## Slide 20: Presentation Roadmap
Motivation
Understanding the Complexity in Process Mapping
Contention Analysis
Experiments and Analysis
Concluding Remarks

## Slide 21: Experiments and Analysis
Study and analyze the impact of various mappings with varying system size
  Micro-benchmarks
  Applications
Demonstrates the performance achieved by our automatic process mapping model

## Slide 22: Micro-benchmark-based Evaluation
2D logical nearest neighbor communication
3D logical nearest neighbor communication
  Both use star stencils  each process has (3d-1) neighbors, where d is logical process grid dimensionality
Nearest neighbor communication
  Each process does point-to-point exchange of some data with its logical neighbors in 2D or 3D plane
  In real applications, this data (typically) corresponds to ghost cells, bordering data points between two processes
Studied effects of varying data size on up to 128K cores with various mappings

## Slide 23: 2D Communication benchmark performance
Chart: 16K cores
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1K | 2K | 4K | 8K | 16K | 32K | 64K | 128K | 256K | 512K | 1MB
TXYZ | 53.713 | 36.74 | 36.598 | 37.756 | 37.99 | 37.859 | 38.865 | 41.508 | 78.486 | 110.828 | 175.271 | 402.968 | 742.294 | 1369.617 | 2613.221 | 4996.153 | 9718.499 | 19067.514 | 37661.589 | 74259.774 | 147237.19
TZXY | 53.633 | 36.691 | 36.744 | 37.808 | 38.033 | 37.951 | 38.885 | 41.505 | 50.701 | 53.903 | 62.035 | 105.604 | 173.924 | 312.014 | 588.713 | 1143.99 | 2253.27 | 4460.155 | 8864.464 | 17660.92 | 35257.259
TYZX | 53.678 | 36.813 | 36.664 | 37.791 | 38.025 | 37.85 | 38.862 | 41.465 | 52.29 | 63.797 | 96.354 | 177.175 | 323.883 | 616.535 | 1207.207 | 2375.378 | 4736.713 | 9427.989 | 18869.275 | 37499.239 | 75170.134
XYZT | 54.834 | 36.424 | 35.553 | 36.055 | 36.601 | 36.27 | 37.273 | 39.422 | 49.303 | 54.114 | 71.616 | 132.859 | 235.362 | 435.38 | 839.737 | 1648.903 | 3280.599 | 6530.64 | 13034.229 | 26065.855 | 52174.086
CDL | 53.633 | 36.424 | 35.553 | 36.055 | 36.601 | 36.27 | 37.273 | 39.422 | 49.303 | 53.903 | 62.035 | 105.604 | 173.924 | 312.014 | 588.713 | 1143.99 | 2253.27 | 4460.155 | 8864.464 | 17660.92 | 35257.259
Chart: 32K cores
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1K | 2K | 4K | 8K | 16K | 32K | 64K | 128K | 256K | 512K | 1MB
TXYZ | 53.322 | 36.368 | 36.257 | 37.384 | 37.751 | 37.762 | 38.721 | 41.408 | 77.586 | 109.574 | 173.595 | 388.487 | 720.137 | 1337.51 | 2541.106 | 4916.382 | 9572.924 | 18702.302 | 36994.183 | 73003.745 | 145371.196
TZXY | 53.324 | 36.457 | 36.408 | 37.427 | 37.813 | 37.779 | 38.719 | 41.399 | 52.237 | 64.116 | 97.031 | 194.873 | 353.756 | 655.14 | 1254.822 | 2450.423 | 4857.745 | 9662.077 | 19261.257 | 38497.613 | 76903.764
TYZX | 53.246 | 36.418 | 36.282 | 37.348 | 37.802 | 37.737 | 38.686 | 41.376 | 52.186 | 63.573 | 96.124 | 176.257 | 323.011 | 616.076 | 1200.605 | 2358.713 | 4713.452 | 9366.931 | 18710.974 | 37410.85 | 74759.747
XYZT | 62.412 | 47.554 | 46.044 | 46.384 | 46.418 | 46.824 | 61.832 | 93.267 | 353.626 | 505.628 | 817.952 | 1730.858 | 3203.075 | 5886.558 | 11123.691 | 21595.854 | 42770.743 | 85056.211 | 169335.121 | 338641.262 | 676190.53
CDL | 53.246 | 36.368 | 36.257 | 37.348 | 37.751 | 37.737 | 38.686 | 41.376 | 52.186 | 63.573 | 96.124 | 176.257 | 323.011 | 616.076 | 1200.605 | 2358.713 | 4713.452 | 9366.931 | 18710.974 | 37410.85 | 74759.747
7-fold performance difference 
due to increased contention count, O(N) link increase but O(N2) process increase
CDL model picks most optimal mapping

## Slide 24: 3D Communication benchmark performance
Chart: 16K cores
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1K | 2K | 4K | 8K | 16K | 32K | 64K | 128K | 256K | 512K | 1MB
TXYZ | 115.788 | 115.09 | 115.396 | 114.5 | 115.018 | 116.426 | 121.543 | 126.986 | 434.508 | 656.147 | 1067.522 | 1259.391 | 2228.146 | 4018.404 | 7870.335 | 15966.537 | 33002.313 | 67912.472 | 138496.018 | 281213.839 | 568835.433
TZXY | 116.136 | 115.897 | 115.497 | 115.456 | 116.455 | 117.289 | 120.784 | 124.966 | 186.084 | 254.527 | 402.88 | 684.429 | 1233.084 | 2253.092 | 4322.606 | 8499.85 | 16923.631 | 33770.763 | 67454.025 | 134811.583 | 269670.784
TYZX | 115.439 | 116.172 | 115.246 | 115.36 | 115.731 | 117.423 | 121.206 | 124.903 | 168.1 | 206.887 | 323.094 | 600.691 | 1036.934 | 1873.494 | 3592.767 | 7084.313 | 14152.913 | 28284.4 | 56544.931 | 113111.514 | 226139.734
XYZT | 137.493 | 135.65 | 135.519 | 135.517 | 135.819 | 136.187 | 181.586 | 280.608 | 1019.125 | 1444.801 | 2315.636 | 5236.601 | 9340.538 | 16708.184 | 31717.543 | 62167.021 | 123884.414 | 247030.941 | 496528.233 | 993302.664 | 1989504.156
CDL | 115.439 | 115.09 | 115.246 | 114.5 | 115.018 | 116.426 | 120.784 | 124.903 | 168.1 | 206.887 | 323.094 | 600.691 | 1036.934 | 1873.494 | 3592.767 | 7084.313 | 14152.913 | 28284.4 | 56544.931 | 113111.514 | 226139.734
Chart: 32K cores
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1K | 2K | 4K | 8K | 16K | 32K | 64K | 128K | 256K | 512K | 1MB
TXYZ | 117.226 | 116.537 | 115.897 | 115.267 | 116.014 | 117.657 | 122.392 | 125.709 | 199.966 | 283.795 | 464.492 | 633.395 | 1174.859 | 2218.681 | 4333.865 | 8664.608 | 17501.486 | 35222.865 | 70652.843 | 141374.721 | 283323.022
TZXY | 117.259 | 117.271 | 115.596 | 115.464 | 116.837 | 118.359 | 122.242 | 126.14 | 182.35 | 243.674 | 386.452 | 664.308 | 1210.898 | 2235.594 | 4297.907 | 8447.356 | 16869.795 | 33685.262 | 67336.422 | 134646.483 | 269471.621
TYZX | 117.42 | 117.829 | 116.207 | 115.805 | 116.848 | 118.268 | 121.954 | 126.26 | 163.96 | 177.191 | 216.657 | 398.566 | 713.56 | 1323.555 | 2557.141 | 5033.751 | 10024.16 | 19960.307 | 39829.986 | 79548.742 | 159029.937
XYZT | 120.894 | 117.262 | 116.7 | 116.666 | 116.854 | 117.752 | 142.45 | 220.32 | 1014.758 | 1512.834 | 2803.693 | 3043.716 | 5469.899 | 10625.968 | 24357.762 | 53957.81 | 121509.84 | 267247.947 | 574498.754 | 1244053.837 | 2589089.073
CDL | 117.226 | 116.537 | 115.596 | 115.267 | 116.014 | 117.657 | 121.954 | 125.709 | 163.96 | 177.191 | 216.657 | 398.566 | 713.56 | 1323.555 | 2557.141 | 5033.751 | 10024.16 | 19960.307 | 39829.986 | 79548.742 | 159029.937
Performance difference
Increases with system size
Increases with message size
Same trends as 2D communication benchmarks

## Slide 25: Application kernel evaluation – P3DFFT
P3DFFT: A popular implementation of parallel 3D FFT algorithm to compute Fast Fourier transform, when applied to 3D volume space
  Computing 1D Fourier transform in each of the 3 dimensions
Communication pattern is dimension-wise
  That is, each process communicates with all processes in its X and Y (logical) dimensions
  Each process communications with √P processes

## Slide 26: P3DFFT performance
Chart: 512 - 8K cores
| 512 | 1K | 2K | 4K | 8K
TXYZ | 1057.9938 | 614.3949 | 230.188 | 128.7595 | 87.0333
TZXY | 1071.727 | 613.3299 | 230.1447 | 128.2207 | 82.768
TYZX | 1060.9883 | 554.9164 | 230.0394 | 131.4203
XYZT | 1069.1671 | 627.9478 | 239.9241 | 135.1656 | 87.5069
CDL | 1060.9883 | 554.9164 | 230.0394 | 131.4203
Chart: 8K – 64K cores
| 16K | 32K | 64K
TXYZ | 44.9877 | 23.9591 | 15.5687
TZXY | 48.0863 | 31.2092 | 19.4637
TYZX | 31.2855 | 19.6822
XYZT | 51.8288 | 31.6206 | 19.2315
CDL | 44.9877 | 23.9591 | 15.5687

## Slide 27: NLOM Ocean Modeling Application
NLOM application is used for ocean simulations; with focus on semi-enclosed seas, ocean basins and the global ocean
Bandwidth sensitive when run on large system size
We study it with varying system size and message size

## Slide 28: NLOM Communication Performance
Chart: 16K cores
| 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1K | 2K | 4K | 8K | 16K | 32K | 64K | 128K | 256K | 512K | 1MB
TXYZ | 2.2e-05 | 2.3e-05 | 2.4e-05 | 2.7e-05 | 5.6e-05 | 8.2e-05 | 0.000141 | 0.00028 | 0.000539 | 0.001016 | 0.001983 | 0.003955 | 0.007967 | 0.016168 | 0.033259 | 0.067066 | 0.13583 | 0.27897 | 0.59859 | 1.1678
TZXY | 2.2e-05 | 2.3e-05 | 2.3e-05 | 2.6e-05 | 3.3e-05 | 4.6e-05 | 7.1e-05 | 0.000143 | 0.000256 | 0.000482 | 0.000924 | 0.001815 | 0.003577 | 0.007158 | 0.014506 | 0.029177 | 0.059219 | 0.1196 | 0.24346 | 0.51157
TYZX | 2.2e-05 | 2.3e-05 | 2.3e-05 | 2.6e-05 | 3.3e-05 | 4.6e-05 | 7e-05 | 0.000142 | 0.000241 | 0.000451 | 0.000871 | 0.001714 | 0.00341 | 0.006801 | 0.013651 | 0.027482 | 0.055329 | 0.11175 | 0.22428 | 0.45398
XYZT | 2.2e-05 | 2.3e-05 | 2.3e-05 | 2.6e-05 | 3.2e-05 | 4.3e-05 | 6.4e-05 | 0.00014 | 0.000224 | 0.000423 | 0.000822 | 0.001628 | 0.003264 | 0.006561 | 0.013228 | 0.026638 | 0.053581 | 0.10757 | 0.2154 | 0.43081
CDL | 2.2e-05 | 2.3e-05 | 2.3e-05 | 2.6e-05 | 3.2e-05 | 4.3e-05 | 6.4e-05 | 0.00014 | 0.000224 | 0.000423 | 0.000822 | 0.001628 | 0.003264 | 0.006561 | 0.013228 | 0.026638 | 0.053581 | 0.10757 | 0.2154 | 0.43081
Chart: 32K cores
| 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1K | 2K | 4K | 8K | 16K | 32K | 64K | 128K | 256K | 512K | 1MB
TXYZ | 2.2e-05 | 2.3e-05 | 2.4e-05 | 2.6e-05 | 3.8e-05 | 5.4e-05 | 8.6e-05 | 0.00018 | 0.000325 | 0.000603 | 0.00116 | 0.002284 | 0.00455 | 0.009085 | 0.018241 | 0.037042 | 0.075027 | 0.15548 | 0.31695 | 0.66168
TZXY | 2.2e-05 | 2.3e-05 | 2.4e-05 | 2.6e-05 | 3.8e-05 | 5.4e-05 | 8.6e-05 | 0.00018 | 0.000324 | 0.000602 | 0.001156 | 0.002271 | 0.004531 | 0.009053 | 0.018217 | 0.036795 | 0.075315 | 0.15327 | 0.3181 | 0.66734
TYZX | 2.2e-05 | 2.3e-05 | 2.4e-05 | 2.6e-05 | 3.8e-05 | 5.4e-05 | 8.5e-05 | 0.000176 | 0.000313 | 0.00059 | 0.001153 | 0.002299 | 0.004605 | 0.00918 | 0.018533 | 0.03784 | 0.0771 | 0.16102 | 0.3319 | 0.68815
XYZT | 2.4e-05 | 2.4e-05 | 2.6e-05 | 3.3e-05 | 7.7e-05 | 0.000143 | 0.000226 | 0.00045 | 0.001084 | 0.001917 | 0.003446 | 0.00662 | 0.013136 | 0.026267 | 0.052812 | 0.10618 | 0.21477 | 0.42871 | 0.85261 | 1.7449
CDL | 2.2e-05 | 2.3e-05 | 2.4e-05 | 2.6e-05 | 3.8e-05 | 5.4e-05 | 8.5e-05 | 0.000176 | 0.000313 | 0.00059 | 0.001153 | 0.002299 | 0.004605 | 0.00918 | 0.018533 | 0.03784 | 0.0771 | 0.16102 | 0.3319 | 0.68815
3-fold performance difference
CDL model does pick most optimal mapping

## Slide 29: NLOM trends on varying system size
Chart: 8KB message size
| 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1K | 2K | 4K | 8K | 16K | 32K | 64K | 128K
TXYZ | 0.003232 | 0.003233 | 0.004133 | 0.004041 | 0.003211 | 0.003242 | 0.004057 | 0.003267 | 0.003499 | 0.003499 | 0.004106 | 0.004614 | 0.007967 | 0.004558 | 0.00455
TZXY | 0.003232 | 0.003233 | 0.004235 | 0.004164 | 0.003205 | 0.003271 | 0.003273 | 0.003379 | 0.003557 | 0.002847 | 0.002847 | 0.002853 | 0.003577 | 0.003438 | 0.004531
TYZX | 0.003232 | 0.003233 | 0.004154 | 0.004147 | 0.003283 | 0.003322 | 0.004194 | 0.004234 | 0.003493 | 0.003399 | 0.004517 | 0.003391 | 0.00341 | 0.003405 | 0.004605
XYZT | 0.002554 | 0.002603 | 0.002826 | 0.002813 | 0.003154 | 0.004095 | 0.005052 | 0.004258 | 0.003269 | 0.003263 | 0.0038 | 0.003265 | 0.003264 | 0.013201 | 0.013136
CDL | 0.002554 | 0.002603 | 0.002826 | 0.002813 | 0.003154 | 0.003242 | 0.003273 | 0.003267 | 0.003269 | 0.002847 | 0.002847 | 0.002853 | 0.003264 | 0.003405 | 0.004531
Chart: 1MB message size
| 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1K | 2K | 4K | 8K | 16K | 32K | 64K | 128K
TXYZ | 0.40991 | 0.40988 | 0.53475 | 0.53549 | 0.4094 | 0.4106 | 0.55567 | 0.40955 | 0.47196 | 0.48496 | 0.58131 | 0.6563 | 1.1678 | 0.66077 | 0.66168
TZXY | 0.40993 | 0.40991 | 0.53979 | 0.55684 | 0.40934 | 0.42107 | 0.42059 | 0.41038 | 0.48049 | 0.36506 | 0.36508 | 0.36508 | 0.51157 | 0.47454 | 0.66734
TYZX | 0.40992 | 0.40982 | 0.54258 | 0.54809 | 0.42113 | 0.42092 | 0.56602 | 0.57193 | 0.45233 | 0.45476 | 0.66998 | 0.45393 | 0.45398 | 0.4559 | 0.68815
XYZT | 0.31897 | 0.31897 | 0.35542 | 0.35383 | 0.39061 | 0.5342 | 0.67281 | 0.5212 | 0.4308 | 0.4308 | 0.51966 | 0.43081 | 0.43081 | 1.7187 | 1.7449
CDL | 0.31897 | 0.31897 | 0.35542 | 0.35383 | 0.39061 | 0.4106 | 0.42059 | 0.40955 | 0.4308 | 0.36506 | 0.36508 | 0.36508 | 0.43081 | 0.4559 | 0.66168
No single mapping performs best in all cases
Mapping becomes more important with increasing system sizes

## Slide 30: Presentation Roadmap
Motivation
Understanding the Complexity in Process Mapping
Contention Analysis
Experiments and Analysis
Concluding Remarks

## Slide 31: Concluding Remarks
Locality aware process mapping is critical in large-scale systems
We studied how mappings can significantly impact application performance and designed a contention model analysis tool to identify the mapping with the least contention
Experiments done on 128K cores of BG/P demonstrate significant impact on performance
Future work: Non-symmetric communication patterns require improved analysis, but form a big fraction of applications

## Slide 32: Thank you!
Contact:
Email: balaji@mcs.anl.gov
Web: http://www.mcs.anl.gov/~balaji

## Slide 33: Argonne BG/P system Torus Dimensions
Application on BG/P are run on a subset of node i.e. partition
  Two different partitions can have the same number of cores; but have different partition dimensions
  For a 4,096 job, partitions of both 8 x 16 x 32 and 16 x 16 x 16 can be used
  Partition sizes can be configured by the administrator  determines network sharing
Nodes | Dimensions
512 | 8 x 8 x 8
1024 | 8 x 8 x 16
2048 | 8 x 8 x 32
4096 | 8 x 16 x 32
8192 | 8 x 32 x 32
16384 | 16 x 32 x 32
32768 | 32 x 32 x32