## Slide 1: Synchronization and Ordering Semantics in Hybrid MPI+GPU Programming
Ashwin M. Aji (Ph.D. Candidate), Wu-chun Feng (Virginia Tech)
Pavan Balaji, James Dinan, Rajeev Thakur (Argonne National Lab.)

## Slide 2: Accelerator-Based Supercomputers
Chart: Accelerator-Based System Share (out of 500)
| Jun 2009 | Nov 2009 | Jun 2010 | Nov 2010 | Jun 2011 | Nov 2011 | Jun 2012 | Nov 2012
With Accelerators | 5 | 7 | 9 | 17 | 19 | 39 | 58 | 62
Accelerator Vendors/Models
NVIDIA 2050/2070/2090/K20x
Intel Xeon Phi (MIC)
IBM PowerXCell 8i
AMD Firepro/Radeon
Notes: It is important to understand how the accelerators, such as GPUs, inter-operate with CPUs in cluster environments. How easy is it to program them? What will be the performance?

## Slide 3: Data Movement in CPU-GPU Clusters
GPU
device memory
GPU
device memory
CPU
main memory
CPU
main memory
PCIe
PCIe
Network
MPI Rank = 0
MPI Rank = 1
if(rank == 0)
{
GPUMemcpy(host_buf, dev_buf, D2H)
MPI_Send(host_buf, .. ..)
}
if(rank == 1)
{
MPI_Recv(host_buf, .. ..)
GPUMemcpy(dev_buf, host_buf, H2D)
}

## Slide 4: Data Movement in CPU-GPU Clusters
GPU
device memory
GPU
device memory
CPU
main memory
CPU
main memory
PCIe
PCIe
Network
MPI Rank = 0
MPI Rank = 1
int processed[chunks] = {0};
for(j=0;j<chunks;j++) { /* Pipeline */
cudaMemcpyAsync(host_buf+offset, gpu_buf+offset,
D2H, streams[j], ...);
}
numProcessed = 0; j = 0; flag = 1;
while (numProcessed < chunks) {
if(cudaStreamQuery(streams[j] == cudaSuccess)) {
/* start MPI */
MPI_Isend(host_buf+offset,...);
numProcessed++; processed[j] = 1;
}
MPI_Testany(...); /* check progress */
if(numProcessed < chunks) /* next chunk */
while(flag) {
j=(j+1)%chunks; flag=processed[j];
}
}
MPI_Waitall();
  Performance vs. Productivity tradeoff
  Multiple optimizations for different...
    …GPUs (AMD/Intel/NVIDIA)
    …programming models (CUDA/OpenCL)
    …library versions (CUDA v3/CUDA v4)

## Slide 5: Data Movement in CPU-GPU Clusters (e.g: MPI+CUDA)
int processed[chunks] = {0};
for(j=0;j<chunks;j++) { /* Pipeline data transfers */
cudaMemcpyAsync(host_buf+offset, gpu_buf+offset,
D2H, streams[j], ...);
}
numProcessed = 0; j = 0; flag = 1;
while (numProcessed < chunks) {
if(cudaStreamQuery(streams[j] == cudaSuccess)) {
MPI_Isend(host_buf+offset,...); /* start MPI */
numProcessed++; processed[j] = 1;
}
MPI_Testany(...); /* check progress */
if(numProcessed < chunks) /* find next chunk */
while(flag) {
j=(j+1)%chunks; flag=processed[j];
}
}
MPI_Waitall();
Sender’s Logic Only

## Slide 6: Intra-node Topology Awareness
Graphics Processing Units (GPUs)
  Many-core architecture
  Prog. Models: CUDA, OpenCL, OpenACC
  Explicitly managed global memory and separate address spaces
CPU clusters
  Most popular parallel prog. model: Message Passing Interface (MPI)
  Host memory only
Disjoint Memory Spaces!
Keeneland Node Architecture

## Slide 7: GPU-integrated MPI
GPU
device memory
GPU
device memory
CPU
main memory
CPU
main memory
PCIe
PCIe
Network
MPI Rank = 0
MPI Rank = 1
if(rank == 0)
{
MPI_Send(any_buf, .. ..)
}
if(rank == 1)
{
MPI_Recv(any_buf, .. ..)
}
  Examples: MPI-ACC, MVAPICH, Open MPI
  Programmability/Productivity: multiple accelerators and prog. models (CUDA, OpenCL)
  Performance: system-specific and vendor-specific optimizations (Pipelining, GPUDirect, pinned host memory, IOH affinity)

## Slide 8: Need for Synchronization
foo_blocking(buf_1);
/* No Sync Needed */
bar(buf_1);
foo_nonblocking(buf_1);
/* Sync Needed */
bar(buf_1);
foo_nonblocking(buf_1);
/* No Sync Needed */
bar(buf_2);

## Slide 9: Need for Synchronization in GPU-integrated MPI
if(rank == 0)
{
GPUExec(any_buf, ...);
MPI_Isend(other_buf, ...)
MPI_Send(any_buf, ...)
GPUMemcpy(any_buf, H2D);
MPI_Waitall();
}
if(rank == 1)
{
GPUMemcpy(other_buf, H2D);
GPUExec(other_buf, ...);
MPI_Recv(any_buf, ...)
GPUMemcpy(any_buf, H2D);
MPI_Isend(other_buf, ...);
}
  Interleaved MPI and GPU operations
  Dependent vs. Independent
  Blocking vs. Non-blocking

## Slide 10: Rest of this talk…
GPU-Integrated MPI
UVA-based
Attribute-based
With interleaved MPI and GPU operations, what are (or should be) the synchronization semantics?
  Explicit
  Implicit
How the synchronization semantics can affect performance and productivity?

## Slide 11: GPU-integrated MPI: UVA-based Design
What is UVA?
  Unified Virtual Addressing
Default case: Multiple Memory Spaces
UVA: Single Address Space
Source: Peer-to-Peer & Unified Virtual Addressing CUDA Webinar
http://on-demand.gputechconf.com/gtc-express/2011/presentations/cuda_webinars_GPUDirect_uva.pdf

## Slide 12: GPU-integrated MPI: UVA-based Design
void * for CPU or GPU0 or GPU1 or GPUn
cuPointerGetAttribute queries for the buffer type (CPU or GPUi)
Exclusive to CUDA v4.0+
UVA: Single Address Space
Source: Peer-to-Peer & Unified Virtual Addressing CUDA Webinar
http://on-demand.gputechconf.com/gtc-express/2011/presentations/cuda_webinars_GPUDirect_uva.pdf

## Slide 13: GPU-integrated MPI: UVA-based Design
  buf: CPU or GPU buffer
  MPI implementation can perform pipelining if it is GPU
  No change to MPI standard
if (my_rank == sender) { /* send from GPU (CUDA) */
MPI_Send(dev_buf, ...);
} else { /* receive into host */
MPI_Recv(host_buf, ...);
}
MPI_Send((void *)buf, count, MPI_CHAR, dest,
tag, MPI_COMM_WORLD);

## Slide 14: GPU-integrated MPI: Attribute-based Design
MPI_Send((void *)buf, count, MPI_CHAR, dest,
tag, MPI_COMM_WORLD);
MPI_Send((void *)buf, count, new_type, dest,
tag, MPI_COMM_WORLD);
  new_type: add attributes to inbuilt datatypes (MPI_INT, MPI_CHAR)
double *cuda_dev_buf; cl_mem ocl_dev_buf;
/* initialize a custom type */
MPI_Type_dup(MPI_CHAR, &type);
if (my_rank == sender) { /* send from GPU (CUDA) */
MPI_Type_set_attr(type, BUF_TYPE, BUF_TYPE_CUDA);
MPI_Send(cuda_dev_buf, type, ...);
} else { /* receive into GPU (OpenCL) */
MPI_Type_set_attr(type, BUF_TYPE, BUF_TYPE_OPENCL);
MPI_Recv(ocl_dev_buf, type, ...);
}
MPI_Type_free(&type);

## Slide 15: GPU-integrated MPI: Attribute-based Design
Extend inbuilt datatypes: MPI_INT, MPI_CHAR, etc.
Compatible with MPI
  Needs more setup code than UVA-based design
Compatible with many accelerator models
Highly extensible; lot of GPU-specific information passed into MPI
MPI_Type_dup(MPI_CHAR, &type);
MPI_Type_set_attr(type, BUF_TYPE, BUF_TYPE_CUDA);
MPI_Type_set_attr(type, DEVICE_ID, 1);
MPI_Type_set_attr(type, STREAM_OBJ, stream);
MPI_Type_set_attr(type, EVENT_OBJ, event);
...
MPI_Send(cuda_dev_buf, type, ...);

## Slide 16: Examples of GPU-Integrated MPI
GPU-Integrated MPI
UVA-based
(MVAPICH, Open MPI)
Attribute-based (MPI-ACC)

## Slide 17: Outline
GPU-Integrated MPI Frameworks
  UVA-based
  Attribute-based
Synchronization Semantics in GPU-Integrated MPI Programs
Evaluating the Impact of Synchronization Semantics
Conclusion
Notes: In completion order does not matter if there is a single hardware queue, but this requirement goes away for Kepler or Multi-GPU environments.

## Slide 18: Synchronization Semantics in MPI
MPI_Send(s_buf, dest, ...);
MPI_Recv(r_buf, source, ...);
foo(r_buf);
MPI_Request requests[2];
MPI_Isend(s_buf, &requests[0], ...);
MPI_Irecv(r_buf, &requests[1], ...);
MPI_Wait(&requests[0]); // OR
MPI_Test(&requests[1]); // OR
MPI_Waitall(requests);
foo(r_buf);
Blocking Point-to-point Communication
Non-blocking Point-to-point Communication
  No synchronization needed
  Explicit synchronization only

## Slide 19: Synchronization Semantics in GPUs
What are Streams?
  Workflow abstractions
  Mechanism to enqueue GPU commands
    H2DMemcpy, D2HMemcpy, KernelExec
Notes: There *may* be some false synchronization between streams due to hardware queue limitations, but for this talk, that aspect is not important.

## Slide 20: Synchronization Semantics in GPUs
D2H
H2D
Kernel
stream 0
stream 1
H2DMemcpy(dbuf0, stream0);
H2DMemcpy(dbuf1, stream1);
KernelExec(dbuf0, stream0);
KernelExec(dbuf1, stream1);
D2HMemcpy(dbuf0, stream0);
D2HMemcpy(dbuf1, stream1, &event1);
WaitForEvent(stream0, event1);
KernelExec(dbuf0, stream0);
Implicit
Synchronization
Explicit
Synchronization
Notes: There *may* be some false synchronization between streams due to hardware queue limitations, but for this talk, that aspect is not important.

## Slide 21: Synchronization Semantics in GPUs
What are Streams?
  Workflow abstractions
  Mechanism to enqueue GPU commands
    H2DMemcpy, D2HMemcpy, KernelExec
  Enforces dependency between two commands (executed in issue-order)
  Implicit synchronization within same stream
  Explicit synchronization across streams
  CUDA: stream; OpenCL: command queue
In this talk, we assume that all GPU commands are non-blocking
Notes: There *may* be some false synchronization between streams due to hardware queue limitations, but for this talk, that aspect is not important.

## Slide 22: Synchronization Semantics in GPU-integrated MPI
MPI_Recv(r_dev_buf);
/* No Sync before GPU */
KernelExec(r_dev_buf, stream1);
MPI_Irecv(r_dev_buf);
/* Explicit Sync before GPU
* (MPI Standards) */
MPI_Wait();
KernelExec(r_dev_buf, stream1);
KernelExec(s_dev_buf, stream1);
/* No Sync before MPI */
MPI_Send(some_other_dev_buf);
KernelExec(s_dev_buf, stream1);
/* Explicit Sync before MPI */
StreamSynchronize(stream1);
MPI_Send(s_dev_buf);
KernelExec(s_dev_buf, stream1);
/* No Sync before MPI */
MPI_Send(some_other_dev_buf);
KernelExec(s_dev_buf, stream1);
/* Implicit Sync using attributes*/
MPI_Type_set_attr(type, STREAM, stream1);
MPI_Send(s_dev_buf, type);
MPIGPU
GPUMPI
UVA-based
Attribute-based

## Slide 23: Outline
GPU-Integrated MPI Frameworks
  UVA-based
  Attribute-based
Synchronization Semantics in GPU-Integrated MPI Programs
Evaluating the Impact of Synchronization Semantics
  Programmability (Implicit vs. Explicit)
  Performance
Conclusion
Notes: In completion order does not matter if there is a single hardware queue, but this requirement goes away for Kepler or Multi-GPU environments.

## Slide 24: Example User Scenario
MPI program with 3 processes
Rank 0: sender; Rank 1 and Rank 2: receivers
MPI rank 0 launches two GPU kernels to compute a large array
  GPU kernels can occur concurrently
----------------------dependency----------------------
MPI rank 0 scatters the large array to the 2 receiver processes (via send/receive)
  MPI Send/Receive occurs sequentially in some order

## Slide 25: UVA-based Design (Simple)
cudaStream_t myStream[N];
for(rank = 1; rank < N; rank++) {
fooKernel<<< myStream[rank]>>>(dev_buf + offset);
}
for(rank = 1; rank < N; rank++) {
/* explicit GPU stream sync before MPI */
cudaStreamSynchronize(myStream[rank]);
/* GPU-integrated MPI */
MPI_Send(dev_buf+offset, rank, ...);
}
Issue Order: K1-K2-MPI1-MPI2
Execution Order: K1-K2-MPI1-MPI2

## Slide 26: UVA-based Design (Simple)
cudaStream_t myStream[N];
for(rank = 1; rank < N; rank++) {
fooKernel<<< myStream[rank]>>>(dev_buf + offset);
}
for(rank = 1; rank < N; rank++) {
/* explicit GPU stream sync before MPI */
cudaStreamSynchronize(myStream[rank]);
/* GPU-integrated MPI */
MPI_Send(dev_buf+offset, rank, ...);
}
Dest rank = 1
Dest rank = 2
Time
Potential for Overlap
MPI_Send
Kernel

## Slide 27: UVA-based Design (Simple: Issue-order Progress)
cudaStream_t myStream[N];
for(rank = 1; rank < N; rank++) {
fooKernel<<< myStream[rank]>>>(dev_buf + offset);
}
for(rank = 1; rank < N; rank++) {
/* explicit GPU stream sync before MPI */
cudaStreamSynchronize(myStream[rank]);
/* GPU-integrated MPI */
MPI_Send(dev_buf+offset, rank, ...);
}
  Issue-order progress
  Explicit synchronization between GPU and MPI
  Poor performance, but reasonable programmability

## Slide 28: Completion-order Progress
MPI_Send
Kernel
Dest rank = 1
Dest rank = 2
Time
Overlapped MPI
Issue Order: K1-K2-MPI1-MPI2
Execution Order: K1-K2-MPI2-MPI1

## Slide 29: UVA-based Design (Advanced: Completion-order Progress)
cudaStream_t myStream[N];
int processed[N] = {1, 0};
for(rank = 1; rank < N; rank++) {
fooKernel<<<myStream[rank]>>>(dev_buf+offset);
}
numProcessed = 0; rank = 1;
while(numProcessed < N - 1) {
/* explicit GPU stream query before MPI */
if (cudaStreamQuery(myStream[rank])==cudaSuccess) {
/* GPU-integrated MPI */
MPI_Isend(dev_buf+offset, rank, ...);
numProcessed++; processed[rank] = 1;
}
MPI_Testany(...); /* check progress */
flag = 1;
if(numProcessed < N - 1) /* find next rank */
while(flag) {
rank=(rank+1)%N; flag=processed[rank];
}
}
MPI_Waitall();
Completion-order Progress

## Slide 30: UVA-based Design (Advanced: Completion-order Progress)
cudaStream_t myStream[N];
int processed[N] = {1, 0};
for(rank = 1; rank < N; rank++) {
fooKernel<<<myStream[rank]>>>(dev_buf+offset);
}
numProcessed = 0; rank = 1;
while(numProcessed < N - 1) {
/* explicit GPU stream query before MPI */
if (cudaStreamQuery(myStream[rank])==cudaSuccess) {
/* GPU-integrated MPI */
MPI_Isend(dev_buf+offset, rank, ...);
numProcessed++; processed[rank] = 1;
}
MPI_Testany(...); /* check progress */
flag = 1;
if(numProcessed < N - 1) /* find next rank */
while(flag) {
rank=(rank+1)%N; flag=processed[rank];
}
}
MPI_Waitall();
  Completion-order progress
  Explicit synchronization between GPU and MPI
  Good performance, but poor programmability

## Slide 31: Ideal Programmability with Performance
cudaStream_t myStream[N];
int processed[N] = {1, 0};
for(rank = 1; rank < N; rank++) {
fooKernel<<<myStream[rank]>>>(dev_buf+offset);
}
numProcessed = 0; rank = 1;
while(numProcessed < N - 1) {
/* explicit GPU stream query before MPI */
if (cudaStreamQuery(myStream[rank])==cudaSuccess) {
/* GPU-integrated MPI */
MPI_Isend(dev_buf+offset, rank, ...);
numProcessed++; processed[rank] = 1;
}
MPI_Testany(...); /* check progress */
flag = 1;
if(numProcessed < N - 1) /* find next rank */
while(flag) {
rank=(rank+1)%N; flag=processed[rank];
}
}
MPI_Waitall();
MPI_Isend(dev_buf+offset)

## Slide 32: Attribute-based Design: Completion-order Progress
cudaStream_t myStream[N];
for(rank = 1; rank < N; rank++) {
fooKernel<<<b, t, myStream[rank]>>>(dev_buf+offset);
/* implicit GPU stream sync before MPI */
MPI_Type_dup(MPI_CHAR, &new_type);
MPI_Type_set_attr(new_type, BUF_TYPE, BUF_TYPE_CUDA);
MPI_Type_set_attr(new_type, STREAM_TYPE, myStream[rank]);
MPI_Isend(dev_buf+offset, new_type, rank, ...);
MPI_Type_free(&new_type);
}
/* explicit MPI sync (as per the MPI standard) */
MPI_Waitall();
  MPI-ACC performs completion-order progress
  Implicit synchronization between GPU and MPI
  Good performance and good programmability

## Slide 33: MPI-ACC’s Implementation of Completion-order Progress
MPI_Isend
GPU Stream Request Object
Request
creation
GPU Stream Request Pool
Perform handshake protocol
Send payload data
On request completion
using multiple GPU
streams.
Progress Engine Loop
CPU buffer
GPU buffer

## Slide 34: Outline
GPU-Integrated MPI Frameworks
  UVA-based
  Attribute-based
Synchronization Semantics in GPU-Integrated MPI Programs
Evaluating the Impact of Synchronization Semantics
  Programmability (Implicit vs. Explicit)
  Performance (Issue-order vs. Completion-order progress)
Conclusion
Notes: In completion order does not matter if there is a single hardware queue, but this requirement goes away for Kepler or Multi-GPU environments.

## Slide 35: Evaluation
Goal: Measure the benefits of attribute-based approaches over UVA-based (simple and advanced)
  Programmability benefits: Explicit vs. Implicit synchronization
  Performance benefits: Issue-order vs. Completion-order progress
Example MPI implementation: MPI-ACC
  UVA-based design emulated by not passing any attributes except BUF_TYPE
Hardware: 3-nodes of a cluster
  Dual-socket oct-core AMD Opteron 6134 CPU
  Two NVIDIA Tesla C2050 GPUs (GF100 Fermi architecture)
  CUDA toolkit v4.0; CUDA driver v285.05.23
Process Setup: 1 sender; 2 receivers

## Slide 36: Experimental Setup Rationale
NVIDIA Fermi GPUs have single hardware queues for H2D, D2H and kernel execution
  Always execute in issue-order
  No performance difference between UVA-based and attribute-based methods
NVIDIA Kepler GPUs have multiple hardware queues
  Completion-order progress is expected to perform the best
To enable multiple hardware queues, we use two NVIDIA Fermi GPUs, each GPU with a unique set of hardware queues

## Slide 37: Performance Evaluation
K0-MPI0
K1-MPI1
Time
K1-MPI1
K0-MPI0
Issue-order progress
K0 < K1
K0 > K1
K0 >> K1
MPI_Send
Kernel
?
?
Completion-order progress

## Slide 38: Performance Evaluation
Effect of kernel computation size
Effect of MPI data size
MPI0
K0
MPI1
K1
MPI1
K1
?

## Slide 39: Performance Evaluation
Effect of kernel computation size
  K0 > K1
  Vary K0 and measure performance gains due to completion-order progress
Chart: Variance in Kernel Computation Time: (K0-K1)/K1
| 6.25E-2 | 0.125 | 0.25 | 0.5 | 1 | 2 | 4 | 8 | 16 | 32 | 64
Attribute-based | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
UVA-based (simple) | 1.0282 | 1.0539 | 1.0877 | 1.1749 | 1.3429 | 1.2663 | 1.1768 | 1.1068 | 1.0586 | 1.033 | 1.0165
UVA-based (advanced) | 0.99178 | 0.99107 | 0.98949 | 0.9924 | 0.99267 | 0.98859 | 0.99294 | 0.99651 | 1.0139 | 1 | 0.99976
34% better
Issue-order
Completion-order

## Slide 40: Performance Evaluation
Effect of MPI data size
  Fix K0 and K1, but K0 > K1
  Vary data size of MPI1
Chart: Ratio of Data Transfer Sizes
| 1/64 | 1/32 | 1/16 | 1/8 | 1/4 | 1/2 | 1 | 2 | 4
Attribute-based | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
UVA-based (simple) | 1.0163 | 1.0286 | 1.0241 | 1.051 | 1.0952 | 1.1788 | 1.3416 | 1.2733 | 1.1614
UVA-based (advanced) | 1.024 | 1.0136 | 1.0021 | 1.0107 | 1.0113 | 1.0063 | 1.0084 | 1.0255 | 1.0176
34% better
Issue-order
Completion-order

## Slide 41: Summary
GPU-Integrated MPI
UVA-based
Explicit Synchronization
Issue-order Progress (Poor performance)
Attribute-based
Implicit Synchronization
Completion-order Progress (Poor Programmability)
Completion-order Progress
(Good Performance and Programmability)
Contact
Ashwin Aji (aaji@cs.vt.edu)
Pavan Balaji (balaji@mcs.anl.gov)

## Slide 42: Backup SLides

## Slide 43: Programming with GPUs: Data and Workflow Abstractions
CUDA
Data Representation
  void *
Workflow
  cudaStream_t, cudaEvent_t
Data Movement
  cudaMempcyAsync(void *, stream)
Kernel Launch
  fooKernel <<<stream>>> (void *)
OpenCL
Data Representation
  cl_mem
Workflow
  cl_command_queue, cl_event
Data Movement
  clEnqueueReadBuffer(command_queue, mem, event)
Kernel Launch
  clEnqueueNDRangeKernel (command_queue, event)

## Slide 44: GPU Streams and Hardware Queues
D2H
H2D
Kernel
stream 2
stream 0
stream 4
stream 3
stream 1
stream n

## Slide 45: Overhead of UVA-based Design for CPU-CPU Communication
Chart: Data Size (bytes)
| 0 | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192
Basic MPI | 0.66 | 0.67 | 0.66 | 0.67 | 0.72 | 0.62 | 0.8 | 0.81 | 0.87 | 1.03 | 1.35 | 1.95 | 3.13 | 6.42 | 9.77
MPI + Datatype attribute check | 0.66 | 0.68 | 0.68 | 0.68 | 0.72 | 0.62 | 0.82 | 0.83 | 0.88 | 1.03 | 1.35 | 1.95 | 3.13 | 6.47 | 9.82
MPI + Automatic detection | 1.92 | 2.07 | 2.03 | 2.03 | 2.06 | 2.08 | 2.09 | 2.14 | 2.45 | 3.36 | 3.87 | 4.81 | 6.58 | 8.07 | 12.05