## Slide 1: On the Reproducibility of MPI Reduction Operations
Pavan Balaji
Computer Scientist
Group Lead, Programming Models and Runtime Systems
Dries Kimpe
Assistant Computer Scientist
Mathematics and Computer Science Division
Argonne National Laboratory

## Slide 2: Scientific Simulations and Parallel Computing
Increasing importance of parallel computing for scientific simulations
Increasingly large system sizes, in the 10s of petaflops today
  Expected to increase to an exaflop level performance by the end of this decade
Used in almost all aspects of scientific computing
  Alternative energy (biofuels, solar cells), improvements to non-fossil-fuels (nuclear reactors), sophisticated batteries, efficient automobiles (flights, cars)
Tianhe-2 (China), 32 Petaflops; 3.12 million cores
Mira (Argonne, USA), 10 Petaflops; 0.76 million cores

## Slide 3: Reproducibility in Scientific Simulations
What is reproducibility?
  When you run the same simulation with the same input, you get the same result
  Different levels of reproducibility exist, including bit-wise reproducibilty
Cost of bit-wise reproducibility is high, especially for large-scale machines
  Cannot have any nondeterminism in the execution; all steps of the execution have the follow the same path every time
Benefits are mainly with correctness checks
  Very simple correctness properties: you either get the same answer (correct) or you don’t (incorrect)
Several applications tend to require bit-wise reproducibility, sometimes just for contractual reasons
  Examples in nuclear reactors, drug designs

## Slide 4: MPI Reduction Operations
MPI (Message Passing Interface) is the de facto standard for parallel programming on supercomputers
MPI Reduction operations are a heavily used subset of the MPI standard
  MPI_REDUCE, MPI_ALLREDUCE, MPI_SCAN, MPI_EXSCAN, etc.
  Used to compute on data contributed by a group of processes, the result of which is deposited on one or all processes
  Every process contributes one element to the reduction (loosely speaking)
MPI-3.0 does not guarantee a deterministic behavior, but strongly recommends it
  Impact: several optimizations need to be disabled
  when MPI runs in “deterministic mode”
  Most MPI implementations provide such a
  “deterministic mode” either by default or through
  an environment or configuration setting

## Slide 5: Reproducibility Issues in MPI Reduction Operations
Two primary sources of nondeterminism
  Nondeterministic computational flow
    E.g., one way of doing reduction is to locally compute in whatever order the incoming messages arrive
    Not a problem in most MPI implementations
  Order of computation: A + (B + C) != (A + B) + C
Example of unordered computation: Topology-aware reduction
  The idea of topology-aware reduction is to take advantage of the physical hierarchy of the system for reduction
  Local reduction on the node; only the result is forwarded to other nodes: improves number of network messages and hence performance
  Obviously, the order of operations depends on the hardware topology

## Slide 6: Reproducibility Issues with Order of Computation
Order of computation: A + (B + C) != (A + B) + C
  Floating point arithmetic loses information when a large value is added to a small value
    Consider: S = A[1] + A[2] + A[3] + … + A[1billion]
    A[1] = A[2] = A[3] = … = A[1billion – 1] = 1e-5
    A[1biillion] = 1e5
    Option 1:
    Add A[1], A[2], …, A[1billion – 1] first, we get: 1e4
    Add this to A[1billion], we get, S = 1e5 + 1e4 = 1.1e5
    Option 2:
    Add A[1billion] + A[1], we get: 1e5 + 1e-5 = 1e5 (rounding)
    Now, add (A[1billion] + A[1]) + A[2]: 1e5 + 1e-5 = 1e5 (rounding)

## Slide 7: Contributions of this paper
The focus of this paper is to understand the performance and correctness implications of nondeterministic MPI reduction operations
How much performance improvement can be get through nondeterministic reductions?
How much inconsistency do we generate in the result due to this nondeterminism?
In this paper, we use MPI_SUM as a case study, but the conclusions apply to other operations as well

## Slide 8: Topology-aware Reductions
Primary goal is performance optimization at the cost of (some) loss of determinism/reproducibility
Example of topology-aware reduction is with multicore nodes
  Several implementations of MPI (e.g., MPICH, MVAPICH, and Intel MPI), detect the physical topology of the node and optimize reduction operations for multicore architectures
12
13
14
15
8
9
10
11
4
5
6
7
0
1
2
3
0
1
4
5
2
3
6
7
8
9
12
13
10
11
14
15

## Slide 9: Consequences of Nondeterminism
Accuracy
  Reproducibility != Accuracy
  The MPI standard does not require reduction operations to be in a particular order
  Even if the result is deterministic, the order of the operations might not lead to the best precision
Precision cost of nondeterminism
  Order of operations can cause an absolute error of:
  abs(E) = g(log(N)) x S|Xi|
  g(N) = (N x u) / (1 – (N x u))
  u: unit of round off (1e-16 for double precision); N: number of elements
  Relative error compared to output:
  rel(E) = log(N) x u / (1 – (log(N) x u))
Nicholas J. Higham. “Accuracy and Stability of Numerical Algorithms”. SIAM, 1996

## Slide 10: Other Sources of Nondeterminism
Compilers
  Languages like C/C++ and Fortran give a lot of freedom to compilers to reorder instructions as needed by ignoring parallelism
  Explicit assembler-level instructions are needed to ensure consistency
Hardware instructions
  Most hardware allows multiple instructions to be in-flight and execute out-of-order between processes
  If an architecture supports fused-multiply-add (FMA) instructions, the compiler might try to take advantage of it; however, in some conditions such an instruction might throw an error or exception forcing execution to a different computation path
Other programming models
  OpenMP reductions have the same problem: threads might contribute their data out-of-order
  MPI implementations might use hardware features in some hardware configurations and not use them in others

## Slide 11: Impact of Topology on Performance (MPI_REDUCE)

## Slide 12: Impact of System Size on Performance (MPI_REDUCE)

## Slide 13: Impact of Topology on Reproducibility
Remember that:
  rel(E) = log(N) x u / (1 – (log(N) x u))
For most modern systems, N is quite small:
  Tianhe-2: N = 3.12e6; log(N) = 21.57
  Sequoia: N = 1.5e6; log(N) = 20.52
  At exascale, N is expected to be around 1e9; log(N) = 29.9
For double precision arithmetic, u = 1e-16
At these values, rel(E) is around 1e-14 to 1e-15 or 0.000000000001%
Unless the application does several billions of reduction operations, and these errors accumulate, it should not make a difference in practice

## Slide 14: Concluding Remarks
Nondeterminism in MPI reduction operation has traditionally been discouraged because of the potential of non-reproducible results
This paper demonstrates that:
  Deterministic computational guarantees in MPI reduction are very expensive with respect to performance: ~3X performance difference
  Do not make significant impact on the accuracy even at Exascale
Recommendations:
  We should completely discard the pretense of deterministic execution
    This is not practical and is already very hard to achieve in practice; it will only get harder
  We should embrace nondeterministic executions and invest in algorithmically bounding such inaccuracies

## Slide 15: Funding Acknowledgments
Funding Grant Providers
Infrastructure Providers

## Slide 16: Programming Models and Runtime Systems Group
Group Lead
  Pavan Balaji (computer scientist)
Current Staff Members
  Antonio Pena (postdoc)
  Wesley Bland (postdoc)
  Huiwei Lu (postdoc)
  Junchao Zhang (postdoc)
  Ken Raffenetti (developer)
Other Affiliates
  Xiaomin Zhu (visiting researcher), to start in 2014
  Yuqing Xiong (visiting researcher)
Past Staff Members
  Ralf Gunter (research associate)
  James S. Dinan (postdoc)
  David J. Goodell (developer)
  Darius T. Buntinas (developer)
Current and Past Students
  Rengbo Pang (Ph.D.), to start in 2014
  Marius Horga (M.S.)
  Xiuxia Zhang (Ph.D.)
  Brian Skjerven (Ph.D.)
  Amer Halim (Ph.D.)
  Chaoran Yang (Ph.D.)
  Min Si (Ph.D.)
  Xin Zhao (Ph.D.)
  Alex Brooks (Ph.D.)
  Huiwei Lu (Ph.D.)
  Yan Li (Ph.D.)
  David Ozog (Ph.D.)
  Palden Lama (Ph.D.)
  Ziaul Haque Olive (Ph.D.)
  Md. Humayun Arafat (Ph.D.)
  Qingpeng Niu (Ph.D.)
  Li Rao (M.S.)
  Lukasz Wesolowski (Ph.D.)
  Feng Ji (Ph.D.)
  John Jenkins (Ph.D.)
  Ashwin Aji (Ph.D.)
  Shucai Xiao (Ph.D.)
  Sreeram Potluri (Ph.D.)
  Piotr Fidkowski (Ph.D.)
  James S. Dinan (Ph.D.)
  Gopalakrishnan Santhanaraman (Ph.D.)
  Ping Lai (Ph.D.)
  Rajesh Sudarsan (Ph.D.)
  Thomas Scogland (Ph.D.)
  Ganesh Narayanaswamy (M.S.)
Advisory Board
  Rajeev Thakur (deputy division director)
  Marc Snir (division director)
  Rusty Lusk (retired, STA)

## Slide 17: We are looking for people!
Multiple openings for various research positions at Argonne (U.S. Department of Energy National Laboratory)
  M.S. level: Graduate students and Predoctoral researchers
  Ph.D. level: Graduate students and Postdoctoral researchers
  Senior positions: Software developer and Assistant computer scientist
  U.S. citizenship not required; work visas are sponsored
Work on the largest supercomputers in the world
  Focus areas are in scientific computing and cloud computing
Various projects on Runtime systems
  MPI and other communication systems
  Threading models and Operating Systems
  Accelerator models (GPUs, Intel Xeon Phi, heterogeneous memory models)
Contact: balaji@mcs.anl.gov or http://www.mcs.anl.gov/~balaji

## Slide 18
Web: http://www.mcs.anl.gov/~balaji Email: balaji@mcs.anl.gov
Group website: http://collab.mcs.anl.gov/display/PMRS