## Slide 1: MT-MPI: Multithreaded MPI for Many-Core Environments
Min Si1,2 Antonio J. Peña2 Pavan Balaji 2
Masamichi Takagi3 Yutaka Ishikawa1
1 University of Tokyo
2 Argonne National Laboratory
3 NEC Corporation

## Slide 2: Presentation Overview
Background and Motivation
Proposal and Challenges
Design and Implementation
  OpenMP Runtime Extension
  MPI Internal Parallelism
Evaluation
Conclusion

## Slide 3: Many-core Architectures
Massively parallel environment
Intel® Xeon Phi co-processor
  60 cores inside a single chip, 240 hardware threads
  SELF-HOSTING in next generation, NATIVE mode in current version
Blue Gene/Q
  16 cores per node, 64 hardware threads
Lots of “light-weight” cores is becoming a common model
Notes: point : parallel massively
240 so far, even more
BG/Q, 64 thread/cores
current KNC, native mode similar to KNL
Since multicore processors are the norm today, the only way to improve the performance for high end processors is to add more threads and cores.
Many core architecture, such as Intel xeon phi and BG/Q, provides us such a massively parallel environment,
The latest Xeon Phi production provides 60 cores on a single chip, and delivered 240 available hardware threads;
Especially, the next generation is expected as self-hosting, which mean the apps could be completely executed on such many-core chip as running on host traditional CPU, but deliver massively parallelism.
The current production already provides us a similar research platform, called native mode, although it still need host assist.
On the other hand, the IBM BGQ also provides us such parallel env, 16 cores, delivers 64 hardware threads per node.
----- 会议笔记(14-5-30 19:38) -----
connect with MPI.
light
----- 会议笔记(14-6-6 18:32) -----
add slide numbers
add an outline

## Slide 4: MPI programming on Many-Core Architectures
Thread Single mode
/* user computation */
MPI_Function ( );
/* user computation */
MPI Process
COMP.
COMP.
MPI COMM.
#pragma omp parallel
{ /* user computation */ }
MPI_Function ( );
#pragma omp parallel
{ /* user computation */ }
Funneled / Serialized mode
#pragma omp parallel
{
/* user computation */
MPI_Function ( );
/* user computation */
}
MPI Process
COMP.
COMP.
MPI COMM.
Multithreading mode
Notes: To utilize such architectures, application programmers are increasingly looking at hybrid programming models, where multiple threads interact with MPI processes.
The most prominent of the threading models used in scientific computing today is OpenMP. The compiler translates these pragmas into semantic information, then the runtime system can use it to schedule the computational work units on multiple threads for parallel execution.
MPI defines four thread modes for working with threads.
The first one is thread single mode, every MPI process is running on different hardware core, no threads.
In the multiple threading mode, a lot of threads are created for user computation in each MPI process, all of them could issue MPI calls by sharing the communication resources
On the other hand, in the other two modes, the funneled & serialized mode, which are the most widely used in current user applications, still generates a large number of computation threads, but only 1 of them is allowed to issue MPI calls.
In this paper, we focuses on these two modes.
----- 会议笔记(14-5-30 19:38) -----
big jump! should connect. use threads->still use MPI for comm->
----- 会议笔记(14-6-6 18:32) -----
mention hybrid, mpi + threads keyworks
justfy funneled mode is the topic
maybe multithreading mode bigger is better
Semanticly different, eg.need separate messages into different threads

## Slide 5: Problem in Funneled / Serialized mode
Funneled / Serialized mode
  Multiple threads are created for user computation
  Single thread issues MPI
MPI Process
COMP.
COMP.
MPI COMM.
#pragma omp parallel
{ /* user computation */ }
MPI_Function ( );
#pragma omp parallel
{ /* user computation */ }
ISSUE
Many threads are IDLE !
Single lightweight core delivers poor performance
Notes: As we introduced, in the Funneled/serialized mode, a lot of threads are created, but only 1 thread is allowed to issue MPI calls, which means that, all the other threads are absolutely idle during MPI calls. Especially on many core architectures, these idle threads actually translate to underused hardware cores! it is a of wasted computational resources.
Moreover, since each single core of such many-core chips is much slower than CPU, even if we gain performance in computation by using multiple threads, however, we may also lose performance in MPI.
It is an urgent issue, if we want to use such massively parallel env more efficiently.
----- 会议笔记(14-6-6 18:32) -----
also write lightweight core in text(mark it)

## Slide 6: Our Approach
Sharing Idle Threads with Application inside MPI
MPI Process
COMP.
COMP.
MPI COMM.
MPI COMM.
#pragma omp parallel
{ /* user computation */ }
MPI_Function ( ){
#pragma omp parallel
    {
      /* MPI internal task */
    }
}
#pragma omp parallel
{ /* user computation */ }
#pragma omp parallel
    {
      /* MPI internal task */
    }
Notes: To solve this issue, we designed a mechanism that allow MPI to be able to share these idle threads from user applications. We utilize these threads inside MPI, to parallelize various internal tasks.

## Slide 7: Challenges (1/2)
Some parallel algorithms are not efficient with insufficient threads, need tradeoff
But the number of available threads is UNKNOWN !
SINGLE SECTION
#pragma omp parallel
{
  /* user computation */
  #pragma omp single
  {
    /* MPI_Calls */
  }
}
Barrier
Notes: However, in practice, this approach has some challenges
1.we modified some algorithms for internal MPI processing, to achieve efficient OpenMP parallelism. But in some cases it is not as efficient for sequential processing. for example, data movement, fine-grained pipeline
However, the parallel version may perform worse than the traditional sequential implementation if the number of threads is not sufficient enough. Thus, we need tradeoff here.
However, at OpenMP runtime, the actual number of available threads is unknown (eg. omp single, when a single thread comes into this region, maybe some threads already arrived and blocked at the implied barrier at the end of single section, but some others may still be working in previous user computation).
----- 会议笔记(14-5-30 19:38) -----
do say example (shared comm)
----- 会议笔记(14-6-6 18:32) -----
less explaination for defination of available threads

## Slide 8: Challenges (2/2)
Nested parallelism
  Simply creates new Pthreads, and offloads thread scheduling to OS,
  Causes threads OVERRUNNING issue
#pragma omp parallel
{
  #pragma omp single
  {
    #pragma omp parallel
    { … }
  }
}
Creates N Pthreads !
Creates N Pthreads !
ONLY use IDLE threads
Notes: 2. nested parallelism
The current openMP runtime system simply creates new pthreads for each nested parallel block
and allow the operating system to schedule them on top of the available cores.
However, this would result in creating additional threads than the available number of cores causing severe degradation in performance
----- 会议笔记(14-5-30 19:38) -----
Not for all, i.e. qthread, but it is not the point today. say different between nthreads and nparallel

## Slide 9: Design and Implementation
Implementation is based on Intel OpenMP runtime (version 20130412)
OpenMP Runtime Extension
MPI Internal Parallelism
Notes: already know #idle threads
expose in mpich.
then, how to use this info

## Slide 10: Guaranteed Idle Threads VS Temporarily Idle Threads
Guaranteed Idle Threads
  Guaranteed idle until Current thread exits
Temporarily Idle Threads
  Current thread does not know when it may become active again
#pragma omp parallel
{
  #pragma omp single nowait
  {…
  }
  #pragma omp critical
  {…
  }
}
#pragma omp parallel
{
  #pragma omp single
  {…
  }
}
Barrier
#pragma omp parallel
{
  #pragma omp critical
  {…
  }
}
Example 1
Example 2
Example 3
Notes: To workaround these limitations of OpenMP runtime,
we modified the Intel OpenMP runtime library to expose information about the idle threads to the MPI implementation.
We defines two kinds of idle threads.
For the threads which are guaranteed idle until current thread exist from MPI stack, we call them guranteed **
For example,**
There are some other threads, they are idle but the current thread does not know when they may become active again.
For example,
We call these threads temporarily available threads.
----- 会议笔记(14-5-30 19:38) -----
put 1 past thread in critical
time-dependent
...
no detail, read paper
add one slide here

## Slide 11: Expose Guaranteed Idle Threads
MPI uses Guaranteed Idle Threads to schedule its internal parallelism efficiently (i.e. change algorithm, specify number of threads)
#pragma omp parallel
#pragma omp single
{
MPI_Function {
num_idle_threads = omp_get_num_guaranteed_idle_threads( );
if ( num_idle_threads < N ) {
/* Sequential algorithm */
} else {
    #pragma omp parallel num_threads(num_idle_threads)
    { … }
    }
}
}
Notes: It can be risky if we utilize Temporarily Available Threads because their status can change to active at any time, hence hurt performance.
Therefore, we choose guaranteed idle threads to help MPI, we modified OpenMP runtime to count the number of these threads and expose it to MPI.
Such information also allows the MPI implementation to choose different algorithms that tradeoff between parallelism
and sequential execution to achieve the best performance in all cases.

## Slide 12
  Derived Datatype Related Functions
  Shared Memory Communication
  Network-specific Optimizations
Implementation is based on MPICH v3.0.4
Design and Implementation
OpenMP Runtime Extension
MPI Internal Parallelism
Notes: already know #idle threads
expose in mpich.
then, how to use this info

## Slide 13: 1. Derived Datatype Packing Processing
MPI_Pack / MPI_Unpack
Communication using Derived Datatype
  Transfer non-contiguous data
  Pack / unpack data internally
#pragma omp parallel for
for ( i=0; i<count; i++ ){
  dest[i] = src[i * stride];
}
block_length
count
stride
0 | 5 | 10 | 15 | 20

## Slide 14: 2. Shared Memory Communication
Parallel algorithm
  Get as many available cells as we can
  Parallelize large data movement
Shared Buffer
Cell[0]
Cell[1]
Cell[2]
Cell[3]
User Buffer
User Buffer
Sender
Receiver
Shared Buffer
Cell[0]
Cell[1]
Cell[2]
Cell[3]
User Buffer
User Buffer
Sender
Receiver
(a) Sequential Pipelining
(b) Parallel pipelining
Original sequential algorithm
  Shared user space buffer between processes
  Pipelining copy on both sender side and receiver side
Notes: ……
However, the parallel version also has serious disadvantage for some cases. Let’s compare…

## Slide 15: Sequential Pipelining VS Parallelism
Small Data transferring ( < 128K )
  Threads synchronization overhead > parallel improvement
Large Data transferring
  Data transferred using Sequential Fine-Grained Pipelining
  Data transferred using Parallelism with only a few of threads (worse)
  Data transferred using Parallelism with many threads (better)
Sender Buffer
Shared Buffer
Receiver Buffer

## Slide 16: 3. InfiniBand Communication
Structures
  IB context
  Protection Domain
  Queue Pair
    1 QP per connection
  Completion Queue
    Shared by 1 or more QPs
RDMA communication
  Post RDMA operation to QP
  Poll completion from CQ
OpenMP contention issue
P0
P1
P2
QP
QP
CQ
PD
HCA
IB CTX
ADI3
CH3
SHM
nemesis
TCP
IB
…
  (critical)
  (critical)
Notes: MPI supports multiple internode networks through unified nemesis API.
Depending on the network implementation, some of them could also benefit from parallelism
Our practice focused on the IB network.
There are several IB resource structures provided for communication programming…
IB library internally support multi-threading. For some contentious resource, such as QP and CQ, they are protected by lock/unlock.
Ideally, the performance improvement is gained from the operations issued to different QPs/CQs, for the operations to the same QP/CQ, it is just equal to the sequential version.
contention issue in current openmp to the QP
However, current intel OpenMP has a contention issue, multi-threads access a critical region may cause very expensive sync overhead.
Although this problem should be solved in future, to workaround this issue, we decided to only parallelize the operations to send to different connections

## Slide 17: Evaluation
  Derived Datatype Related Functions
  Shared Memory Communication
  Network-specific Optimizations
All our experiments are executed on the Stampede supercomputer at the Texas Advanced Computing Center (https://www.tacc.utexas.edu/stampede/).

## Slide 18: Derived Datatype Packing
Parallel packing 3D matrix of double
Chart: Number of Threads
| 1.0 | 2.0 | 4.0 | 8.0 | 16.0 | 32.0 | 64.0 | 128.0 | 240.0
256 | 1.0025 | 1.9887 | 3.9705 | 7.7618 | 13.428 | 20.1111 | 20.388 | 21.4246 | 22.1035
1K | 1.0021 | 1.9894 | 3.7443 | 7.7889 | 13.6122 | 20.7472 | 21.2788 | 22.6374 | 26.7791
4K | 1.0054 | 2.0201 | 3.7155 | 7.7133 | 14.0733 | 20.826 | 20.7103 | 21.5349 | 24.2218
16K | 1.022 | 2.0092 | 3.7985 | 7.8181 | 14.3539 | 22.3126 | 23.3203 | 25.179 | 26.8752
64K | 1.0078 | 1.9829 | 3.979 | 7.8912 | 15.2168 | 29.346 | 53.6382 | 71.6343 | 87.1879
256K | 1.0059 | 1.9974 | 3.9834 | 7.6696 | 15.016 | 29.6959 | 54.8406 | 77.5352 | 95.9237
Ideal | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 240
Z
Y
X
  Packing the X-Z plane with varying Z
Graph Data:
Fixed matrix volume 1 GB
Fixed length of Y: 2 doubles
Length of Z: graph legend
  Packing the Y-Z plane with varying Y
Chart: Number of Threads
| 1.0 | 2.0 | 4.0 | 8.0 | 16.0 | 32.0 | 64.0 | 128.0 | 240.0
256 | 0.3803 | 0.35254 | 0.39309 | 0.38765 | 0.36501 | 0.32239 | 0.24329 | 0.23723 | 0.21019
1K | 0.43316 | 0.66882 | 0.95972 | 1.1263 | 1.1487 | 1.0989 | 0.87344 | 0.8562 | 0.77199
4K | 0.45789 | 0.8392 | 1.4407 | 2.3481 | 3.2657 | 3.5069 | 3.0971 | 3.0978 | 2.8531
16K | 0.46823 | 0.86617 | 1.6447 | 3.1921 | 5.4735 | 8.1084 | 8.8841 | 9.9804 | 9.6162
64K | 0.45241 | 0.88247 | 1.7578 | 3.4275 | 6.4541 | 11.0821 | 16.7884 | 22.1997 | 24.9637
256K | 0.44878 | 0.8932 | 1.7647 | 3.2247 | 6.015 | 12.0658 | 20.4811 | 31.2567 | 42.5551
Ideal | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 240
Graph Data:
Fixed matrix volume 1 GB
Fixed length of X: 2 doubles
Length of Y: graph legend
Block
Vector
Vector
(Parallelize here)
Hvector
Notes: ----- 会议笔记(14-5-30 19:38) -----
Mention:
Different numbers on different surface because using different datatypes
Get some worse perf in graph 2(less than 1), because compiler does inefficient prefetching, we discussed the details in paper

## Slide 19
3D internode halo exchange using 64 MPI processes
Chart: Number of Threads
| 1.0 | 2.0 | 4.0 | 8.0 | 16.0 | 32.0 | 64.0 | 128.0 | 240.0
Cube | 0.76351 | 1.4497 | 2.4925 | 3.8281 | 5.1921 | 5.7917 | 4.8915 | 4.7487 | 4.1245
Large X | 0.6118 | 1.1969 | 1.3822 | 1.5144 | 1.5729 | 1.553 | 1.5325 | 1.4994 | 1.5141
Large Y | 0.81605 | 1.5938 | 3.0393 | 5.6881 | 9.5699 | 14.7041 | 18.9843 | 22.181 | 23.4471
Large Z | 0.71661 | 1.0335 | 1.4332 | 1.7021 | 1.8492 | 1.6862 | 1.3321 | 1.0881 | 1.0201
Cube 512*512*512 double
Large X 16K*128*64 double
Large Y 64*16K*128 double
Large Z 64*128*16K double
Not strong scaling
BUT we are using IDLE RESOURCES !
Z
Y
X
Notes: Most expensive communication cost is in Y-Z dimension halo, takes 85% of the time, therefore larger Y delivers greater speedup!
----- 会议笔记(14-5-30 19:38) -----
say worse scala, but still get performance, threads are idle

## Slide 20
Hybrid MPI+OpenMP NAS Parallel MG benchmark
Chart: Number of Threads
| 1.0 | 2.0 | 4.0 | 8.0 | 16.0 | 32.0 | 64.0 | 128.0 | 240.0
Communication Time Speedup | 1 | 0.99237 | 1.2761 | 2.0386 | 2.7716 | 3.8274 | 4.5098 | 4.6798 | 3.0823
Execution Time Speedup | 0.99468 | 1.035 | 1.1464 | 1.316 | 1.5401 | 1.8317 | 2.1685 | 2.3479 | 2.2245
V-cycle multi-grid algorithm to solve a 3D discrete Poisson equation.
Halo exchanges with various dimension sizes from 2 to 514 doubles in class E with 64 MPI processes
Graph Data:
Class E using 64 MPI processes

## Slide 21: Shared Memory Communication
OSU MPI micro-benchmark
Chart: Number of Threads
| 1.0 | 2.0 | 4.0 | 8.0 | 16.0 | 32.0 | 64.0 | 120.0
64 KB | 0.99012 | 1.5487 | 2.6174 | 3.7105 | 4.714 | 4.3799 | 3.6097 | 2.2028
256 KB | 0.68882 | 1.4366 | 2.6679 | 4.5216 | 7.2432 | 9.8678 | 9.8694 | 8.8163
1 MB | 0.13051 | 0.253 | 0.52887 | 1.109 | 2.0099 | 3.1237 | 3.8988 | 5.0786
4 MB | 0.12504 | 0.2448 | 0.48044 | 0.94414 | 1.9595 | 3.3219 | 4.5514 | 5.3277
16 MB | 0.13515 | 0.26944 | 0.52513 | 1.0313 | 1.8787 | 3.3402 | 4.2556 | 5.2108
P2P Bandwidth
Chart: 
| 1.0 | 2.0 | 4.0 | 8.0 | 16.0 | 32.0 | 64.0 | 120.0
64 KB | 0.8681 | 1.2696 | 2.172 | 2.9928 | 3.708 | 3.4266 | 3.0901 | 1.834
256 KB | 0.52065 | 1.0809 | 2.0862 | 3.3834 | 5.8655 | 7.4515 | 8.2161 | 7.2416
1 MB | 0.13546 | 0.25899 | 0.50414 | 1.093 | 2.03 | 3.0866 | 3.9852 | 5.2497
4 MB | 0.12562 | 0.24387 | 0.47887 | 0.91295 | 1.754 | 3.1237 | 4.3521 | 4.6894
16 MB | 0.13357 | 0.26324 | 0.51931 | 1.0048 | 1.8542 | 3.1913 | 4.2178 | 4.6334
Chart: 
| 1.0 | 2.0 | 4.0 | 8.0 | 16.0 | 32.0 | 64.0 | 120.0
64 KB | 0.99012 | 1.5488 | 2.6175 | 3.7105 | 4.7141 | 4.3799 | 3.6098 | 2.2029
256 KB | 0.68881 | 1.4366 | 2.6679 | 4.5216 | 7.2431 | 9.8677 | 9.8692 | 8.8162
1 MB | 0.13051 | 0.253 | 0.52887 | 1.109 | 2.0099 | 3.1237 | 3.8989 | 5.0786
4 MB | 0.12504 | 0.24481 | 0.48045 | 0.94414 | 1.9595 | 3.3219 | 4.5515 | 5.3277
16 MB | 0.13512 | 0.26945 | 0.52514 | 1.0314 | 1.8787 | 3.3402 | 4.2557 | 5.2109
Similar results of Latency and Message rate
Caused by poor sequential performance due to too small Eager/Rendezvous communication threshold on Xeon Phi.
Not by MT-MPI !
Poor pipelining but worse parallelism

## Slide 22: One-sided Operations and IB netmod Optimization
Micro benchmark
  One to All experiment using 65 processes
    root sends many MPI_PUT operations to all the other 64 processes (64 IB QPs)
P0
P1
P2
P64
QP
QP
QP
QP
QP
QP
…
…
Parallelized
Chart: Number of Threads
| 1.0 | 2.0 | 4.0 | 8.0 | 16.0 | 32.0 | 64.0
1000 | 1 | 1.0552 | 1.0677 | 1.1527 | 1.1543 | 1.1699 | 1.1482
2000 | 1 | 1.0485 | 1.0636 | 1.1565 | 1.1328 | 1.1521 | 1.1444
4000 | 1 | 1.1157 | 1.1261 | 1.1806 | 1.2148 | 1.229 | 1.2021
8000 | 1 | 1.2186 | 1.2457 | 1.328 | 1.3465 | 1.362 | 1.3307
16000 | 1 | 1.1995 | 1.2356 | 1.3551 | 1.4223 | 1.4291 | 1.4401
Chart: Number of Threads
| 1.0 | 2.0 | 4.0 | 8.0 | 16.0 | 32.0 | 64.0
QPs only | 1 | 1.5853 | 2.2338 | 2.6894 | 3.1169 | 3.3362 | 3.1452
Parallelized IB Communication
Nthreads | Time(s) |  | 
 | Total | SP | SP/Total
1 | 5.8 | 2.2 | 37.9%
Profile of the experiment issuing
16000 operations
Ideal Speedup = 1.61
Notes: ----- 会议笔记(14-5-30 19:38) -----
put table here
** why sp/total become smaller ? Fix it, show we get less potentiality to parallelize.

## Slide 23: One-sided Graph500 benchmark
Every process issues many MPI_Accumulate operations to the other processes in every breadth first search iteration.
Scale 222, 16 edge factor, 64 MPI processes
Chart: Number of Threads
| 1.0 | 2.0 | 4.0 | 8.0 | 16.0 | 32.0 | 64.0
Improvement | 1 | 1.1078 | 1.1201 | 1.1669 | 1.268 | 1.2882 | 1.2925
Harmonic Mean TEPS | 1259790 | 1395650 | 1411090 | 1470110 | 1597420 | 1622820 | 1628310
Notes: ----- 会议笔记(14-5-30 19:38) -----
2^22 format

## Slide 24: Conclusion
Many-core Architectures
Most popular Funneled / Serialized mode in Hybrid MPI + threads programming model
  Many threads parallelize user computation
  Only single thread issues MPI calls
Threads are IDLE during MPI calls !
We utilize these IDLE threads to parallelize MPI internal tasks, and delivers better performance in various aspects
  Derived datatype packing processing
  Shared memory communication
  IB network communication
Notes: ----- 会议笔记(14-6-6 18:32) -----
show numbers to summarize evaluation

## Slide 25: Backup

## Slide 26: OpenMP Runtime Extension 2
Waiting progress in barrier
  SPIN LOOP until timeout !
  May cause OVERSUBSCRIBING
Solution: Force waiting threads to enter in a passive wait mode inside MPI
  set_fast_yield (sched_yield)
  set_fast_sleep (pthread_cond_wait)
while (time < KMP_BLOCKTIME){
  if (done) break;
  /* spin loop */
}
pthread_cond_wait (…);
#pragma omp parallel
#pragma omp single
{
  set_fast_yield (1);
  #pragma omp parallel
  { … }
}
Notes: However, in current implementation, to avoid overhead of sync in the case only waiting shortly, use spin loop instead of passive wait.
But want to use it asap
defined 2 func
mpi enable fast yield, then waiting threads yield. even if new pthreads, no overuse
Since fast_sleep cause more expensive overhead, we choose set fast_yield in our implementaion
----- 会议笔记(14-5-30 19:38) -----
the

## Slide 27: OpenMP Runtime Extension 2
set_fast_sleep VS set_fast_yield
  Test bed: Intel Xeon Phi cards (SE10P, 61 cores)
set_fast_sleep
set_fast_yield
Chart: KMP_BLOCKTIME
| 0.0 | 50.0 | 100.0 | 150.0 | 200.0 | 250.0 | 300.0
1 Thread | 0.32667 | 0.33667 | 0.44417 | 0.31583 | 0.385 | 0.26667 | 0.42917
4 Threads | 5.4667 | 1.1758 | -0.50083 | 1.7058 | 0.735 | -0.22917 | 1.0383
16 Threads | 1.6883 | 27.2425 | 29.5925 | 22.3075 | 29.4592 | 36.1783 | 24.8308
64 Threads | 47.0367 | 147.8592 | 173.92 | 123.475 | 113.5217 | 130.1483 | 115.5367
240 Threads | 17.7342 | 251.9833 | 249.6442 | 215.96 | 278.0833 | 307.9858 | 250.9992
Chart: KMP_BLOCKTIME
| 0.0 | 50.0 | 100.0 | 150.0 | 200.0 | 250.0 | 300.0
1 Thread | 0.30083 | 0.375 | 0.36083 | 0.2725 | 0.36667 | 0.30667 | 0.3275
4 Threads | 6.585 | 1.4817 | -0.40583 | 0.86667 | 0.37583 | 0.0275 | 1.1942
16 Threads | -0.33 | 2.6617 | 1.2442 | 4.755 | 3.505 | 5.2883 | 1.9583
64 Threads | 14.2092 | 17.375 | 16.6817 | 13.0583 | 14.6717 | 15.1592 | 14.855
240 Threads | 5.8733 | 28.72 | 25.33 | 25.91 | 32.905 | 26.1308 | 27.8983

## Slide 28: Prefetching issue when compiler vectorized non-contiguous data
Chart: Total Execution Cycle
| 8.0 | 32.0 | 64.0 | 128.0 | 512.0 | 2048.0
vec | 31667 | 59173 | 98263 | 110201 | 683617 | 718409
no-vec | 59204 | 71078 | 89738 | 90413 | 116420 | 265357
Chart: L2 Cache Miss
| 8.0 | 32.0 | 64.0 | 128.0 | 512.0 | 2048.0
vec | 463 | 1245 | 2293 | 2561 | 4175 | 6629
no-vec | 476 | 1305 | 2461 | 2436 | 2455 | 3649
for (i=0; i<count; i++){
  *dest++ = *src;
  src += stride;
}
#pragma omp parallel for
for (i=0; i<count; i++){
  dest[i] = src[i * stride];
}
(a) Sequential implementation (not vectorized)
(b) Parallel implementation (vectorized)

## Slide 29: Intra-node Large Message Communication
Sequential pipelining LMT
  Shared user space buffer
  Pipelining copy on both sender side and receiver side
Shared Buffer
Cell[0]
Cell[1]
Cell[2]
Cell[3]
User Buffer
User Buffer
Sender
Receiver
Sender
Get a EMTPY cell from shared buffer, and copies data into this cell, and marks the cell FULL; Then, fill next cell.
Receiver
Get a FULL cell from shared buffer, then copies the data out, and marks the cell EMTPY ; Then, clear next cell.

## Slide 30: Parallel InfiniBand communication
  Two level parallel policies
    Parallelize the operations to different IB CTXs
    Parallelize the operations to different CQs / QPs
HCA
QP
CQ
IB CTX
QP
CQ
IB CTX
QP
CQ
IB CTX
HCA
CQ
IB CTX
QP
QP
CQ
CQ
QP
(a) Parallelism on different IB CTXs
(b) Parallelism on different CQs / QPs
Notes: ----- 会议笔记(14-5-30 19:38) -----
backup

## Slide 31: Parallelize InfiniBand Small Data Transfer
3 parallelism experiments based on ib_write_bw:
  IB contexts 1 process per node, 64 IB CTX per process, 1 QP + 1 CQ per IB CTX
  QPs and CQs 1 process per node, 1 IB CTX per process, 64 QPs + 64 CQs per IB CTX
  QPs only 1 process per node, 1 IB CTX per process, 64 QPs + 1 shared CQ per IB CTX
  Test bed: Intel Intel Xeon Phi SE10P Coprocessor, InfiniBand FDR
  Data size: 64 Bytes
Chart: Number of Threads
| 1.0 | 2.0 | 4.0 | 8.0 | 16.0 | 32.0 | 64.0
IB contexts | 1 | 1.9675 | 2.6994 | 2.8771 | 3.3316 | 3.6382 | 3.628
QPs and CQs | 1 | 1.7516 | 2.7398 | 2.9317 | 3.2188 | 3.5336 | 3.4074
QPs only | 1 | 1.5853 | 2.2338 | 2.6894 | 3.1169 | 3.3362 | 3.1452
Notes: MPI implements often use 1 shared CQ for all the QPs, which is shown as the green line. improved less due to sequential execution during polling CQ.
Expected parallelized sending processing should deliver similar improvement.
----- 会议笔记(14-5-30 19:38) -----
back

## Slide 32: Eager Message Transferring in IB netmod
When send many small messages
  Limited IB resources
    QP, CQ, remote RDMA buffer
  Most of the messages are enqueued into SendQ
  All sendQ messages are sent out in wait progress
Major steps in wait progress
  Clean up issued requests
  Receiving
    Poll RDMA-buffer
    Copy received messages out
  Sending
    Copy sending messages from user buffer
    Issue RDMA op
P0
Enqueue messages
into SendQ
wait progress start
Send some messages
immediately
Send messages in SendQ
P1
SYNC
wait progress start
SYNC
wait progress end
wait progress end
…
Send messages in SendQ
Receive message
Receive message
Parallelizable
Parallelizable
Clean up request
Clean up request

## Slide 33: Parallel Eager protocol in IB netmod
Parallel policy
  Parallelize large set of messages sending to different connections
    Different QPs : Sending processing
      Copy sending messages from user buffer
      Issue RDMA op
    Different RDMA buffers : Receiving processing
      Poll RDMA-buffer
      Copy received messages out

## Slide 34: Example: One-sided Communication
Feature
  Large amount of small non-blocking RMA operations sending to many targets
  Wait ALL the completion at the second synchronization call (MPI_Win_fence)
MPICH implementation
  Issue all the operations in the second synchronization call
PUT 0
Origin
Process
Target
Process 2
Target
Process 1
PUT 1
PUT 2
PUT 3
PUT 4
PUT 5
MPI_Win_fence
MPI_Win_fence
Th 0
Th 1
Th 0
Th 1

## Slide 35: Parallel One-sided communication
Challenges in parallelism
  Global SendQ
    Group messages by targets
  Queue structures
    Stored in [Ring Array + Head / Tail ptr]
  Netmod internal messages (SYNC etc.)
    Enqueue to another SendQ (SYNC-SendQ)
P0
1
2
3
0
Send-Arrays
SYNC-SendQ
IN
OUT

## Slide 36: Parallel One-sided communication
Optimization
  Every OP is issued through long critical section
    Issue all Ops together
  Create large number of Requests
    Only create one request
ADI3
CH3
SHM
nemesis
IB
PUT
PUT
PUT
PUT
PUT
SendQ
Critical
Fig. Issue RMA operations from CH3 to IB netmod

## Slide 37: Profiling
Measured the execution time of the netmod send-side communication processing at the root process (SP)
  Copy from the user buffer to a preregistered chunk
  Posting of the operations to the IB network.
Chart: Number of Threads
| 1.0 | 2.0 | 4.0 | 8.0 | 16.0 | 32.0 | 64.0
1000 | 1 | 1.4177 | 2.2221 | 4.3897 | 7.3464 | 9.1098 | 10.4708
2000 | 1 | 1.4399 | 2.2164 | 4.2935 | 5.879 | 5.6858 | 6.6959
4000 | 1 | 1.8443 | 1.9173 | 3.7446 | 5.8431 | 6.52 | 6.9957
8000 | 1 | 1.9811 | 2.463 | 4.7628 | 6.919 | 7.5474 | 6.7977
16000 | 1 | 1.4131 | 1.6731 | 3.2119 | 4.9955 | 5.6424 | 6.9005
Nthreads | Time |  |  | Speedup | 
 | Total | SP | SP/Total | Total | SP
1 | 5.8 | 2.2 | 37.9% | 1.0 | 1.0
4 | 4.7 | 1.3 | 27.3% | 1.2 | 1.7
16 | 4.0 | 0.4 | 9.8% | 1.4 | 5.0
64 | 4.0 | 0.3 | 8.0% | 1.4 | 6.9
Expected speedup but the percentage of time spent in SP becomes less and less
Profile of the experiment issuing
16000 operations