## Slide 1: Techniques for Enabling Highly Efficient Message Passing on Many-Core Architectures
Min Si
PhD student at University of Tokyo, Tokyo, Japan
Advisor : Yutaka Ishikawa
Guest graduate student at Argonne National Laboratory, IL, USA
Mentor : Antonio J. Peña Supervisor : Pavan Balaji
Email: msi@il.is.s.u-tokyo.ac.jp, msi@anl.gov
Homepage: http://sudalab.is.s.u-tokyo.ac.jp/~msi
Notes: Have worked at Argonne for 1 year,

## Slide 2: Scientific Programming on Many-Core Architectures
Massive Parallel Many-Core Environment
  Intel® Xeon Phi co-processor, Blue Gene/Q
Hardware Characteristics
  Simple and low frequency cores
  Other on-chip resources are growing at a lower rate…
We need Parallelism and Resource Sharing !
Thus we are studying two popular programming models
  1. Hybrid MPI+Threads model
  2. MPI RMA-based PGAS model
  Massive parallelism in computation
  On-chip resource sharing between threads
  Global shared arrays
  Memory sharing across nodes on distributed memory systems
Typical Get-Compute-Update
Local buffer
ACC
GET
GET
MPI Process
OpenMP Threads

## Slide 3: Communication Optimization in Hybrid MPI+threads Model
Problem Statement
  Only single thread issues MPI
  Most threads are IDLE during MPI calls
MT-MPI: Multi-threaded MPI[1]
  Sharing Idle Threads with application inside MPI
  Optimizing MPI internal processing by massive parallelism
MPI_Function( ){
  #pragma omp parallel
  { /* Internal Processing */ }
}
#pragma omp parallel
{ /* user computation */ }
MPI_Function ( );
MPI Process
COMP.
MPI COMM.
MPI COMM.
Many threads are IDLE !
Sharing IDLE threads inside MPI
Hybrid NAS MG class E using 64 MPI processes
on TACC Stampede supercomputer
Chart: Number of Threads
| 1.0 | 2.0 | 4.0 | 8.0 | 16.0 | 32.0 | 64.0 | 128.0 | 240.0
Communication Time Speedup | 1 | 0.99237 | 1.2761 | 2.0386 | 2.7716 | 3.8274 | 4.5098 | 4.6798 | 3.0823
Execution Time Speedup | 0.99468 | 1.035 | 1.1464 | 1.316 | 1.5401 | 1.8317 | 2.1685 | 2.3479 | 2.2245
[1] M. Si, A. J. Pena, P. Balaji, M. Takagi, and Y. Ishikawa, “MT-MPI: Multithreaded MPI for Many-Core Environments,” in Proceedings of the 28th ACM international conference on Supercomputing, ICS 2014.

## Slide 4: Process-based Asynchronous Progress Model for MPI RMA
MPI RMA Communication
  Not truly one-sided
Casper : Process-based ASYNC Progress[2]
  Flexible & Portable & Low overhead
  Improve SW-handled RMA operations without affecting HW-handled RMA.
Process 0
Process 1
+=
Computation
ACC(data)
MPI call
Communication Delay
Process 0
Process 1
+=
Computation
Acc(data)
Ghost
Process
MPI Recv
Process-based Asynchronous Progress
Chart: Number of Cores
| 1440.0 | 1920.0 | 2400.0 | 2800.0
Original MPI | 67.6983 | 50.95 | 39.9467 | 33.67
Casper | 36.8717 | 27.595 | 22.235 | 18.445
Thread (O) | 62.6583 | 46.065 | 36.745 | 30.7567
Thread (D) | 60.905 | 46.195 | 37.3383 | 31.2033
  NWChem CCSD(T) simulation for C20
  on NERSC Edison supercomputer
Reduced 45%
[2] M.Si, A.J.Pena, J.Hammond, P.Balaji, M.Takagi, and Y.Ishikawa, “Casper: An Asynchronous Progress Model for MPI RMA on Many-Core Architectures,” in Parallel and Distributed Processing, 2015. IPDPS 2015.