## Slide 1: Towards Implementing Robust Support for Portals 4 Networks in MPICH
Ken Raffenetti, Antonio J. Pena, Pavan Balaji
{kraffenetti,apenya,balaji}@anl.gov

## Slide 2: Portals 4 netmod in MPICH
Portals 4:
  Connectionless, hardware independent network API
Portals 4 netmod in MPICH 3.2:
  Network module (netmod) responsible for non-local communication
  Relies on Portals 4 MEs (matching list entries)
    MPI matching offloaded to hardware
  Messaging design
    Messages <= eager threshold in single PtlPut operation
    Hybrid Put/Get protocol for larger messages (receiver gets the rest of the data)
    Support for messages greater than implementation defined max_msg_size
PtlPut
PtlGet

## Slide 3: Portals 4 - Reliability
Multiple scenarios can cause Portals 4 to go into flow control state
  Event queue overflow
  Unexpected buffer exhaustion
MPICH adds a reliability layer (Rportals)
  Uses a separate EQ for origin side events
    Queues operations if they will overflow the local EQ
  Recovery from flow control events
    Global protocol to quiesce the network in rportals
      Pause/Pause Ack/Unpause
    NACKed operations are re-issued
target 0
target 1
op 0
op 1
op 2
target 2
issued
acked
acked
issued
PAUSE
PAUSE ACK
UNPAUSE
Explicit flow-control when hardware cannot handle messages
issued
nacked