## Slide 1: GLT: A Unified API for Lightweight Thread Libraries
Adrián Castelló
Rafael Mayo
Enrique S. Quintana-Ortí
Universitat Jaume I de Castelló
(Spain)
Antonio J. Peña
Barcelona Supercomputing Center (Spain)
Sangmin Seo
Pavan Balaji
Argonne National Lab
(USA)
Euro-Par 2017. 28th August – 1st September. Santiago de Compostela (Spain)

## Slide 2
CPU
CPU
CPU
CPU
NODE
Pthreads
NODE
?????????
Current Systems
Exascale Systems
CPU
NODE
Sequential
Former Systems

## Slide 3
Pthreads is the standard to exploit the current on-node parallelism
  Using pthreads library
  Using high-level programing models
Pros:
  Works well for hardware characteristics
Cons:
  Falls from the point of view of software requirements
  Context switch and synchronizations are expensive mechanisms
OS thread
Pthreads

## Slide 4
U
U
U
OS thread
Lightweight thread with low context-switch overhead
Dynamic data scheduling
To better overlap computation and communication/IO
To exploit fine-grained task parallelism
U
User-level thread
Lightweight Thread Libraries

## Slide 5
Specific OS
Windows Fibers
Solaris Threads
Specific Hardware
Tiny-Threads
High-level programming model
ConverseThreads
Nanos++
Lightweight Thread
abstraction
Cilk Go Intel TBB
Stackless threads
MassiveThreads Argobots
Qthreads
General purpose
MassiveThreads Argobots
Qthreads
Stackless Python
Protothreads
Lightweight Thread Libraries

## Slide 7
Goals of this work
  Improve Pthreads API
  Offer code portability
  Unify LWT semantics and Programming Model

## Slide 8
Generic Lightweight Thread (GLT) library
GLT common API
Qthreads
MassiveThreads
Argobots
* Based on work “A Review of Lightweight Thread Approaches for High Performance Computing” presented in Cluster 2016
*

## Slide 9
Generic Lightweight Thread (GLT) library
GLT common API
Qthreads
MassiveThreads
Argobots
Unified API for LWT solutions
Programming Model:
  Each thread composed by:
    OS thread
    Work unit queue
    Scheduler
  Scheduling relies on the underlying library
  Two types of work-unit support: Tasklet and ULT
Two approaches:
  Stand-alone (dynamic) and Headers (static)

## Slide 10
GLT objects
GLT | Argobots | Qthreads | MassiveThreads
GLT_thread | ABT_xstream | qthread_sheperd_id_t | myth_thread_t
GLT_ult | ABT_thread | aligned_t | myth_thread_t
GLT_tasklet | ABT_task | aligned_t | myth_thread_t
GLT_mutex | ABT_mutex | aligned_t | myth_mutex_t
GLT_barrier | ABT_barrier | qt_barrier_t | myth_barrier_t
GLT_cond | ABT_cond | aligned_t | myth_cond_t
GLT common API
Qthreads
MassiveThreads
Argobots

## Slide 11
GLT semantic mapping
GLT | Argobots | Qthreads | MassiveThreads
glt_ult_creation | ABT_thread_create | qthread_fork | myth_create
glt_tasklet_creation | ABT_task_create | qthread_fork | myth_create
glt_ult_creation_to | ABT_thread_create | qthread_fork_to | myth_create
glt_yield | ABT_thread_yield | qthread_yield | myth_yield
glt_ult_join | ABT_thread_free | qthread_readFF | myth_join
GLT common API
Qthreads
MassiveThreads
Argobots

## Slide 12
GLT improves Pthreads API
Library-thread model (N:1)
Hybrid model (M:N)
Kernel-thread model (N:1)
ULT
Just on thread at a time
Constrains concurrency
Glibc
High overhead because the OS
Lightweight Thread model
Two level scheduler
Programming model point of view

## Slide 13
GLT improves Pthreads API
Semantic point of view
Functionality/API | Pthreads API | GLT API
Pthreads API functions | Yes | Yes
Yield / Yield_to | No* | Yes
Migrate / Work-dispatch | No* | Yes
GLT exposes the kernel scheduled entities so programmers can schedule/map the threads as they need.
Pthreads API assumes those entities in the programming model so it relies on the underlying implementation.
* Not supported but included in some implementations as Non-portable functions

## Slide 14
Why a new API instead of the extending Pthreads API?

## Slide 15
Pthread = OS thread
Why a new API instead of the extending Pthreads API?

## Slide 16
Hardware & Software
2x Intel Xeon E5-2699 v3 (2.3 GHz)
  18 cores
  128 GB of RAM
GLT 01-2017
Argobots 01-2017
Qthreads 1.10
MassiveThreads 0.95

## Slide 17
GLT portability
Each thread creates its own subset of ULTs
A single thread creates all the ULTs
Without GLT: 2 tests x 3 lightweight thread libraries = 6 implementations
With GLT: 2 tests x 1 implementation = 2 implementations

## Slide 18
GLT overhead (microbenchmarks)
GLT overhead for Argobots
GLT overhead for Qthreads
GLT overhead for MassiveThreads
Init, Malloc and Creation present a small overhead
Yiel, Join and num_threads increment the number of instructions just in the stand-alone mode

## Slide 19
GLT overhead (apps)
UTS benchmark (T1XXL size)
N-Queens (n = 12)
0.1% for Headers approach (static)
0.6% for Stand-alone approach (dynamic)
Chart: Overhead (%)
| Argobots(T) | Argobots(U) | MassiveThreads | Qthreads
Stand-alone | 0.28 | 0.54 | 0.18 | 0.29
Headers | 0 | 0 | 0.05 | 0.06
Chart: Overhead (%)
| Argobots | MassiveThreads | Qthreads
Stand-alone | 0.35 | 0.49 | 0.56
Headers | 0.05 | 0 | 0.08

## Slide 20
Conclusions
Implementation of a common API for lightweight thread solutions
GLT improves the Pthreads API by adding functionality
GLT offers portability to programmers
GLT does not add any perceptible overhead

## Slide 21
Future work
GLT common API
Qthreads
MassiveThreads
Argobots
Pthreads
GLT common API
Pthreads API
Pthreads-GLT interaction
High-level Programming Models
GLT common API
OpenMP* OmpSs Charm++ others
* Paper: “GLTO: On the Adequacy of Lightweight Thread Approaches for OpenMP Implementations.” presented at ICPP 2017

## Slide 22
Thanks!
Contact: adcastel@uji.es
Doc: www.hpca.uji.es/GLT
Source code: github.com/adcastel/GLT.git